## Slide 1: WF on CR(s) for 2Rx exception for NR vehicle UE
SAMSUNG, LG Electronics, Volkswagen AG
3GPP TSG-RAN #82 Meeting
Sorrento, Italy, 10-13 Dec, 2018 Agenda Item: 9.3.16
RP-182845 (revision of RP-182798)

## Slide 2: Steps agreed for conclusion on 2 Rx exception
Revise existing SI on 2 Rx (RP-181990) by including external TR which is identical with contents of TR38.826
Approve the external TR
Approve RAN4 CR by referring external TR
Appove RAN2 CRs for TS36.300 and TS38.300
Approve LS to 5GAA by referring external TR
Approve LS to GCF CAG/RAN5

## Slide 3: 1. CR to TS 38.101-1

## Slide 4: Agreement 1: Definitions and notes in TS 38.101-1
Section 3 in TS 38.101-1
“An UE embedded in a vehicle, permanently connected to an embedded antenna system that radiates externally for NR operating bands”
Note: Vehicular UE does not refer to other UE form factors placed inside the vehicle.
Section 7 in TS 38.101-1 (Table 7.3.2-1)
NOTE 1:Four Rx antenna ports shall be the baseline for this operating band, except for 2 Rx vehicular UE [external TR].

## Slide 5: 2. CR to TS 36.300

## Slide 6: Agreement 2: SPID agreement in TS 36.300
Define SPID as shown below:
Table I.2-4: Network local configuration in idle and connected mode for SPID = 253
Configuration parameter | Meaning
Automotive device subscriber | The selection provides information that subscriber is using an automotive device and is permitted to utilise a minimum of two Rx antenna ports for the NR bands where four Rx antenna ports are baseline as given in TS 38.101-1 [86]

## Slide 7: 3. CR to TS 38.300

## Slide 8: Agreement 3: Add new Annex E to TS 38.300
Annex E (informative): SPID ranges and mapping of SPID values to cell reselection and inter-RAT/inter frequency handover priorities
The SPID values are defined in Annex I of TS 36.300 [2].From the SPID reference values, only the SPID=253 also applies for 5GC.