## Slide 1: On the scope of non-BL UE in CE mode for R15 eFeMTC WI
Intel
3GPP TSG RAN Meeting #83
Shenzhen, China, March 18-21, 2019
RP-190245
Document for: Approval

## Slide 2: Background
In the WID[1] of “Even further enhanced MTC for LTE”, the scope was described as below,
  The objective is to specify the following improvements for machine-type communications for BL/CE UEs.
The ambiguity to RAN4 is that some companies understand BL/CE as ‘BL and CE’ and some other companies understand it as ‘BL or CE’.
Upon the completion of this WID, there is no exceptional sheet to indicate non-BL/CE UE requirements are missed Rel-15 eFeMTC WI.

## Slide 3: Background
It is not straightforward to interpret “BL/CE” to include both BL+CE and non-BL+CE UE.
  In RAN4 spec TS36.133, the requirement is specified for both BL/CE and non-BL/CE UE, respectively, with term “non-BL/CE” introduced to distinguish the two cases.
In RAN4 spec TS36.133 the usage of “A/B” in lots of cases means “A and B”, e.g.,
  SSB: SS/PBCH block as defined in TS 38.211 [42, section 7.4.3]. (in section 3.1, TS36.133)
  are compliant to the requirements specified in TS 36.101 for inter-band CA with uplink in one E-UTRA band and without simultaneous Rx/Tx. (in section 3.6.1, TS36.133)
The terminologies of “non-BL/CE” are changed to “non-BL CE” for R14 RAN4 spec [3] and the terminologies in R15 spec was not changed, so there is a mismatch between R14 TS36.133 and R15 TS36.133.

## Slide 4: Discussion and proposal
There are four key new features introduced for R15 eFeMTC WI:
  Dense PRS
  CRS muting
  High velocity
  SI reading delay reduction
However, so far there was no any discussion in RAN4 for how non-BL UE in CE mode work or perform on these features above. On the other hand, the above features also tightly reply on the UE implementation, e.g.
  SI reading delay reduction needs UE to do the soft combining of the SI samples on the time domain
  High velocity also need UE to improve its receiver algorithm.
  Hence, we don’t think it can be simply concluded on requirement for non-BL UE in CE mode WITHOUT any solid analysis and evaluation on those new features.

## Slide 5: Discussion and proposal
In the latest status report [4] in RANP #82 meeting, this WI was claimed to be 100% finalized for both core and performance part, and in this sense we don’t think we could deploy those new features for non-BL UE in CE mode in R15 (TEI is not realistic to discuss new features for UE).
Based on all the background information and analysis, we propose that,
Proposal: the R15 RAN4 requirement for non-BL UE in CE mode shall reuse the R14 requirements for non-BL UE in CE mode, i.e., no requirements for new features introduced in R15 eFeMTC WI will be specified for R15 non-BL UE in CE mode in RAN4.

## Slide 6: Reference
[1] RP-172811, Revised WID on Even further enhanced MTC for LTE, Ericsson, Qualcomm
[2] R1-1807499, Introduce definition of non-BL/CE in Definitions section, Ericsson
[3] R4-1811334, Correction of terminology for non-BL CE UE for Rel-14, Ericsson
[4] RP-182591, Status report for WI Even further enhanced MTC for LTE, Ericsson