## Slide 1: Motivation for new WI on NR performance requirement enhancement
China Telecom
March 2019
3GPP TSG RAN Meeting #83
Shenzhen, China, March 18-21, 2019
Agenda: 9.1.4
RP-190257

## Slide 2: General motivation
With the very tight time schedule for NR Rel-15 performance work, several important NR features specified in Rel-15 core part are not covered when developing the Rel-15 performance requirements, such as:
  URLLC features targeting 10-5 BLER
  UE and BS receivers for handling inter-cell, inter-layer or inter-user interference
  PDSCH CA demodulation requirements are not complete in Rel-15
Meanwhile, these features are very important Rel-15 features, and some operators have plans to deploy them in the early deployments.
Thus it is proposed to open a new Rel-16 WI to define performance requirements for the selected NR features that are specified in Rel-15 core part but not covered in Rel-15 performance part.

## Slide 3: URLLC related features
Motivation
  In NR Rel-15, RAN1 has introduced new CQI and MCS tables for URLLC with target BLER of 10-5 [1].
  In Rel-16 SI on physical layer enhancements for NR URLLC, L1 improvements for achieving higher reliability of up to 10-6 level is under investigation [2].
  However, the RAN4 performance requirements for targeting 10-5 reliability are still absent [3] [4].
Propose to consider the following performance requirements:
  BS side: PUSCH requirements with 10-5 BLER test metric
  UE side:
    PDSCH requirements with 10-5 BLER test metric
    CQI reporting requirements for the CQI table corresponding to 10-5 BLER target
    PDSCH requirements for DL pre-emption indication

## Slide 4: Interference-aware receivers (1/2)
  Motivation
  Co-channel interference has substantial impact on DL and UL performance.
  In LTE, several interference-aware receivers have been introduced for data channel throughput improvement, and some of them have no impact on core specification:
    PDSCH: inter-cell interference rejection combining (IRC), inter-stream interference cancellation (IC) [5]
    PUSCH: inter-cell IRC, intra-cell inter-user IC [6]
  In NR Rel-15,
    PDSCH and PUSCH performance requirements are defined without explicit modeling of inter-cell interference, i.e., inter-cell IRC is not considered [7] [8].
    Meanwhile, PUSCH performance requirements are defined without considering intra-cell inter-stream/user interference handling [7].
  In NR NOMA SI [9], two main classes of receiver architecture are considered based on linear filters with IC for handling intra-cell inter-user interference
    Low complexity: hard-IC (hard L-CWIC)
    Medium complexity: hybrid-IC (mixing hard-IC and soft-IC/turbo L-CWIC)
  It is an efficient way to improve NR spectral efficiency by employing interference-aware receiver.

## Slide 5
  Propose to consider performance requirements with the following receivers:
  BS side:
    PUSCH requirements with enhanced receivers for handling co-channel inter-cell interference
    PUSCH requirements with enhanced receivers for handling co-channel intra-cell inter-stream/user interference
      For intra-cell inter-user interference handling, hard-IC (hard L-CWIC) and hybrid-IC (mixing hard-IC and soft-IC) receivers as defined in NOMA TR 38.812 can be considered as reference receiver
  UE side:
    PDSCH requirements with enhanced receivers for handling co-channel inter-cell interference
    PDSCH requirements with enhanced receivers for handling co-channel intra-stream interference for SU-MIMO
      Up to 4 transmission layers for SU-MIMO are to be considered, and parallel - soft IC can be considered as reference receiver
  Interference-aware receivers (2/2)

## Slide 6: CA requirements
  Motivation
  In Rel-15, the RF requirements has been specified for both intra-band and inter-band NR CA [10].
  However, for the performance part, only some SDR requirements are defined for NR CA, while the other requirements for NR CA has been de-prioritized [11].
  To verify the correct implementation of NR CA feature, PDSCH normal demodulation requirements for CA needs to be defined.
  Propose to consider the following performance requirements:
  UE side: PDSCH normal demodulation requirements

## Slide 7: Proposal and scope
The general objective is to define performance requirements for the selected NR features that are specified in Rel-15 core part but not covered in Rel-15 performance part.
The main objectives are as follows:
  Phase I (Q2 2019 to Q3 2019):
    Identify the scope and objectives for UE demodulation requirements, CSI requirements and BS demodulation requirements.
    Consider the features listed in slide #3 to #6, and make further down-selection and/or prioritization among them.
  Phase II (Q3 2019 to Q1 2020):
    Specify the UE demodulation performance requirements based on the outcome from Phase I.
    Specify the UE CSI reporting performance requirements based on the outcome from Phase I.
    Specify the BS demodulation performance requirements and conformance test requirements based on the outcome from Phase I.
    Discuss which set(s) of requirements can be release independent from Rel-15.

## Slide 8: References
[1] RP-181278, Status Report of WI on New Radio Access Technology; rapporteur: NTT DOCOMO, RAN #80, Jun 2018.
[2] RP-181477, New SID on Physical Layer Enhancements for NR URLLC, Huawei, HiSilicon, Nokia, Nokia Shanghai Bell, RAN #80, Jun 2018.
[3] R4-1809336, WF on NR PUSCH demodulation requirements, Nokia, Nokia Shanghai Bell, RAN4 AH-1807, Jul 2018.
[4] R4-1809392, Way forward on NR UE PDSCH demodulation requirements, NTT DOCOMO, Intel Corporation, RAN4 AH-1807, Jul 2018.
[5] TS 36.101, E-UTRA User Equipment (UE) radio transmission and reception
[6] TS 36.104, E-UTRA Base Station (BS) radio transmission and reception
[7] R4-1813942, WF for NR PUSCH demodulation, Nokia, Nokia Shanghai Bell, RAN4 #88bis, Oct 2018.
[8] R4-1814239, Simulation assumptions for NR PDSCH demodulation performance requirements, Intel, RAN4 #88bis, Oct 2018.
[9] RP-182478, TR 38.812 v1.0.0 on Study on Non-Orthogonal Multiple Access (NOMA) for NR, ZTE, RAN #82, Dec 2018.
[10] TS 37.865-01-01, NR Carrier Aggregation for intra-band (m Down Link (DL) / 1 Up Link (UL) bands) and inter-band (n Down Link (DL) / 1 Up Link (UL) bands)
[11] R4-1814238, Way forward on NR UE PDSCH demodulation requirements and General aspects, Intel, RAN4 #88bis, Oct 2018.

## Slide 9
Thanks!