## Slide 1: Discussion on C-IoT evolution for NR
LG Electronics
RP-190266
3GPP TSG RAN #83
Shenzhen, China, 18 - 21 Mar 2019
Agenda Item: 9.8

## Slide 2: Market roadmap for LTE-IoT
Source : “NB-IoT and LTE-M Networks Worldwide,” Global mobile Suppliers Association, Jan. 2019
By mid-January 2019,
78 operators in 45 countries have deployed or launched NB-IoT networks
30 operators in 21 countries have deployed or launched LTE-M networks
Altogether 47 countries now have at least either a launched NB-IoT network or a launched LTE-M network, there are still more than a few countries where LTE-IoT has not been deployed. And the counties may want to start their Cellular-IoT business together with NR services, herein both in the same RAT.

## Slide 3: Coexistence of LTE-IoT and NR systems
Observation and conclusion in Rel-16 Coexistence of LTE-MTC/NB-IoT with NR
  RAN1#94
    Observation in LTE-M
      From RAN1 perspective, no issues were identified that would prevent the coexistence of NR and eMTC
  RAN1#96
    Conclusion in LTE-M
      Non-backwards-compatible approaches for reduced CRS overhead or reduced impact from frequency hopping is not supported in Rel-16
    Conclusion in NB-IoT
      From RAN1 perspective, no issues were identified that would prevent the coexistence of NR and FDD/TDD NB-IoT
A set of sub-topics, however, were listed for further study to provide better coexistence property, because presumably the current LTE-IoT or NR would not be efficiently serviced when they are concurrently enabled.

## Slide 4: Objectives of release 17 NR-IoT
Coverage enhancement
  may not as much as LTE-IoT
  to compensate a loss mainly due to narrower nominal bandwidth, reduced # receiving antennas, and so on
A unified technology
  scalable in terms of bandwidth, capability, complexity and so on, but not as much as NR
  Fast and efficient mode switch depending on required power saving level, data rate, and so on
Mobility
  Power efficient RRM and cell (re-)selection

## Slide 5
Rel-13
Rel-14
Rel-15
Rel-16
Rel-12
MTC enhancements
NB-IoT
enhancement
EC-GSM-IoT
1.4 MHz bandwidth
in-band
Coverage enh. 155.7dB
FD-FDD: ~800 kbps/~1 Mbps
180 kHz bandwidth
In-band, guard-band, standalone
Coverage enh. 164 dB
inband ~22.6 kbps/ ~58.3 kbps
Up to 5 MHz BL/CE
Large TBS support
Enh. positioning : OTDOA
Multicast support
VoLTE enhancement
4Mbps/7Mbps
Positioning : OTDOA
Multicast support
Non-Anchor RACH, Paging
New power class (14dBm)
127kbps/143kbps
Mobility enh.
Power consumption (WUS)
Latency enh. (EDT)
System acquisition time (RSS)
DL 64QAM, UL sub-PRB
Early ACK for FD-FDD and TDD
Support of higher UE velocity
Power consumption (WUS)
Latency enh. (EDT)
System acquisition time (SIB)
NPRACH enhancement
TDD
Small cell
G-WUS
Tx. on Preconfigured UL resources
Multi-TB scheduling
Early CQI report
Coexistence b/w MTC and NR
Standalone MTC
MPDCCH performance enh.
Non-BL UE enh.
G-WUS
Tx. on Preconfigured UL resources
Multi-TB scheduling
Early CQI report
Coexistence b/w MTC and NR
Power saving on non-anchor carrier
eFeMTC
LTE Cat-M2 (FeMTC)
LTE Cat-M1 (eMTC)
FeNB-IoT
LTE Cat-NB2 (eNB-IoT)
LTE Cat-NB1 (NB-IoT)
Reduced complexity
Lower power
Deeper coverage
Higher density
Single-cell multicast
Positioning
Higher data rate
VoLTE enh (FeMTC)
Wake-up signal
Early data transmission
Higher spectral eff. (efeMTC)
TDD (FeNB-IoT)
Enhanced DL/UL tx. eff.
Enhanced power consumption
Coexistence
Mobility enh
Standalone MTC (MTC)
Rel-17
NR track
Rel-15
Rel-16
eMBB and URLLC oriented NR
Covers extreme corners of Use-cases
Supports almost full-flexibility
Enhanced eMBB and URLLC
Power saving
NR-U
Rel-17
Keep evolving under LTE track
Stabilization
Better coexistence with NR
Enhanced Cellular-IoT
Sub-set of techniques can be borrowed
from LTE-IoT
LPWA target

## Slide 6: Release 17 NR-IoT
Rel-17 NR-IoT may address the following aspects of Rel-16 NR
  Minimum bandwidth of SSB
    5MHz for SCS 15kHz
  Mandatory UE bandwidth
    Currently 100MHz, at minimum, for FR1
  Mandatory UE receiving antennas
    2 or 4
  Dynamic TDD configuration
    Dynamic SFI
    More than 2 DL-UL switching in a slot
  URLLC service
    intra- and inter-UE prioritization
  Different numerologies
    15kHz, 30kHz, and 60kHz for FR1
  RRM
    At minimum 4 SSBs in a cell
  No always-on signals