## Slide 1: REL-17 NR work on Connection-free Data Transfer

## Slide 2: Use cases for a burst of transmissions
There are many scenarios where UEs generate a burst of uplink transmissions and/or receive a burst of downlink transmissions in real networks.
  SNS applications generate frequent small transmissions of short texts, video clips or photos/images in a burst on the radio.
  URLLC/V2X services generate small data transmissions requiring low latency and high reliability in some cases.
  For IOT, massive number of devices generate massive number of small data transmissions in uplink.
Lots of users are using SNS applications. In addition, support of URLCC/V2X/IOT services become more important on the market. Hence, it is essential for NR to provide more efficient way of small transmissions to our customers.

## Slide 3: Drawbacks of the existing mechanisms
Frequent bursty transmissions would lead to frequent occurrences of connection establishment/resume which mean:
  CP latency before start of every burst of transmissions
  UE power consumption due to establishment/resume
  Signaling overhead due to establishment/resume
  The amount of resources wasted due to establishment/resume
  Network overhead due to management of massive number of UEs in connected

## Slide 4: New Trends in 3GPP
LTE is currently moving towards support of data transmissions in RRC_IDLE for IOT use cases.
  REL-16 eMTC/NB-IOT work plans to specify small data transmissions in RRC_IDLE focusing on IOT use cases.
  IOT small data transmissions would be supported in RRC_IDLE or RRC_INACTIVE not only for EPC-connected LTE but also for 5GC-connected LTE
Idle/inactive IOT transmission in 5GC can be extended to NR for several use cases, i.e. SNS/URLLC/V2X as well as IOT.

## Slide 5: Proposal for REL-17
Study support of uplink/downlink transmissions in RRC_IDLE and/or RRC_INACTIVE with focus on:
  frequent transmissions of a small amount of data; and
  high reliable transmissions with low latency; and
  massive number of transmissions