## Slide 1
Motivation for Study on Enhancement for Disaggregated gNB Architecture
3GPP TSG RAN Meeting #83 RP-190285
Shenzhen, China, March 18-21, 2019
Agenda Item: 9.1.3
Document for: Discussion
Source: China Telecom, CATT , China Unicom,CAICAT

## Slide 2
Background
For NR system, the disaggregated deployment has been introduced for gNB. In this deployment, gNB node is further split into two entities, namely gNB-DU (gNB Distributed Unit) and gNB-CU (gNB Central Unit). Furthermore, the benefits and scenarios for a separation of CP and UP functions have also been identified in Rel-15. In order to provides the possibility of optimizing the location of different RAN functions based on the scenario and desired performance, the CU entity is further split into two entities, namely gNB-CU-CP (gNB Central Unit control plane) and gNB-CU-UP (gNB Central Unit user plane).

## Slide 3
Intra-CU/Inter-DU Resource Aggregation
It was agreed to include NR-NR DC in Rel-15 as late drop. At the same time, with the introduction of CU/DU split and millimeter waves in network, there may be one case that two adjacent DUs have overlapping coverage for the coverage performance of FR1 is much more than that of FR2. In this case, it is reasonable to aggregate the radio resource from the two gNB-DUs to achieve the optimal performance.
Considering the intra-CU/inter-DU resource aggregation scenario has some difference with NR-NR DC architecture, further discussion and analysis on this scenario are needed

## Slide 4
Assistance Information for Handover Decision
For intra-gNB-CU/inter-cell handover, gNB-CU decides the target SpCell. Since gNB-CU doesn’t have the load status of each cell, gNB-CU may select a cell that is overloaded and the selected SpCell may be rejected by the gNB-DU.
In this case, extra delay for handover preparation would be introduced which would impact the overall performance of the handover procedure. If the handover is urgent, handover failure may happen since the suitable target SpCell could not be found promptly.

## Slide 5
Resource Utilization Improvement
For duplicated transmission within two gNB-DUs, duplicated resources would be allocated to the UE which maybe unnecessary, especially for DRB with AM mode.
For intra-gNB/ inter-gNB-DU fast re-transmission scenario, if some RLC PDU segments are lost in one leg, currently, the whole PDCP PDU will be re-transmitted in another leg. Similarly, in case of duplication transmission, currently, the discard mechanism only focus on PDCP PDU.
However, it is possible that other part of the data which share the same PDCP SN has already been transmitted successfully in the first leg. In this case, it is not necessary to re-transmit these data to save radio resources.
Further optimization of radio resource utilization for duplicated transmission and fast re-transmission should be considered

## Slide 6: Scenario for Multiple gNB-CU-UPs Connectivity
For the CP/UP separation, in the SI phase, several scenarios are identified in which the gNB-CU-UP may be either centralized or distributed. It is also analysed that different scenarios may be beneficial for different applications, for example, the distributed gNB-CU-UP may be beneficial for user plane delay critical application while central gNB-CU-UP may enable virtual deployment and applied to eMBB applications. For one UE, it is possible that it has both delay critical service and service with enormous traffic at the same time in which case the corresponding UP may be deployed separately.
The scenario that one UE connects to several gNB-CU-UPs needs to be considered.

## Slide 7: Multiple gNB-DUs connectivity for EN-DC/NGEN-DC
In EN-DC/NGEN-DC scenario, for the UE located in the overlapping area of two adjacent gNB-DUs, it is optimal to enable the UE to connect with both of the gNB-DUs and eNB. The following benefits are foreseen:
Improve the throughput for the UE
Enable MBB during inter-gNB-DU change procedure
Enable fast re-transmission in NR side
It is proposed to consider how to support one UE connecting with two gNB-DUs for ENDC/NGEN-DC scenario.

## Slide 8: Objective of this Study Item
The objectives of this SI are to:
Identifying detailed solutions to support/optimize the scenario that one UE connects to two gNB-DUs within one gNB-CU.
Further enhancement on current flow control mechanism to minimize the unnecessary radio resource utilization
Study the necessary solutions to help gNB-CU make handover decision for intra-gNB-CU/inter-gNB-DU mobility
Identifying detailed solutions to solve the left open issues on CP/UP separation e.g. how to support the scenario that one UE connects to several gNB-CU-UPs.
Identifying detailed solutions to support multiple gNB-DUs connectivity for EN-DC/NGEN-DC scenario
Time Budget: Jan,2019~June,2019

## Slide 9
Thanks For Your Attention