## Slide 1: Title: « Preliminary views on NTN activities in Rel-17 » Document type: discussion For: Information Agenda item: 15 Sources: Thales, Intelsat, HNS
3GPP RAN#83 plenary
Shenzen/China, 18-21st March 2019

## Slide 2: On going Rel 16 NTN standardisation activity
The on going Study item (FS_NR_NTN_solutions) is identifying Solutions for NR to support non-terrestrial networks (NTN)
Preliminary results are reflected in TR 38.821
Possible NR features impacted
  RAN1: timing and frequency acquisition, timing advance, random access, control loops (power, ACM, CSI), HARQ, transmission timing, ..
  RAN2: user plane timer extension, HARQ turned off, mobility handling, paging, radio link monitoring , adaptation of 2 step RACH, SN and window sizes for RLC and PDCP …
  RAN3: Tracking Area management, network identities, Hand-over robustness to latency, ..
  RAN4: Radio Resource Management

## Slide 3: Rel 17 NTN standardisation activity planning
New Work item RAN1/2/3/4 « NR support non-terrestrial networks - basic » (V1)
  Using outcomes of Rel-16 Study item FS_NR_NTN_solutions
  Mandatory changes to make NR support Non-Terrestrial networks
New Work item RAN1/2/3/4 « NR support non-terrestrial networks - enhanced » (V2)
  Using outcomes of Rel-16 Study item FS_NR_NTN_solutions
  Enhancements to improve performance/behaviour of NR in Non-Terrestrial networks context
New Work item RAN1/2/3/4 « NB-IoT evolution »
  Including
    NB-IoT supports Non-terrestrial networks integrated with 5G core network

## Slide 4: Release 16/17 NTN standardisation activities in RAN
2021 Q1
2019 Q2
2019 Q3
2019 Q4
RAN1/SI: NR non-terrestrial
RAN2/SI: NR non-terrestrial
RAN3/SI: NR non-terrestrial
Phy
layer
Access
layer
RAN
architecture
Release 16
2020 Q3
2020 Q4
2020 Q1
2020 Q2
Release 17
RAN1/WI: NR supports non-terrestrial (V1)
RAN2/WI: NR supports non-terrestrial (V1)
RAN3/WI: NR supports non-terrestrial (V1)
RAN1/WI: NR supports non-terrestrial (V2)
RAN2/WI: NR supports non-terrestrial (V2)
RAN3/WI: NR supports non-terrestrial (V2)
2021 Q2
RAN4/WI: NR supports non-terrestrial (V1)
RAN4/WI: NR supports non-terrestrial (V2)
RAN
Performance
RAN1/2/3/4/WI: NB-IoT evolution

## Slide 5: END