## Slide 1
Way Forward on Scope of Private Network for NG-RAN
China Telecom, Huawei, Nokia, Nokia Shanghai Bell, ZTE
RP-190656
3GPP TSG RAN WG Meeting #83
Shenzhen, P.R.China, Mar. 18th -21st, 2019
Document for: Discussion
Agenda Item: 9.3.1

## Slide 2: Scope of Private Network Support for NG-RAN
According to the request of SA2 non-public network functionality, the following functionality should be specified in RAN:
Support NPN in NG-RAN refer to TS23.501:
  CAG/SNPN cell discovery, selection/reselection [RAN2]
  CAG/SNPN cell access control [RAN2/3]
  For CAG, in the case of Intra-RAT intra-system and inter-RAT intra-system, the connected mode mobility support [RAN2/3]
  The connected mode mobility support within SNPN[RAN2/3]
For CAG/SNPN, necessary modifications to NG-C and Xn interfaces to communicate the CAG-ID/NID related parameters to NG-RAN nodes, respectively[RAN3]
Support CAG/SNPN with CU-DU split [RAN3]
Support CAG/SNPN with CP-UP split, if any [RAN3]

## Slide 3: Proposal
Approve the objectives listed in the previous page.
Discuss the leading working group.

## Slide 4: Appendix
Justification for Private Network Support for NG-RAN
  According to TS23.501 [1], “A Non-Public Network (NPN) is a 5GS deployed for non-public use, see TS 22.261. An NPN may be deployed as a stand-alone Non-Public Network (SNPN), i.e. not relying on network functions provided by a PLMN, or a non-stand-alone Non-Public Network, i.e. with the support of a PLMN.”
  Obviously, the former i.e. a stand-alone Non-Public Network (SNPN) could be operated in a proprietary way on top of what has been specified for 5G for a public PLMN, while the latter i.e. a non-stand-alone NPN requires further investigations on possible RAN impacts.
  Although NPN solutions are limited to the support of Vertical and LAN Services in SA2, from operator points of view, the solutions of non-stand-alone NPNs (e.g. CAG*) shall also be applicable for a much wider range of use cases, such as SOHO and residential, private NR coverage deployments and so on.
  Furthermore, the NPN support with CU/DU and CP/UP architectures also need to be investigated.