## Slide 1: Way forward on cross-carrier scheduling in DC and CA enhancements WID
Nokia, Nokia Shanghai Bell, Ericsson, Qualcomm, Intel
RP-190748

## Slide 2: Background
From RP-190184 (SR on DC and CA enhancements WI):
  Cross-carrier scheduling with different numerologies on the scheduling and scheduled carriers
    Details of the PDCCH-to-PDSCH timing need to be determined.
    Work item scope was questioned in RAN1:
      Should RAN1 prioritize the case with high-SCS scheduled cell and low-SCS scheduling cell?
      Is new DCI format for continuous scheduling of many high-SCS slots from one low-SCS slot in scope of the WI?
      Is uplink cross-carrier scheduling with different numerologies in scope of the WI?
      Should the WI enable Cross-carrier A-CSI triggering with different numerologies?
      Is revisiting UE processing time requirement, i.e. whether the processing time is based on lower SCS or not in scope of the WI?

## Slide 3: Discussion
Should RAN1 prioritize the case with high-SCS scheduled cell and low-SCS scheduling cell?
  Proposed answer: Both high-SCS scheduled cell from low-SCS scheduling cell and low-SCS scheduled cell from high-SCS scheduling cell should be supported. No prioritization is needed.
Is uplink cross-carrier scheduling with different numerologies in scope of the WI?
  Proposed answer: Yes
RAN1 is expected to resolve the remaining technical aspects as part of their work

## Slide 4: Proposed update to the WID
The objective of this work item is to investigate enhancements to DC and CA. At least the following topics should be considered in the work:
5. Cross-carrier scheduling with different numerologies on the scheduling and scheduled carriers [RAN1, RAN2, RAN4]
  This objective applies to CA only
  Includes the cases of high-SCS scheduled cell from low-SCS scheduling cell as well as high-SCS scheduling cell from low-SCS scheduled cell
  Includes uplink cross-carrier scheduling with different numerologies between scheduled cell and scheduling cell
  Target completion by RAN#84.