## Slide 1: WF on beam correspondence tolerance requirement
Intel
3GPP TSG-RAN Meeting #84 RP-191028
Newport Beach, CA USA, June 3rd – 6th, 2019
Agenda Item: 9.2.1
Document for: Approval

## Slide 2: Background
Beam correspondence requirement with UL beam sweeping has been specified based on the assumption that # of SRS =8
Beam correspondence tolerance requirements, i.e. value of Y, for PC3 were approved based on majority view in RAN4#91 [R4-1907611]
Intel and LGE expressed the technical concerns about agreed Y values
Operating band | Max ∆EIRPBC at 85%-tile ∆EIRPBC CDF (dB)
n257 | [3]
n258 | [3]
n260 | [3.2]
n261 | [3]
Note: The requirements in this table are verified only under normal temperature conditions as defined in Annex E.2.1 | 
Table 6.6.4.2-1: UE beam correspondence tolerance for power class 3

## Slide 3: Concerns about the Y values
The following issues are identified that
  In principle, RAN4 requirements should not restrict UE from achieving better performance.
  Y=3dB, which is so-called beam correspondence tolerance, can restrict some “good” UE from achieving larger EIRP gain with assistance of UL beam sweeping.
    E.g. if EIRP performance enhancement due to UL beam sweeping is more than 3dB, UE will fail the requirement and test
    As an example,
      EIRP1 is close to beam correspondence minimum requirements, e.g. 1dB short of spherical coverage at 50%-tile for PC3
      With UL sweeping assistance, EIRP2 can pass minimum peak EIRP and spherical requirements with large margin and but leads to Y’= 4dB at 85%-tile of CDF of EIRP2-EIRP1
      These UEs fail beam correspondence tolerance test since Y’ = 4dB > Y= 3dB [3.2dB for n260] in current agreement

## Slide 4: Concerns about the Y values
A set of figures to illustrate the issues
  EIRP1 is not too ‘bad’, but fails Y=3dB tolerance test
Y’ = 4dB at 85% tile of CDF of delta EIRP = EIRP2 -EIRP1
CDF curves of EIRP1 and EIRP2
1.0
0.5
0.0
11.5dB
The required Min EIRP at 50%-tile CDF for n257
10.5dB
EIRP1 CDF
EIRP2 CDF
Margin of EIRP2 @ 50%-tile
CDF curve of delta EIRP = EIRP2 - EIRP1 at top of 50% grids
1.0
0.85
4dB
Z = 1dB

## Slide 5: Proposal for beam correspondence tolerance requirements
Proposal:
To solve concerns about the Y values
  Option 1: Add additional margin on Y value. Y = [4] dB for PC3
  Option 2: Keep existing agreement Y=[3]dB unchanged and introduce the following applicability rules.
    EIRP2 should always meet the minimum EIRP requirement.
    For PC3, UE can be exempt from the BC tolerance requirement Y=3dB, providing the delta EIRP value between EIRP spherical requirement and 50-percentile of CDF value of EIRP1 is within [2.5]dB.
Considering Rel-15 time limit, one of two options should be decided in RAN Plenary #84.