## Slide 1: Motivation for new WI on-demand SI enhancement for NR

## Slide 2: Issue 1：connected mode SI request is not supported
SIBs may be needed for UEs in connected
  SIB6/7/8 for ETWS/CMAS
  SIB9 for GPS time/UTC which is important for Rel-16 IIOT TSN
  MBMS if introduced in Rel-17
  Other use cases in Rel-16/17， e.g. V2X
In Rel-15, for connected UEs, network can only use dedicated signalling to send the SI or temporarily broadcast it even if there may be no UE interested in it, which is quite inefficient. Further, considering the case that lots of UEs locating on a BWP not configured with common search space for SI-RNTI, broadcasting is not possible, SI has to be dedicated signalled to every UE on this BWP, which consumes significant radio resources. If there is URLLC traffic, the service quality may also be greatly degraded.

## Slide 3: Issue 2: resource inefficience of current SI request procedure
In NR Rel-15, for msg1 based SI request, UE can only request either one SI message or all the SI messages, it is not possible for UE to request multiple but not all SI messages.
  If UE wants to receive multiple but not all the SI messages, UE has to request them one by one, which increases UE power consumption and overall signalling.
When gNB broadcasts an on-demand requested SI, it has to broadcast it till the end of modification period, which is unnecessary in many cases.

## Slide 4: Potential enhancements
Support on-demand SI request in connected mode
  Dedicated RRC signalling support of on-demand SI in connected mode
  Msg1/Msg3 based on-demand SI request in connected mode
  The solutions should take multiple-BWP/CA, NR-DC/NE-DC/EN-DC into consideration
Optimization on signaling overhead and power consumption
  Reduce UE power consumption/signaling overhead in requesting for multiple SIs
  Improve resource efficiency when providing SIs

## Slide 5
Thanks