## Slide 1: CATT's view on NR evolution in Rel-17
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #84 RP-191462
Newport Beach, USA, June 3-6, 2019

## Slide 2: Vision of 5G
5G is expected to change every aspects of modern society
  Smart city, education, health, industry, transportation, environment, entertainment, finance, agricultures…
Agriculture
Health
Education
Transportation
Finance
Environment
Wearable devices
Home
AR
VR
Entertainment
Cloud
Mobile device
Industry

## Slide 3: Target scenarios and use cases of Rel-15/16
URLLC/eURLLC
V2X
ITU-R
Enhanced Mobile Broadband
Massive Machine Type
Communications
Ultra-reliable and Low Latency Communications
3D video, UHD screens
Smart City
Industry automation
Gigabytes in a second
Self Driving Car
Augmented reality
Smart Home/Building
Work and play in the cloud
Voice
Mission critical application
Future IMT
NBIoT/eMTC
Connection
Primary focus of Rel-15

## Slide 4: NR Evolution to Rel-17 and Beyond
User-oriented system evolution –
  Evolution of network architecture and operation
    Maximizing revenue generation – new revenue from diverse vertical applications
    Minimizing TCO (total cost of operation) – functional virtualization
  Better user experience
    Platform for user service creation
    Optimizing user perceived throughput
    Minimizing mobile phone power consumptions
Vertical Extensions of 5G network
  Network enhancement in support of vertical services
    Linkage between the user APP and server
  Functional virtualization and distributed control
  Local and small cluster optimization

## Slide 5: Rel-17 Focus Area
Enhanced support of eMBB
  MIMO enhancement
  SON/MDT
  NR compression
Enhanced support of verticals
  High accuracy positioning
  V2X enhancement and D2D
  IIoT evolution
Improvement of UE and network energy efficiency
Exploring new spectrum
  Beyond 52.6GHz
Seamless network coverage
  Integration of NTN with terrestrial network
  Multiple connectivity

## Slide 6: Potential topics for Rel-17
Continued evolution
  Power saving
  V2X & D2D
    Including broadcast/multicast
  Positioning enhancement
  MIMO enhancement
  NR non-terrestrial networks
  IIoT
  Big data collection
New topics
  NR extension to beyond 52.6GHz
  Network synchronization
  NR compression
  Multiple connectivity
  NR QoE

## Slide 7: Revolution to “Green”
Power consumption reduction for both UE and gNB through antenna adaptation
    The number of Tx/Rx antenna for UE and gNB would be dynamic adapted based on the traffic
      Both of UE and gNB would reduce the number of Tx/Rx antenna during monitoring and no traffic
      Fast antenna adaptation for high load and heavy traffic
Multi-RAT UE power saving
  Power Saving signal/channel to indicate the wakeup of selected RAT
    Preparation period – for channel tracking and triggering RS transmission
    Measurements
gNB: 4Tx/Rx for high data rate
UE: 4Tx/Rx for high data rate
gN: 2Tx/Rx for no traffic
UE: 2Tx/Rx for
PDCCH monitoring
LTE: DRX ON
NR: DRX ON
Low power
Power Saving signal triggering
Preparation
period
Preparation
period

## Slide 8: Power Saving in Rel-16
RAN1 study on UE power saving in NR had been completed in Rel-16
RAN1 work on UE power saving starting in 2nd quarter 2019
  Specify the power saving techniques with power saving signal/channel
  Specify the procedure of cross-slot scheduling power saving techniques
  Evaluate the required switching and interruption times for UE dynamic adaptation to the maximum number of MIMO layers [RAN4]
  Specify the power saving techniques with power saving signal/channel as the wakeup signal/channel in triggering UE adaptation to the DRX operation in RRC_CONNECTED mode
  Specify DCI-based mechanism in skipping PDCCH monitoring or switching PDCCH monitoring periodicity
  Specify the power saving techniques of UE adaptation to the BWP/SCell operation
  Specify the power saving techniques of UE dynamic adaptation to the maximum number of MIMO layers
  Specify the UE assistance information for the associated power saving techniques.
  Specify the power saving techniques in RRM measurements in synchronous and asynchronous network deployment
RAN2 continues study until June 2019
  DRX operation, PDCCH skipping/switching PDCCH monitoring periodicity, UE adaptation to the BWP/SCell operation, adaption to the MIMO layer, UE assistance information, RRM
  Study the enhancement of UE paging procedure based on the additional power saving signal/channel/procedure
  Study the enhancement of UE power saving procedure in supporting efficient transition from RRC_CONNECTED to RRC_IDLE/RRC_INACTIVE mode

## Slide 9: Rel-17 UE and Network Power Saving WI
Tx/Rx antenna adaptation for UE and Network
  UE dynamic adaptation to the MIMO layer
  UE adaptation to the number of Rx/Tx antenna
  Network adaptation to the number of Tx/Rx antenna based on system load and the day of use
    UE procedures in support of gNB antenna adaptation
    UE procedure in support of network cells ON/OFF in both CONNECTED and IDLE/INACTIVE states
Power saving signal/channel triggering UE adaptation to the power saving techniques in multi-RAT network [RAN1]
  Power saving signal/channel for triggering UE adaptation in both CONNECTED and IDLE/Inactive
    Study the low power consumption power saving signal
    Study and specify the interaction to Rel-16 PDCCH-based power saving signal/channel
    Specify the power saving signal triggering UE adaptation to DRX operation in multi-RAT operation, such as EN-DC, NE-DC, NR-DC, NR-CA
  Study and specify the power saving signal triggering preparation period in multi-RAT operation
    Configuration additional RS in assisting UE measurements, such as RRM and CSI measurements
    Enhancements of CSI feedbacks
Multi-RAT UE PDCCH monitoring reduction
  Power saving signal triggering PDCCH monitoring reduction
  PDCCH blind decoding reduction techniques

## Slide 10
Motivations of NR Positioning Enhancements
5G positioning performance requirements [TS 22.261]
Absolute positioning
  Horizontal: accuracy 10m to 0.3m with 95% confidence and 95% to 99.9% availability
  Vertical: 3m to 2m with 95% confidence and 95% to 99.9% availability
Relative positioning
  Horizontal: 0.2m with 95% confidence and 99% confidenceVertical: 0.2m with 95% confidence and 99% confidence
Time latency (time to first fix): from seconds to milliseconds
  Target Rel-16 positioning performance [TR 38.855]
  Horizontal positioning error < 3m (80%) (indoor ) and < 10m (80%) (outdoor)
  Vertical positioning error < 3m (80) (indoor) and error < 3m (80) (outdoor)
  Time latency (time to first fix) < 1 second
There is a huge gap between the target positioning performance in Rel-16 and the 5G positioning performance requirements defined in TS 22.261 in terms of positioning accuracy, availability and confidence level, etc.
Many promising techniques for positioning enhancements were proposed during Rel-16 NR Positioning SI [TR 38.855]. These technologies were not fully discussed due to the tight time schedule of the SI.
Huge gap

## Slide 11: Rel-17 WI: NR Positioning Enhancements
Identify the target commercial performance requirements of NR positioning based on the performance requirements defined in TS 22.261
Identify the commercial deployment scenarios (extending from Indoor office, UMi, UMa) [RAN1]
Study and specify the enhanced positioning techniques in RRC_CONNECT, RRC_IDE/INACTIVE states [RAN1]
  RAT-dependent positioning techniques with high precision (e.g., NR carrier phase based positioning, multipath mitigation techniques.)
    RS and procedure for the enhanced positioning techniques
    Optimization of resource for positioning
  Novel positioning techniques (e.g., Corporative positioning)
  Tracking application (hybrid within RAT-dependent and hybrid with RAT-independent)
Specify the functional interfaces, signaling and procedures including UE reporting for the enhanced positioning techniques [RAN2, RAN3]
Define corresponding core and performance requirements, as well as test cases for NR positioning enhancements [RAN4]

## Slide 12: Motivation of Precise Network Synchronization
Precise frequency, time and phase synchronization among TRPs for UE positioning and multi-TRP coherent communication
Network synchronization requirements
  For data communication
    Frequency synchronization accuracy within ± (0.05 ~ 0.1) ppm
    Absolute time synchronization accuracy within 3 µs for TDD cells
  For multi-TRP coherent communication – precise frequency, time, and phase synchronization in the range of ns to tens of ns.
  For NR positioning
    The time/phase synchronization should be around 1 ns (which is 0.3 meter in positioning)
Wireless network frequency/time/phase synchronization techniques
  GNSS (Global Navigation Satellite System)
  IEEE1588 PTP (Precision Time Protocol)
  SyncE (Synchronous Ethernet)
  NTP (Network Timing Protocol)
  RIBS (Radio Interface Based Synchronization)

## Slide 13: Network Synchronization based on NR Signals
Precise network synchronization based on NR reference signals were proposed recently for supporting NR positioning
  Example 1: One cell transmits the NR reference signals (e.g., PRS) periodically for time synchronization. A neighboring cell estimates the time offsets between the cells
  Example 2: On top of transmitting PRS, Cell 1 also transmits continuously the carrier reference signals (C-PRS). Cell 2 monitors PRS and C-PRS for precise synchronization
The technique can be used to whole network synchronization where multiple cells monitor the PRS and C-PRS from multiple other cells, supporting the network synchronization for both wireless data communication and positioning.

## Slide 14: Rel-17 WI: NR Network Synchronization
WI Objectives
  Explore the methods of supporting precise frequency, time, and phase synchronization for NR data communication and NR positioning based on NR radio network reference signals [RAN1]
  Identify the environments where the network synchronization based on NR signals may work properly, and/or more cost-effectively than GNSS-based and IEEE 1588 PTP based techniques [RAN1]
  Investigate and develop the NR reference signals and the methods for precise frequency, time, and phase synchronization for the Identified environments [RAN1]
  Investigate and develop high-layer architecture, protocols, messages, and configuration for supporting the synchronization approaches based on NR signals [RAN3, RAN2]
  Investigate potential and benefits of the integration of NR-based and existing synchronization approaches for supporting precise frequency, time, and phase synchronization for whole NR networks [RAN3, RAN1, RAN2]
  Define the core and performance requirements, and test cases for precise frequency, time, and phase synchronization for NR networks based on NR radio network reference signals [RAN4]

## Slide 15: Motivation of Rel-17 NR V2X
Target use case of Rel-16 NR V2X, advanced V2X service, including vehicles platooning, extended sensors, advanced driving and remote driving.
Rel-16 NR V2X WI could not specify all the aspects identified by NR V2X SI due to the limited time of NR V2X SI/WI
  Rel-16 NR V2X focuses on the design aspects of FR1
    Features specific to FR2 could be addressed in Rel-17
  Rel-16 NR V2X focuses on the design aspects of NR sidelink, some Uu enhancements would be left for future release, e.g., broadcast/multicast.
    V2X broadcast and group cast are the main use cases of Uu broadcast/multicast
Rel-16 NR V2X study does not address the coverage issues
  Range extension of Uu control V2X applications and sidelink V2X applications

## Slide 16: Rel-17 NR V2X WI
NR Uu broadcast and multicast transmission for the support of advanced V2X services
Sidelink multi-carrier operation
  Aggregation of SL communication in ITS and commercial carriers
UE-to-NW and UE-to-UE relay operation, including
  Relay UE discovery and selection procedure
  Relay UE coordinated transmission mechanism to improve link reliability
Sidelink enhancement for V2P
  Enhancement of resource allocation and sensing/collision avoidance mechanism for Pedestrian-UE
  Power saving techniques for V2P
Enhancement on multiple antenna techniques

## Slide 17: Motivation of NR sidelink for D2D
SA2 requirements of sidelink enhancement for D2D
  TS22.278 defined requirements on discovery for both commercial and PS
    Discovery procedure and related messages are up to upper layers in NR V2X
  TS22.261 defines requirement on support of UE-to-Network relay
    UE relaying resource (pool) configuration is not supported in Rel-16 V2X work
Sidelink Enhancement
  Evaluation of deployment scenarios of D2D for public safety and commercial services
    Indoor scenarios with large penetration loss
    Outdoor scenarios with extended coverage
  Sidelink enhancement in support of D2D communication –
    Coverage extension – PSSCH beamforming
    Higher data rate - multi-antenna operation and carrier aggregation
  D2D proximity discovery
    D2D discovery in support of applications (e.g., social media)
    D2D discovery to assist direct communication – network-to-UE and UE-to-UE relay
    Multi-carrier discovery – NR and LTE discovery
  Device power saving

## Slide 18: Objectives of NR Support of D2D
Objectives of NR support of D2D
  Evaluation of deployment scenarios of D2D for public safety and commercial services
    Indoor scenarios with large penetration loss
    Outdoor scenarios with extended coverage
  Extend the V2X SL framework to support D2D services for PS and commercial use cases
    Optimization of NR resource utilization through direct communication
  Study the sidelink enhancement in support of coverage extension of D2D direct communication
    UE-to-network relay -
      Multiple connectivity of UE-to-Network relay
    UE-to-UE relay
    Sidelink beamforming and beam management for FR1 and FR2
  Study the enhancements of sidelink MIMO schemes for high data rate D2D direct communication
  Study D2D proximity discovery
    Study NR sidelink physical layer structures, procedure(s), and L2/L3 protocols for D2D proximity discovery in single and multi-carrier
    Study the interaction between NR D2D discovery and LTE D2D discovery
    Study the D2D proximity discovery in assistance of UE-to-network relay and UE-to-UE relay
  Study the device power saving techniques for D2D discovery and directly communication

## Slide 19: Motivation on Uplink MIMO enhancement
UL MIMO performance is lagging behind DL
  NR UL MIMO features inherit that of LTE
  No major UL enhancement and the system has been stagnant over several releases (LTE and NR)
  Limited UL coverage and lower throughput compared to DL, potential performance bottleneck
UL MIMO enhancement motivated by
  New deployment scenarios
  New use cases
  New carrier frequency
  New system bandwidth

## Slide 20: New Deployment Scenarios for feMIMO (1)
Beyond 52.6GHz:
  Higher dimension digital MIMO precoding due to reduced wavelength and more compact array
  Advanced analog beamforming with greater number of beams, coverage, flexibility, and overhead reduction
Ultra-high-density scenario
  Very high user density and low mobility
  Very high UL data rate requirement due to e.g. video surveillance, uploading, AR/VR, wireless data center access etc.
IAB:
  Higher-order MIMO (e.g. beyond 4Tx) to achieve high data rate
V2X:
  Multi-beam related enhancements in FR2 e.g. panel TX identification and selection, fast RX panel/RSU selection and switching,

## Slide 21: New Deployment Scenarios for feMIMO
Multi-panel UE
  NR currently only supports single panel transmission, to a single TRP
  Enhancement on multi-panel joint transmission, potentially to one or different TRP, are promising for spectral efficiency and link robustness
Indoor deployment
  High frequency selectivity due to lack of LOS
  Frequency-selective precoding enabled by much wider bandwidth than LTE
AI & ML
  Network operation is becoming too complicated as the number of configuration parameters keep increasing;
  RAN-side overhead causing severe congestion/latency/interference
  A decentralized network topology, toward self-learning, prediction, and adaptation toward better energy-efficiency, overhead reduction, faster and more agile beam management

## Slide 22: Enhancement Areas on Uplink MIMO
UL frequency selective precoding
  Closed-loop based or reciprocity based
Higher-order UL-MIMO beyond 4Tx
  (e.g. V2X UE/RSU, IAB, beyond 52.6GHz), including SRS and PUSCH enhancements
Higher-order MU-MIMO
  Targeting ultra-density indoor deployment
Beam management enhancements with multi-panel TX and multi-panel/TRP RX
  Targeting FR2 considering multi-panel, multi-site and multi-RSU scenario
  Fast TX panel identification, switching, coordination, including possibly multi-panel coherent joint transmission
  Fast Rx panel/TRP selection and switching at network side (e.g. V2X RSU selection)
Study and evaluate decentralized network topology, protocol and interfaces that enable self-learning, prediction and adaptation based on AI/ML
  Targeting overhead reduction (e.g. RS overhead, CSI/beam management overhead) as a first stage

## Slide 23: Study on Higher frequency band
Study the enhancement of NR Uu interface in support of frequency band beyond 52.6GHz in Rel-17 timeframe
  Basic waveform and numerology
  Uplink and downlink channel structure
  Beam management (in MIMO work item)
52.6GHz
100GHz

## Slide 24: Motivations for NR Compression
Motivation
  Harmonization between E-UTRA and 5GS
  UDC support of “Option 3” (ENDC)
  Mobility performance
  Voice performance with NR (Options 3/2/4/7)
    UDC can improve the voice robustness for NR e.g. with Option 2. .
  Low-hanging fruit - minimal additions to NR UP.
  Power Saving with UDC
  IIoT packets effective transmission
  Large size signalling compression

## Slide 25: NR Compression Work in Rel-17
NR UDC
  RLC-AM data compression if not supported in Rel-16:
    Adopt DEFLATE based algorithm at least;
    Specify corresponding signalling and procedures
  RLC-UM data compression (may study first):
    E.g. IIoT data;
    Adopt DEFLATED based algorithm;
    Specify corresponding signalling and procedures
NR signalling size optimization aspect (may study first)
  UE capability compression
    PDCP layer vs. A new layer between RRC and PDCP
    Combination with UE capability ID based and/or segmentation
    Specify corresponding signalling and procedure if needed

## Slide 26: Motivation of Enhancement of IIoT
Rel-16 IIoT Status
  Rel-16 IIoT SI had been completed
  Rel-16 IIoT WI is planned to be completed in March 2020
    TSN
      Time synchronization with TSN
      QoS enhancement
      Ethernet header compression
    Intra-UE prioritization/multiplexing
    PDCP duplication
    Higher-layer multi-connectivity
Motivation of IIoT enhancement
  Support diverse services with different configurations:
    Data rate
    Higher protocol configuration (such as non-IP packets)
    Data characteristics – periodic data (especially non-deterministic which is low priority in R16 IIoT)
  Fast data transmission in any UE states
  Support distributed network deployment in workshop efficiently
  Further non-public network support

## Slide 27: Rel-17 IIoT Enhancement
Objectives
  Flexible L2 protocol structure, such as MAC only or RLC+MAC only for special service data
  Small data transmission
  Distributed network deployment
    Study real factory deployment scenarios for IIoT
    Study and specify the network deployment and distributed control
      E2E
      Multi-hop control nodes
      Centralized control

## Slide 28: Motivation of big data collection enhancement
Status of Rel-16 big data collection
  RAN3 prioritizes work on SON, including:
    PCI confusion handling
    Mobility Robustness Optimization
    RACH Optimization
    Load Balancing
    Capacity and Coverage Optimization
    Energy Efficiency
  RAN2 prioritizes work on MDT, including log MDT and immediate MDT.
  For L2 measurement, the following would be discussed:
    SA2 QoS monitoring solution
    SA5 defined measurements
    Active Antenna System optimization
Motivation:
  Further improve user experience and optimize radio resource allocation.
  Customize the configuration for the UE among the same/different vendors in RAN.
  Support load balance and/or network energy saving.
  Optimize V2X operation

## Slide 29: Rel-17 Enhancement of big data collection
Objective:
  UE behaviour prediction.
  Edge computing optimization including service aware RAN optimization and RAN information exposure.
  Per-UE Local RRM Policy Information Storage and Retrieval.
  V2X related information/measurements collection
Timeline:
  Study first and follow with the specification work in Rel-17

## Slide 30: Multiple Connectivity work in Rel-17
Motivation
  To improve/guarantee UE throughput for MR-DC scenario
  To improve the connectivity reliability in NR side for MR-DC scenario (Fast re-transmission is already introduced to improve reliability in Rel-15)
Objective
  Support one UE connects with more than one DUs for MR-DC scenarios.
  It could also be extended to multiple connectives among multiple gNBs(more than two legs).