## Slide 1
Relax synchronization requirement on R16 NR CA
CMCC
3GPP TSG RAN Meeting #85 RP-191790
Newport Beach, USA, September 16-20, 2019
Document for: discussion
Agenda Item: 9.4.10

## Slide 2
Three levels on synchronization in NR
  In Section 5.4.1 Carrier aggregation of TS38.300 v15.2.0 and onwards, synchronization requirements on NR CA is described as below:
    In Carrier Aggregation (CA), two or more Component Carriers (CCs) are aggregated. A UE may simultaneously receive or transmit on one or multiple CCs depending on its capabilities. CA is supported for both contiguous and non-contiguous CCs. When CA is deployed frame timing and SFN are aligned across cells that can be aggregated.
  In section 7.5.4 of TS38.133 v15.6.0, Synchronization on NR CA is described as below
    For inter-band carrier aggregation, the UE shall be capable of handling at least a relative transmission timing difference between slot timing of different carriers to be aggregated as shown in Table 7.5.4-1 below:
Table 7.5.4-1: Maximum transmission timing difference requirement for inter-band NR carrier aggregation
  Based on these requirements or descriptions, there are three different levels on synchronization, i.e., slot timing, SFN alignment and Frame timing
    In Carrier Aggregation (CA), two or more Component Carriers (CCs) are aggregated. A UE may simultaneously receive or transmit on one or multiple CCs depending on its capabilities. CA is supported for both contiguous and non-contiguous CCs. When CA is deployed frame timing and SFN are aligned across cells that can be aggregated. The maximum number of configured CCs for a UE is 16 for DL and 16 for UL.
Frequency Range | Maximum transmission timing difference (µs)
FR1 | 34.6
FR2 | 8.5
Between FR1 and FR2 | 26.1

## Slide 3
Slot timing
  About slot timing, it seems no misunderstanding, which is not only defined in NR CA as referred in last slides, but also defined for EN-DC as below:
    7.5.2 Minimum Requirements for inter-band EN-DC
    The UE shall be capable of handling a maximum uplink transmission timing difference between E-UTRA PCell and PSCell as shown in Table 7.5.2-1.
    Table 7.5.2-1 Maximum uplink transmission timing difference requirement for asynchronous EN-DC
    The UE shall be capable of handling a maximum uplink transmission timing difference between E-UTRA PCell and PSCell as shown in Table 7.5.2-2. The requirements for synchronous EN-DC are applicable for E-UTRA TDD-NR TDD, E-UTRA FDD-NR FDD, E-UTRA TDD-NR FDD and E-UTRA FDD-NR TDD inter-band EN-DC.
    Table 7.5.2-2 Maximum uplink transmission timing difference requirement for inter-band synchronous EN-DC
Sub-carrier spacing in E-UTRA PCell (kHz) | UL Sub-carrier spacing for data in PSCell (kHz) | Maximum uplink transmission timing difference (µs)
15 | 15 | 500
15 | 30 | 250
15 | 60 | 125
15 | 120Note1 | 62.5
NOTE 1: For E-UTRA FDD-NR FDD and E-UTRA TDD-NR TDD intra-band EN-DC, for which the requirement is defined in clause 7.5.3 and this Table 7.5.2-1 is also applicable, the scenario with 120kHz PSCell does not exist. |  | 
Sub-carrier spacing in E-UTRA PCell (kHz) | UL Sub-carrier spacing for data in PSCell (kHz) | Maximum uplink transmission timing difference (µs)
15 | 15 | 35.21
15 | 30 | 35.21
15 | 60 | 35.21
15 | 120 | 35.21

## Slide 4
SFN alignment
  From the referred Section 5.4.1 Carrier aggregation of TS38.300 v15.2.0 and onwards, SFN alignment is different from frame timing alignment, which is to guarantee a UE knows the SFN number on the Scell/Pcell at the time instance when the UE identifies the SFN number on a Pcell/Scell, rather than require the UE to get the SFN number by detecting MIB on the target cell.
  This concept is also adopted in handover procedure as defined in TS38.211, v15.5.0 as below:
For handover purposes to a target cell in paired or unpaired spectrum where the target cell uses , the UE may assume the absolute value of the time difference between radio frame in the current cell and radio frame in the target cell is less than if the association pattern period in Section 8.1 of [5, TS 38.213] is not equal to 10 ms.
For inter frequency handover purposes where the source cell is either in paired or unpaired spectrum and the target cell is in unpaired spectrum and uses , the UE may assume the absolute value of the time difference between radio frame in the current cell and radio frame in the target cell is less than
Which means the FR2 network has to be SFN aligned with FR1 network unless the network does not support handover from FR2 to FR1 network, however, it may not be true that all UE support DC by default. And to support intra FR1 handover, the network is expected to be SFN aligned
  Based on above understanding, it is quite straight way forward to assume SFN alignment supported by default in the real network, regardless NR CA or NR DC is deployed or not.

## Slide 5
Frame timing alignment in R15 NR CA
    On top of slot alignment, SFN alignment, Frame timing alignment means Frame boundary alignment, which is required in LTE CA, and it is copied and pasted in TS38.300 v15.2.0 by default, even it is necessarily required anymore from NR CA
    In RAN1#97 meeting, observation about the two interpretations on timing assumption, as well as their corresponding impact on the implementation is confirmed as below:
From some cross-carrier operation, e.g., cross-carrier scheduling, cross-carrier triggering, etc., in 214, at least in cross-carrier scheduling, the timing on the scheduled cell may have two interpretations:
Interpretation 1: UE takes the slot numbering of the scheduling cell as timing reference for scheduled behavior;
  If UE goes with this interpretation, frame boundary alignment or not will cause different timing in scheduled cell
Interpretation 2: UE takes the timing location of the numbering slot of the scheduling cell as timing reference for scheduled behavior;
  If UE goes with this interpretation, frame boundary alignment or not will have no impact on timing in scheduled cell

## Slide 6
Frame timing alignment in R15 NR CA
    On top of slot alignment, SFN alignment, Frame timing alignment means Frame boundary alignment, which is required in LTE CA, and it is copied and pasted in TS38.300 v15.2.0 by default, even it is necessarily required anymore from NR CA
    In RAN1#97 meeting, observation about the two interpretations on timing assumption, as well as their corresponding impact on the implementation is confirmed as below:
From some cross-carrier operation, e.g., cross-carrier scheduling, cross-carrier triggering, etc., in 214, at least in cross-carrier scheduling, the timing on the scheduled cell may have two interpretations:
Interpretation 1: UE takes the slot numbering of the scheduling cell as timing reference for scheduled behavior;
  If UE goes with this interpretation, frame boundary alignment or not will cause different timing in scheduled cell
Interpretation 2: UE takes the timing location of the numbering slot of the scheduling cell as timing reference for scheduled behavior;
  If UE goes with this interpretation, frame boundary alignment or not will have no impact on timing in scheduled cell

## Slide 7
Requirements by Cross-carrier operation
    Based on feedback from some chipset vendors on this implementation, it seems some implementation has followed Fig2.1, which means it will cause some unexpected consequence if the network without applying frame boundary alignment while supporting cross-carrier scheduling/cross-carrier triggering for the cross-carrier capable UEs, however, it does not mean the cross-carrier should always be configured even if CA is supported, in this sense, the requirement of frame boundary alignment can still be relaxed

## Slide 8
Proposals
    Proposal 1: Send RAN1&2 a LS to confirm that it is not mandatory to restrict frame timing alignment in NR CA
      State it clearly to RAN1, no more action than clarifying how to interpreter the timing in cross-carrier operation
      State it clearly to RAN2 to add slot alignment requirement and remove the frame timing alignment requirement from TS38.300 Section 5.4.1 Carrier aggregation
    Proposal 2: For NR R16, it is recommended to introduce additional UE capability to help the network distinguish if a UE require strict frame timing alignment
      In the synchronization-relaxed network, the UE requires strict frame timing alignment will not be configured with cross-carrier operation, and even carrier aggregation