## Slide 1
Views on NR coverage enhancements
3GPP TSG RAN Meeting #85 RP-191900
Newport Beach, USA, September 16-20, 2019
Agenda item: 8.1.5
Notes: 1st,

## Slide 2: Background for NR coverage enhancement
In RAN#84, NR coverage enhancement was identified as one RAN work area for Rel-17 and RAN level email discussion was assigned
  Clarify requirements for all relevant deployment scenarios focusing on extreme coverage (not including LPWA). Data rate target FFS.
  ­Start from Rel-16 email discussion outcome.
  ­Include both indoor as well as wide area.
Email rapporteur proposed the email discussion comprises two phases:
  Phase 1 (till RAN#85): Further clarify the requirement and deployment scenarios starting from initial email discussion in Rel-16 and outcome of link budget evaluation for ITU submission.
  Phase 2 (from RAN#85 to RAN#86): Scope out the objectives for the SID or WID.

## Slide 3: Requirements and scenarios
Scenarios
  Study the scenario that indoor users served by outdoor gNB, which is similar to Macro/Micro scenarios defined by ITU evaluation.
  Also including rural scenario
Services
  VoIP should also be included
  For eMBB UL data rate, medium data-rate should be guaranteed for NR, e.g., 1Mbps/2Mbps
Including both uplink and downlink channel
Prioritize evaluation for FR1. While for FR2, major differences are as follows,
  Indoor users served by outdoor gNB is not considered in this study, focused on indoor UEs served by indoor gNB. Dense urban can be also considered.
  VoIP is not considered for FR2.
  For eMBB UL data rate, medium data-rate should be guaranteed. The target UL data rate can be different from the FR1 case

## Slide 4: Proposed items for Rel-17 coverage SI
RAN1 to study the evaluation methodologies
  The MCL evaluation for both uplink and downlink shall be start point, e.g., model referred to TR 39.913.
  Further considering different antenna configurations (e.g., for different channels), and report exact coverage in terms of, e.g., maximum cell radius. This should include multi-cell link budget analysis.
  We expect a full evaluation of all channels based on the link budget results. Then we can identify the bottleneck of which channel is the bottleneck.
Note: how to split the work between NR-Light item and coverage item should be further discussed.

## Slide 5
Thanks