## Slide 1
Views on Rel-17 NR MIMO enhancement
3GPP TSG RAN Meeting #85 RP-191903
Newport Beach, USA, September 16-20, 2019
Notes: 1st,

## Slide 2: Background
MIMO work area was agreed in RAN#84 (RP-191515).
  Enhancements motivated by current commercial deployments
  Expand use cases
  E.g. Support for cases with high speed mobility, better support for FDD

## Slide 3: Potential Rel-17 scope
Motivation
  On multi-beam and multi-TRP operation there are still many items not addressed in Rel-16, and due to limited time current scope may further be down scoped. Further refinement and optimization of multi-beam and multi-TRP is necessary in Rel-17 in order to enhance the overall performance of the system. Rel-15/16 mainly focused on DL MIMO, UL MIMO can be enhanced including sub-band precoding in Rel-17. Further CSI enhancement can be considered taking into account UL/DL, DL/UL channel reciprocity.
Scope
  Multi-TRP enhancement
  Multi-beam operation enhancement
  UL enhancement
  CSI enhancement

## Slide 4: Multi-TRP enhancement
PDCCH, PUCCH, PUSCH enhancement for both FR1 and FR2
  Improved reliability of PDCCH/PUCCH/PUSCH channels
  Support of PUCCH/PUSCH simultaneous transmission
CSI feedback for M-TRP
  CSI feedback enhancement to support NCJT
Mobility support via M-TRP including inter-cell M-TRP and intra-cell M-TRP
  Seamless “handover” via fast TRP selection for both FR1 and FR2
High-speed train scenario
  E.g. enhancement of SFN transmission in high speed train scenarios

## Slide 5: Multi-beam operation enhancement
Multi-panel UE
  Simultaneous transmission across multi-panel and fast panel selection for link robustness and spectral efficiency
  Beam management enhancement for multi-panel UE and multi-TRP
  Consider efficiency including UE power consumption
Latency reduction for DL/UL beam selection
  Event based beam management procedure
  Fast and simple beam selection/switching including mobility enhancement

## Slide 6: UL enhancement
Power efficiency improvement
  PAPR reduction
  Ultra-dense indoor deployment
  PUSCH enhancement for Higher-order MU-MIMO
Spectral efficiency improvement
  SRS and PUSCH enhancement including DL/UL channel reciprocity
  Frequency selective precoding

## Slide 7: CSI enhancement
Study partial reciprocity in FDD, e.g.,
  In angular domain (e.g., AoA/AoD and ZoA/ZoD)
  In delay domain (e.g., PDP)
  In Doppler domain
Study CSI enhancements, e.g.,
  CSI feedback enhancement/optimization in conjunction with partial reciprocity at network
  CSI enhancement for specific deployment scenario such as distributed MIMO

## Slide 8
Thanks