## Slide 1: Views on Rel-17 Non-Terrestrial Networks

## Slide 2: Review of Rel-16 NTN SI Scope
Only 0.5 TU per meeting is allocated for NTN
However, too many issues have been raised
  MAC(HARQ, RACH) enhancements
    Enabling / disabling of HARQ feedback, impacts of disabling uplink HARQ feedback on DRX operation, ambiguity on preamble reception, random access with/without GNSS-capabilities, RAR window extension, RACH capacity estimation, common timing advance etc.
  Mobility enhancements for connected/idle mode
    Conditional handover, signaling overhead, signaling latency reduction, invalid configuration indication, frequent SI update, necessity of MSE mechanism, geographical area-based barring mechanism and frequency priorities etc.
  Feeder-link switch
    Feeder link switch for regenerative and transparent payload
  Service continuity between NTN and TN
    Service continuity and mobility between (outdoor) NTN coverage and indoor TN coverage, Coverage area detectability and measurements
  RLC/PDCP enhancements
    RLC/PDCP sequence numbers and window size, PDCP interruptions during handover

## Slide 3: Review of Rel-16 NTN SI Progress
Progress summary
  MAC enhancements (HARQ and RACH)
    Some consensus was reached after study on the HARQ and RACH procedure.
  Mobility enhancements for connected/idle mode
    CHO and fixed-on-earth TA were adapted. Potential solutions are just identified, but lack of technical discussion yet.
  Feeder-link switch
    Email discussion was just triggered. No discussion yet.
  Service continuity between NTN and TN
    Some issues were clarified, but it is not clear what to be discussed further.
  RLC/PDCP enhancements
    No discussion.
Further remarks
  No online discussion. Progress only relies on email discussions.
  In the RAN2#107 meeting, 5 email discussions were just opened and closed shortly.
Discussions diverges to unreasonably large extents, results in no sufficient technical discussions
Current SI progress of NTN may jeopardize the actual WI to be possibly initiated in Rel-17.

## Slide 4: Considerations for scope of Ren-17 NTN WI
For successful introduction of NTN-related features in Rel-17, it is essential to define a manageable scope
For scoping of Rel-17 NTN WI, raised issues during Rel-16 NTN SI should be carefully evaluated if each of those is essential or just good to have
In practice, Rel-17 NTN will not expected to be allocated a ‘large’ TU value.
 Rel-17 NTN WI should focus only essential features required to support NTN.
  Optimization should be considered only after essential features are mature.

## Slide 5: Work Priority Classification For Rel-17
Essential enhancements to support NTN deployments
  MAC enhancements (HARQ and RACH)
    Considering very large coverage of GEO, burst RACH and not enough RACH capacity may cause the UEs in the coverage unable to access to the network.
    Very long propagation delay of GEO may cause multiple transmissions
  Mobility enhancement for idle/connected mode
    As LEO satellites periodically appear/disappear to the UEs on the earth, unnecessary/too frequent mobility and access to the cell may happen. Also UEs cannot camp on/access to the cells because of long propagation delay
Non-essential enhancements (just performance optimization)
  Feeder-link switch
    Network implementation/deployment.
  NTN-TN service continuity
    Potential optimization can be considered only after essential NTN functionalities are mature
  RLC/PDCP enhancements
    No problems are identified yet.

## Slide 6: Proposed Scope of Rel-17 NTN WI
Enhancements to support NTN deployments
  MAC enhancements (HARQ and RACH)
    To avoid burst RACH because of large coverage by preamble allocation
    Enhancements on RACH procedure to use RACH resource efficiently
    Impacts on enabling / disabling uplink HARQ feedback
  Mobility enhancement for idle/connected mode
    Enhancements on CHO considering LEO satellites movements to improve handover robustness
    Adaptation of fixed-on-earth TA to avoid frequent TAU
    Utilization of ephemeris information and UE location information