## Slide 1: Views on Rel-16 Industrial IOT

## Slide 2: IIOT discussions in RAN2#107
RAN2 spent 6 hours (3 TUs) for discussing IIOT
  However, not much progress was made in intra-UE prioritization/multiplexing and PDCP duplication enhancements.
For intra-UE prioritization/multiplexing;
  RAN2 discussed PUSCH vs. PUSCH conflicts and SR vs. PUSCH conflicts, and made some agreements. However, due to the potential RAN1 impacts, RAN2 could not make firm decisions.
  RAN2 finally decide that intra-UE prioritization/multiplexing is deprioritized until RAN1 has made more progress.

## Slide 3: IIOT discussions in RAN2#107
For PDCP duplication enhancements;
  Network-controlled mechanism had good progress, but UE-based mechanism was controversial and no conclusion was reached.
  E-mail discussion summary on UE-based mechanisms;
    UE-based leg selection is not supported by RAN2.
    UE-based number of copies selection is not pursued by RAN2.
    UE-based activation/de-activation of PDCP duplication needs discussion whether or not to introduce such mechanism.
    Per-packet packet duplication is to be agreed by RAN2.
  RAN2 finally decide that UE-based activation/deactivation and per-packet duplication will be treated with less priority at least for the RAN2#107bis meeting.

## Slide 4: eURLLC discussions in RAN2#107
RAN2 spent 1 hours (0.5 TU) for discussing eURLLC
  However, many companies think that there are too many overlaps with IIOT, and don’t know what to do in this WI. Still there are many issues not resolved in RAN1.
  Moreover, RAN2 agreed that a single CR will be produced for the aspects overlapped with IIOT.

## Slide 5: Proposal for Rel-16 IIOT
RAN2 de-prioritize intra-UE prioritization/ multiplexing until RAN1 make sufficient progress.
  This objective could be moved from IIOT to eURLLC.
RAN2 discuss only per-packet duplication among various UE-based mechanisms.
  However, it should be de-prioritized until basic scheme of more than 2-leg duplication is completed.
RAN2 merge TUs for IIOT and eURLLC.
  Focus on scheduling enhancement for TSC supporting multiple CG/SPS.

## Slide 6: RAN2 focus in 4Q
RAN2 focus on followings in 4Q:
  PDCP duplication enhancements
    Per-packet duplication can be discussed in RAN2#108 if basic scheme is completed.
  Ethernet header compression
  Reference timing delivery
  Scheduling enhancement for TSC