## Slide 1: Views on UDC and IDC in TEI16

## Slide 2: UDC and IDC discussions in RAN#83
UDC and IDC were proposed as Rel-16 WIs in RAN#83.
After severe discussion, those two items were agreed to be excluded from Rel-16 due to RAN2 work overload.

## Slide 3: UDC and IDC discussions in RAN#83
Following the conclusion, RAN2 chairman assessed that no further WIs can be agreed (RP-190750).
No discussion was held on UDC and IDC in RAN#84

## Slide 4: UDC and IDC discussions in RAN2#107
In RAN2#107, TU was allocated for TEI16, and UDC and IDC were proposed as TEI16.
The proponents of those items claimed that;
  The possibility to discuss them in TEI16 is not excluded.
  They are merely copy of LTE mechanism, and could be handled in TEL16.
RAN2 spent some time to discuss those items (UDC in UP session, IDC in CP session), but no conclusion was reached.
  The discussion was postponed, and RAN2 chair decide to report this discussion to RAN#85.

## Slide 5: LG Electronics’ view on UDC and IDC
The possibility to discuss them in TEI16 was already discussed in RAN#83, but not agreed.

## Slide 6: LG Electronics’ view on UDC and IDC
NR and LTE are different, and mere copy of LTE mechanism may not work in NR.
For UDC;
  LTE UDC operates on AM RLC where in-sequence delivery is guaranteed. However, NR RLC uses out-of-order delivery.
  Dual Connectivity was not considered for LTE UDC, but it has to be considered in NR UDC to support EN-DC.
For IDC;
  Beam, BWP, and SUL were not considered in LTE. The impacts of them should be cautiously evaluated.

## Slide 7: Proposals
RAN gives clear guideline to RAN2 that RAN2 do not discuss UDC and IDC in Rel-16, neither as new WI nor as TEI16.