## Slide 1: Motivation of new work item: NR Network Synchronization in Rel-17
RP-191980
3GPP TSG RAN WG Meeting #85
Newport Beach, USA, Sept 16 – 20, 2019
Document for: Discussion
Agenda Item: 8.2.5
China Academy of Telecommunications Technology (CATT)

## Slide 2: Network Synchronization
It is essential to support cost-effective techniques for precise frequency, time and phase synchronization for NR wireless networks
Frequency synchronization
  Baseband signals are mixed with the carrier frequency for transmission and the reception. Carrier frequency accuracy and stability have direct impact on the performance of the wireless communication
Time synchronization
  Accurate timing is critical for supporting the various operations, such as antenna switching, start/stop of data sampling, carrier aggregation, MBMS, and especially NR positioning
Phase synchronization
  Phase synchronization is between frequency synchronized signals. Phase synchronization is crucial for beamforming, MIMO, and carrier phase based precise NR positioning

## Slide 3: NR Synchronization Requirements
Synchronization requirements for NR data communication
  Frequency synchronization accuracy [TS 38.104]
    ±0.05 ppm for wide area BS
    ±0.1 ppm for medium range and local area BS
  Cell phase synchronization accuracy [TS 38.133]
    the maximum absolute deviation in frame start timing between any pair of cells on the same frequency that have overlapping coverage areas within 3 µs for TDD cells
  Time alignment error [TS 38.104]
    For MIMO or TX diversity transmissions, at each carrier frequency, TAE shall not exceed 65 ns.
    For intra-band contiguous carrier aggregation, with or without MIMO or TX diversity, TAE shall not exceed 260ns.
    For intra-band non-contiguous carrier aggregation, with or without MIMO or TX diversity, TAE shall not exceed 3µs.
    For inter-band carrier aggregation, with or without MIMO or TX diversity, TAE shall not exceed 3µs.
Synchronization requirements for NR positioning
  3GPP has so far not defined the network synchronization requirements for LTE/NR positioning.
  It is well-understood that network synchronization requirements for NR positioning will be much tighter than that for NR data communication

## Slide 4: Existing Network Synchronization Techniques
Techniques popularly used for the time and frequency synchronization of wireless networks include GNSS-based and IEEE 1588 PTP based methods
GNSS based
  Capable of supporting from µs-level to ns-level synchronization
  Major drawbacks :
    Not suitable for environments where GNSS signals are weak or blocked, such as indoor scenarios
    Significantly high installation and operational costs especially in city area
IEEE 1588 PTP (Precision Time Protocol)
  Based master/slave synchronization paradigm
  PTP estimates the time difference between the master and slave devices from the round-trip delay
  Major drawbacks:
    Synchronization accuracy is impacted by network asymmetry (delay difference between the send path and receive path) and Packet Delay Variation (PDV)
    A chain of network elements between the master and the slave with variable network load and varying queuing and processing delays can cause delay variations in the PTP messages
    Changes in packet arrival time are problematic, since the slave cannot identify the difference between variation in packet delay and a timing drift in the master

## Slide 5: Radio-interface based Synchronization
3GPP has investigated radio-interface based synchronization (RIBS) solutions for LTE networks
In RIBS, one or more cells monitors the reference signals (e.g, CRS, CSI-RS and PRS) from other cells to estimate the time offsets among the cells and maintain synchronization among them
It was shown that RIBS can obtain 3 s or better synchronization accuracy under reasonable SNR level for LTE networks [TR 38.898, TR 38.872]
RIBS solutions based on NR reference signals were proposed recently for supporting NR positioning [Ref. 5–7]
RIBS may support very precise time/phase/frequency synchronization with carrier phase tracking techniques [Ref. 8]
  When the phase lock loop (PLL) of a cell is locked to the carrier signal from another cell, any the time and phase changes between cells, which may be caused by clock drifts and frequency offset or other factors, are tracked by the PLL.
Optimized network synchronization solutions can be developed based on the RIBS architecture that supports flexible configuration of the resource usage, information exchanges among the cells (e.g., timing measurements)
Cost-affective and reliable network synchronization solutions can be further developed based on the combination of NR RIBS with other network synchronization techniques

## Slide 6: Salient advantages of NR RIBS
It works without the dependency of external signals
It can work by reusing NR signals transmitted for NR data communication and/or NR positioning without additional RF resources
It may save significant deployment cost in the installation and implementation of the network
Full time, phase and frequency synchronization can be achieved for precise UE positioning (e.g., cm-level positioning).

## Slide 7: Rel-17 WI: NR Network Synchronization
WI Objectives
  Explore the RIBS mechanisms for precise frequency, time, and phase synchronization for NR data communication and NR positioning based on NR reference signals [RAN3, RAN1]
    New NR reference signals can be introduced for supporting NR RIBS if necessary [RAN1]
  Investigate effective NR RIBS architecture for supporting flexible configuration of the resource usage, information exchanges (e.g., timing measurements) among the cells for performance optimization [RAN3]
    Architectures that support the combination of NR RIBS with other synchronization techniques for more reliable and accurate synchronization of NR networks may also be considered
  Define high-layer architecture, protocols, messages, and configuration for supporting the synchronization of NR networks [RAN3, RAN2]
  Define the core and performance requirements, and test cases for NR RIBS [RAN4]

## Slide 8: References
3GPP TS 38.104, “NR; Base Station (BS) radio transmission and reception”
3GPP TS 38.133, “NR; Requirements for support of radio resource management”
3GPP TR 36.898, “Network Assistance for Network Synchronization”
3GPP TR 36.872, “Small cell enhancements for E-UTRA and E-UTRAN - Physical layer aspects”
R1-1902344, “Discussion on measurement reporting for network synchronization error compensation scheme”, CMCC
R1-1901849, “DL and UL based NR Positioning”, Nokia, Nokia Shanghai Bell
R1-1903141, “On the use of RTT for positioning”, Ericsson
R1-1905350, “Network synchronization based on RAT-dependent signals”, CATT