## Slide 1: Supporting High Accuracy Positioning for A-BDS
CATT, CAICT
RP-191984
3GPP TSG RAN WG Meeting #85
Newport Beach, USA, Sept. 16 - 20, 2019
Document for: Discussion
Agenda Item: 8.2.5

## Slide 2: Outline
Background and motivations
Proposed work scope of supporting high accuracy positioning for A-BDS

## Slide 3: Background and motivation (1)
In 2017, China Satellite Navigation Office published Interface Control Documents of Open Service Signals B1C and B2a for Beidou Navigation Satellite System (Version 1.0)
B1C signal is the main core signal of BDS, which uses the same frequency as GPS L1 and satisfies the “civil signal compatibility and interoperability” requirements of satellite navigation system.
B2a signal can be used together with B1C to support multiple-frequency, higher-accuracy positioning etc.
BDS has provided global navigation services since 2018.
In the RAN2#107 meeting, it was agreed that the B1C signal can be introduced in TEI16.
Reference : China Satellite Navigation Office, “Beidou Navigation Satellite System Signal in Space Interface Control Document—Open Service Signal B1C (Version 1.0)”, www.beidou.gov.cn/xt/gfxz/201712/P020171226741342013031.pdf, Dec. 2017.
China Satellite Navigation Office, “Beidou Navigation Satellite System Signal in Space Interface Control Document—Open Service Signal B2a (Version 1.0)”, www.beidou.gov.cn/xt/gfxz/201712/P020171226742357364174.pdf, Dec. 2017.
Proposal: Introduce B2a signal to support multiple-frequency positioning in Rel-17.

## Slide 4: Background and motivations (2)
  Background:
  In Rel-15, Positioning Accuracy Enhancements for LTE WI (RP-181298 has specified the requirements for supporting RTK, N-RTK, SSR and PPP for A-GNSS but which only considers GPS and GLONASS satellite navigation systems.
  In Rel-16, the extension work to support GNSS SSR (PPP-RTK support) based on the “Compact SSR” definitions specified for QZSS for both LTE and NR is under discussion in RAN2.
  BDS has been used widely to support global positioning including high accuracy positioning with RTK, N-RTK, SSR and PPP techniques.
Motivations:
  Similar to other GNSS (e.g. GPS and GLONASS), there is a need for 3GPP to introduce the requirements to support high accuracy positioning for A-BDS.
  Observation: Both above work items do not consider Beidou navigation system.
  Proposal: Supporting high accuracy positioning for A-BDS for both LTE and NR.

## Slide 5: Proposed work scope of supporting high accuracy positioning for A-BDS
Support multiple frequencies positioning:
  Introduce new signal, e.g. B2a, which can be used together with B1C
Support RTK, PPP, SSR for A-BDS:
  Define extensions of LPP protocol to support GNSS RTK, PPP and SSR definitions specified for A-BDS for both LTE and NR
  Define extensions of LPPa and NRPPa to support GNSS RTK, PPP and SSR assistance information for A-BDS
    Note: Both PPP and RTK are already supported in Rel-15 LPP. SSR is already supported in Rel-15/Rel-16. The extensions are for RTK, PPP and SSR which requires additional info for A-BDS in Rel-17.
See detailed WIDs in RP-191985