## Slide 1: Motivation on Further MIMO Enhancements in Rel-17
CATT
RP-191988
3GPP TSG RAN WG Meeting #84
Newport Beach, California, USA
September 16 – 20, 2019
Agenda Item: 8.2.3

## Slide 2: Motivation
UL MIMO performance is lagging behind DL
  Core features of NR UL MIMO inherited from LTE
  No major UL enhancement over years and the UL system has been stagnant over several releases (LTE and NR)
  Subpar UL coverage and throughput compared to DL
UL MIMO enhancement in Rel.17 motivated by
  New deployment scenarios
  New use cases
  New carrier frequency
  New system bandwidth

## Slide 3: New Deployment Scenarios
Beyond 52.6GHz:
  Smaller wavelength and more compact antenna array makes higher-order digital MIMO precoding possible
  Advanced analog beamforming is needed with more beams, better coverage, greater flexibility, and reduced overhead
Ultra-high-density scenario
  Very high user density and low mobility (e.g. indoor office)
  Very high UL data rate due to particular applications, e.g. video surveillance, video uploading, AR/VR, wireless data center access
IAB:
  Higher-order MIMO (e.g. beyond 4Tx) to achieve high data rate
V2X:
  Multi-beam and multi-panel related enhancements in FR2, e.g.
  UL TX identification and selection,
  UL RX panel (including RSU) selection and switching

## Slide 4: New Deployment Scenarios
Multi-panel UE
  NR currently only supports single panel UL transmission
  Enhancement on multi-panel joint transmission is considered beneficial but lacks time to materialize in Rel.16
  Multi-panel transmission are promising for spectral efficiency and link robustness
  Applicable in eMBB and URLLC
Indoor deployment
  LTE/NR only supports wideband precoding in the UL
  Frequency-selective precoding may achieve substantial throughput gain, considering much wider system bandwidth than LTE, use cases with rich multipath propagation and large channel selectivity (e.g. urban micro)

## Slide 5: Potential Enhancement Areas
UL frequency selective precoding
Higher-order UL-MIMO beyond 4Tx
  (e.g. V2X UE/RSU, IAB, beyond 52.6GHz), including SRS and PUSCH enhancements
Higher-order MU-MIMO
  Targeting ultra-density indoor deployment
Beam management enhancements with multi-panel TX and multi-panel/TRP RX deployment
  Considering multi-panel, multi-site and multi-RSU scenario

## Slide 6: Draft Rel.17 Enhancement Scope
Evaluate, identify and specify UL MIMO enhancements in both digital and analog beamforming
  Specify frequency-selective UL precoding
  Specify higher-dimension UL-MIMO beyond 4port (e.g. V2X UE/RSU, IAB, beyond 52.6GHz), including SRS and PUSCH enhancements
  Specify advanced analog beamforming targeting FR2 considering multi-panel, multi-site and multi-RSU scenario
    Fast TX panel identification, switching, coordination, including possibly multi-panel coherent joint transmission
    Fast Rx panel/TRP selection and switching at network side (e.g. V2X RSU selection)
  Evaluate and specify, if sufficient gain is found, higher-order UL MU-MIMO targeting ultra-density indoor deployment