## Slide 1
China Unicom
Motivation paper for study on NR QoE management and optimizations for diverse services
3GPP TSG RAN meeting #85 RP-192016
USA, Sep.16-20, 2019

## Slide 2: VR market growing rapidly
VR consumer market has grown rapidly in last two years, and VR will be a popular 5G service provided by operators. It is forecast that the VR market in China will grow up to $ 24billion by the end of 2021. 5G VR will be a new growth for revenue.
5G brings new opportunities in new vertical industries, and these new applications and services require operators to provide a high-quality 5G network and guarantee the performance of all 5G new services.
Chart: VR Market Forecast for China(Billion/$)
| 2017 | 2018 | 2019 | 2020 | 2021
2017 2018 2019 2020 2021 | 2.2857 | 4.1143 | 7.4 | 13.3286 | 24

## Slide 3: 5G is very attractive for VR
OpenXR was established for promoting and developing the VR ecosystem. The main objective is to solve the IoDT issue of different VR devices and applications.
Based on Cloud VR architecture and hardware facilities, application processing and content rendering are operated on the cloud platform. Cloud VR is beneficial for reducing the weight, size and cost of devices, which is critical for VR market expansion.
For the VR industry, 5G network provides the interactive link between VR devices and platform, and all the data between the platform and the device can be transfered via 5G network.

## Slide 4
SA4 WI of VR QoE
In SA4, the SI of “QoE metrics for VR” has been completed. The related WI“VR QoE metrics” was approved in June, and the target completion date is December, 2019.
This WI is to add VR QoE metrics functionality to 3GPP specifications, covering at least the following aspects:
  A client reference model for VR QoE measurements;
  Basic VR device metrics;
  Metrics describing the VR interaction delay;
  Expanded configuration and reporting schemas to cover the above.
There is a need to define QoE metrics for VR services, and at least the basic and most important aspects of the VR experience can be exactly measured.

## Slide 5
SA4 SI of XR In 5G
During SA plenary #99, the new SI “Study on eXtended Reality (XR) in 5G”was approved in SP-180667. The latest completion level is 45%, and the target completion date is December, 2019.
For the SI, the main objectives are as below:
  Collecting the associated use cases and identifying the 3GPP service(s) they map to;
  Identifying relevant QoS service parameters and other core network and radio functionalities that would be required or at least beneficial for XR use cases;
  Collecting key performance indicators for relevant XR services and the applied technology components.
During the study, companies are interested in XR use cases, QoS metrics/QoS parameters, XR architectures and functions.

## Slide 6
Key Metrics of Cloud VR (for example)
Four interaction types of Cloud VR service and the network requirements of customer's experience (including bandwidth, latency and packet loss rate) are summarized in the following table.
Standard |  | Pre-VR | Entry-Level VR | Advanced VR | Ultimate VR
Weak interactive VR | Typical code rate | 16Mbps | Full screen： 50Mbps（2D）; 80Mbps（3D） FOV： 26Mbps（2D）; 42Mbps（3D） | Full screen：420Mbps FOV：220Mbps | Full screen：2.94Gbps FOV：1.56Gbps
 | Typical bandwidth requirement | 25Mbps | Full screen： 75Mbps（2D）; 120Mbps（3D） FOV： 40Mbps（2D）; 63Mbps（3D） | Full screen：630Mbps FOV：340Mbps | Full screen：4.40Gbps FOV：2.34Gbps
 | Typical RTT | 30ms | 30ms（2D）; 20ms（3D） | 20ms | 10ms
 | Typical network packet loss rate | 2.40E-04 | 2.40E-05 | 1.00E-06 | 1.00E-06
Strong interactive VR | Typical code rate | 18Mbps | 40Mbps（2D）; 60Mbps（3D） | 390Mbps | 680Mbps
 | Typical bandwidth requirement | 50Mbps | 120Mbps（2D）; 200Mbps（3D） | 1.40Gbps | 3.36Gbps
 | Typical RTT | 10ms | 10ms | 5ms | 5ms
 | Typical network packet loss rate | 1.00E-06 | 1.00E-06 | 1.00E-06 | 1.00E-06

## Slide 7
Network requirements of URLLC services (for example)
The requirements of URLLC services, such as electrical power distribution and factory automation (in TR 38.824), are summarized in the following table.
Use case | Reliability (%) | Latency | Data packet size and traffic model | Description
Power distribution | 99.9999 | 5 ms (E2E latency) Note: 2-3 ms air interface latency | DL & UL: 100 bytes ftp model 3 with arrival interval 100 ms | Power distribution grid fault and outage management (TR 22.804:5.6.4)
 | 99.999 | 15 ms (E2E latency) Note: 6-7 ms air interface latency | DL & UL: 250 bytes Periodic and deterministic with arrival interval 0.833 ms Random offset between UEs | Differential protection (TR 22.804:5.6.6)
Factory automation | 99.9999 | 2 ms (E2E latency) Note: 1 ms air interface latency | DL & UL: 32 bytes Periodic deterministic traffic model with data arrival interval 2 ms | Motion control

## Slide 8
QoE evaluation scheme of VR service (for example)
The QoE of VR service refers to the level of presence perceived by VR users. It is evaluated based on the level of immersion provided by VR system and the quality of the interaction link between users and VR environment.
Key QoE metrics of VR are as below:
  Video quality: three-dimensional attributes, number of pixels per degree, code rate, projection, angle of view, compression, frame rate.
  Audio quality: three-dimensional attributes, channel and sampling rate, compression.
  Degree of freedom: three degrees of freedom.
  Network quality: perceived delay, number of cartons;
  Display quality: playback quality, audio and video synchronization, audio and video spatial alignment.
  Interaction quality: VR environment interaction, VR interaction space accuracy.

## Slide 9
Scenarios
    In UTRAN and E-UTRAN, QoE Measurement Collection (QMC) for streaming services have been specified in relevant WI. In LTE QoE WI (the WID RP-181640), operators utilize QoE measurements to evaluate user experience accurately. Moreover, operators can combine QoE measurement with radio measurement optimize the network parameters to provide a better user experience.
    Typical Traffic Types for QoE Measurement Collection:
  Streaming service
  MTSI service, e.g. OTT voice
  AR/VR video service, and real-time gaming
  URLLC, e.g. remote healthcare, and smart factory
    Network Deployments:
  NR SA, NR NSA, MR-DC
  Note: Rel-17 QoE feature should focus on the NR related network deployments.

## Slide 10
Motivation
QoE management in 5G will not only collect the experience related parameters of traditional audio/video/streaming services but also consider 5G new services (AR/VR and URLLC).
According to 5G service requirements, it is proposed to focus on adaptive QoE management schemes, and corresponding network intelligent optimizations to fulfill the requirements of diverse services in R17.
  For UTRAN and E-UTRAN, QoE Measurement Collection for streaming services have been specified. In 5G era, the 5G network will support diverse services (e.g. various kinds of vertical industry). It is observed that the 5QI will not exactly reflect the user experience in 5G network.
  On top of the fact that user KPI/KQI information could be collected from the RAN side, it is believed that QoE information could be applied to efficiently improve user experience and optimize network resource configuration/utilization.

## Slide 11
Scope for NR QoE
NR QoE in RAN
The RAN-side QoE measurement metrics is collected from UE side, in order to support traditional stream services and other new NR services, the following aspects can be considered:
Mechanism to support for RAN QoE parameters collection and RAN network optimization.
  Define trigger, configuration and optimization procedure for QoE measurement collection.
  Define and optimize QoE measurement reporting procedures.
  Define UE service type-relative RAN QoE parameters, e.g. VR/AR, streaming, URLLC .
Mechanism for QoE-assistant network resource management.
  Solutions to optimize the RAN resource utilization according to the QoE report.
RAN provides the resource usage information to OAM or CN (Core Network) for UE-specified customized service requirements.

## Slide 12
Thank you!