## Slide 1: Rel-17 NTN Support for NB-IoT - Motivation -
MediaTek Inc., Eutelsat, Novamint, Sequans, Fraunhofer, TNO
RP-192067
3GPP TSG RAN#85
Newport Beach, CA, USA
September 16th -20th , 2019
A.I. 8.1.6

## Slide 2: Ubiquitous NB-IoT Accelerate global industries transformation
IoT = lifeline
  Many industries depend on IoT e.g. transportation & logistics, energy, utilities, farming, environment, etc.
  Operation in areas with low/no cellular connectivity
Satellite NB-IoT: connectivity in remote areas with low/no cellular connectivity
  Deep rural areas, mountains, oceans, terrestrial/maritime/rail road networks etc.
  Complementary to cellular NB-IoT
Satellite NB-IoT bridges the coverage gap to
  Enable and secure new businesses
  Prevent service outage for business critical uses
Clear existing global market demand for true global IoT coverage with NB-IoT cost structure
  A number of competing proprietary solutions already exist e.g. Iridium IoT, Inmarsat, Sigfox, LoRA, etc.
  Critical timing
Satellite NB-IoT is a major opportunity to fill a known market gap with a successful proven cost-efficient and energy-efficient technology with unprecedented economies of scale

## Slide 3: Satellite NB-IoT Proposal
Simple adaptation to satellite use
  Preserving NB-IoT cost & energy efficiency
Very limited specification impact
  System information, paging, TAU [RAN2]
  Mobility [RAN2, RAN4]
    Idle mode beamspot / cell re-selection
  Initial access [RAN1/RAN2]
    Timing advance acquisition and update
    New RACH preamble format (*)
    4-step RACH
  RRM/RF performance requirements [RAN4]
No need to disable HARQ
  Legacy HARQ scheduling delay can accommodate delay
  Latency is not an issue for delay-tolerant IoT applications
Simpler operations with NB-IoT
  No HO in connected mode
  No CSI UE re-selects new cell when RLF is triggered
Can also be deployed inband an NR carrier
  see RP-190846 – Rel-16 NB-IoT WID
NOTE *: may not be needed for LEO 600km depending on maximum cell size

## Slide 4: NOTES Leverage of NTN NR SI Recommendations
The following NR NTN SI recommendations could be reused for NB-IoT
  Satellite-assisted SI
  Pre-compensation for common Doppler, common propagation delay, UL frequency correction indication in Msg2 in RA procedure
  NTN NR SI Recommendations pending confirmation by RAN
Issues associated to NB-IoT to be studied and solutions defined taking into account NR NTN SI outcome