## Slide 1: 3GPP TSG RAN Plenary Meeting #84 RP-192109 Newport Beach, USA: June 3-6, 2019 Agenda item: 8.1.10 Source: AT&T Title: IAB Enhancements for Rel 17 Document for: Discussion/Decision

## Slide 2: IAB Enhancements - Overview
    Use case enhancements
    Mobile IAB nodes – Support for CP/UP split, group mobility, access aware/local traffic routing
    IAB-U – IAB in unlicensed spectrum, beam-based LBT, mesh connectivity
    Topology related enhancements
    Inter-CU topology adaptation
    Mesh-connectivity between IAB nodes for local control/user plane routing
    User plane enhancements
    Duplication and network coding over redundant routes – efficient reliability improvement
    Multi-hop scheduling enhancement – exchange of benefit metric between IAB nodes to enable radio-aware multi-hop scheduling to improve throughput performance
    Hop-by-hop flow control – manage local congestion
    PHY/RF enhancements
    Multiplexing beyond TDM (FDM/SDM/multi-panel Tx/Rx), case 6/7 timing alignment, DL power control optimization, built on a forward compatible Rel.16 design.

## Slide 3: Mobile IAB
  Regular (Rel-16) IAB nodes and Rel-17 mobile IAB nodes may be part of the same tree
  Separate CP and UP architecture  UP is similar to Rel-16 IAB (hierarchical tree) and CP is a single hop
    Reduces disruption and latency for downstream IAB in case of link failure/HO events
  Introduce support for “group mobility” (e.g. HO for UEs on a bus that is acting as mIAB node)
  Access UE enhancements which support awareness of IAB deployment and architecture can also be considered (e.g. based on hop count + RRM measurements)
Mobile IAB Topology
Donor
Hop 1
Hop 2
MT U-Plane
UE C/U-Plane
MT C-Plane

## Slide 4: Multi-Panel Tx/Rx (MPTR) for IAB
Multi-panel Tx/Rx on a IAB-node (e.g. DU Tx/MT Rx) basis may have limited standards impact
Simultaneous multi-panel transmission for IAB
    SDM: Simultaneously Tx or Rx on backhaul and access links
    MPTR: Simultaneously Tx and Rx on backhaul and access links (UEs to remain half-duplex)
Reduction in latency and more efficient frame structure for IAB nodes
Specific CLI characterization and mitigation enhancements for MPTR should be studied
    Ensure that access UEs are not impacted by different multiplexing alternatives
SDM
MPTR
SDM
MPTR
MPTR

## Slide 5: Multi-hop Scheduling Enhancement
    Introduce generic field at BAP layer (BAP CE or header) to allow exchange of benefit metric between child and parent IAB nodes
    Specific benefit metric need not be defined (left up to companies to innovate upon)
    Enabler for radio-aware multi-hop scheduling
    Shown to provide significant improvement to experienced user throughput:
        E.g. multi-hop scheduling metric computed based on multi-hop capacity derived from access and backhaul link effective SINR values shows significant improvement in user experienced throughput (simulation results from fully dynamic event-driven system-level simulation of an IAB network)

## Slide 6: IAB Power Control
At the IAB node the received power level of the backhaul (DL) and access (UL) can be very different. The access (UL) is power controlled whereas the backhaul (DL) is not power controlled. Lead to significant difference is received PSD across backhaul and access.
A similar problem also happens on the transmit PSD between the backhaul and access. The backhaul (UL) and access (DL) have very different EiRP.
FDM/SDM of backhaul and access Tx/Rx functions on the same RF chains (or panels) is not possible without enhancements to power control.
The alternating frame-structure across the multiple hops leads to CLI. CLI measurement and mitigation is a key functionality to make IAB operate effectively and efficiently.

## Slide 7: IAB-U – IAB in Unlicensed Spectrum
Rel-17 NR-based access to unlicensed spectrum
Primary focus is unlicensed spectrum beyond FR2, e.g., E-band, but also 6 GHz
RAN #82 agreed a study on NR beyond 52.6 GHz to be concluded at RAN #86 (RP-182861)
Regulatory requirements as well as NR design requirements and considerations pertinent to IAB and directional LBT shall be addressed in Rel. 16 already
Allow for no LBT for fixed backhaul links in IAB  Beam-based LBT design
Mesh connectivity
Donor
gNB-DU
Donor
gNB-CU
IAB-node 1
IAB-node 2
IAB-U
Link 1
(NR-U)
DU
MT
DU
MT
DU
IAB-U
Link 2
(NR-U)
UE
Access
Link
(NR Uu)

## Slide 8: Network Fountain Coding for IAB
Packet duplication via multiple IAB paths/links can provide good reliability but it is highly inefficient
Fountain code is an outer rate-less code applied at a higher layer (FEC at PHY is not touched)
    Fountain coded segments are transmitted over multiple paths/links
    Any combination of N coded segments from any paths can be used to decode
    Can achieve the same reliability as packet duplication with much less overhead
Fountain Encoder
Decoder
Message Passing
Path 1
Path 2
Path 3
pkt
Core
Network
IAB Donor
Access UE
Access
IAB
pkt
Any combination of 3 segments from any path is enough to decode

## Slide 9: IAB Enhancements - Summary
    IAB is an important feature developed in Rel-16 with many practical deployment benefits. Due to the tight timeline to complete the first version of IAB in Rel-16, certain proposed features will be pushed out to the next release. Such enhancements need to be considered in Rel-17.
    Furthermore, additional use cases and enhancements need to be developed in Rel-17 to continue benefits offered by this useful feature.
    Consequently, the following proposal is offered for consideration:
    Proposal 1: Rel-17 should support IAB enhancements to develop further use cases, topology enhancements, user plane enhancements, and PHY enhancements as described in this contribution.