## Slide 1: Agenda Item: 8.2.2 Source: AT&T Title: NR Beyond 52.6GHz Document for: Discussion/Decision
3GPP TSG RAN Plenary Meeting #85 RP-192111
Newport Beach, USA: September 16-20, 2019

## Slide 2: NR Beyond 52GHz
Currently bands beyond FR2 have been identified for various 5G use cases
Based on licensing rules, power levels and uses cases we propose to split the beyond 52GHz work into two separate item:
FR4: 57-71 GHz band
FR5: 71-114 GHz band
The eco system and component maturity/availability in FR4 is far more mature so it should be prioritized in terms of the work in 3GPP over FR5
Unlicensed Band
Licensed Band
Passive ESS Band
52.6
114
57
71
76
81
86
92
95
100
102
108.2
111.8
Current Beyond 52GHz Landscape in US

## Slide 3: Key Design Considerations
System BW Requirement:
Target CC bandwidth up to 3GHz (still fits the RAN1/2 design by scaling up SCS to 960). A lower value is also acceptable as along as >= 1GHz is addressed
System Gain (max coupling loss):
Target same system gain for all channels as FR2 assuming same occupied BW.
Antenna Array:
Much larger antenna aperture (relative to wavelength) than FR2. Typically up to 1024 antenna elements.
Due to HW limitations we might need to consider multi-aperture antennas and multi-RF to one baseband design.
Standalone System:
Should support standalone operation which in this case means supporting a >52GHz system w/o any FR1/FR2 components for use cases where it makes sense.

## Slide 4: Metric for Waveform Selection
Spectral Efficiency
Power Efficiency
Both spectral efficiency and power efficiency are key in these bands. But unlike FR1 and FR2 these bands tend to be very noise limited due to very large system BW (high noise floor).
Overall system performance can be limited by the total power instead of the total spectrum. So we need to take into consideration a careful tradeoff between designing for spectral efficiency vs designing for power efficiency.
Hardware Impact/Complexity
HW impact can be significant and can depend on various aspects such as waveform design, multi-access design etc. In particular the following HW complexities need to be cosndered:
    ADC and DAC bandwidth
    PA and various RF component design and requirements
    Phased array design
Use Case Requirements

## Slide 5: Beyond 52GHz Waveform Candidates
Currently 2 waveforms have been studied extensively in 3GPP up to FR2:
CP-OFDM (for DL and UL)
SC-FDM (for UL)
Our preference is to limit the waveform for beyond 52.6GHz to some or other variant of these two. That way many of the channel and RS design can be utilized from the current Rel 16 design from FR1 and FR2
Make the necessary changes in the waveform, PHY and higher layers as needed.
Candidate Waveforms:
Symbol Map
Symbol Map
S/P
S/P
iFFT
P/S
CP
RE MuX
D/A
UE1
UE2
CP-OFDM
Symbol Map
Symbol Map
S/P
S/P
P/S
CP
MuX
D/A
UE2
UE1
SC-FDM (SC-FDE)

## Slide 6: Beyond 52GHz Waveform Design
Key Consideration for Evaluation:
Numerology choices (240KHz, 480KHz, 960KHz)
PA Model
Phase Noise Model
Power Consumption Model (RF, ADC/DAC)
Multi CC PAPR Reduction Technique
GaAs PA Model
CMOS PA Model
60GHz
60GHz
Phase Noise Model
Need PA models @ 90GHz
Need PN models @ 90GHz
What about memory based model
Source IEEE 802.1- 09/1213r1

## Slide 7: EVM Analysis for CP-OFDM and SC-FDE
EVM is a measure of the signal quality and comes from multiple sources:
    PA Non Linearity
    Other RF Impairments (e.g. IQ Modulator Impairments, Phase Noise etc)
QPSK
16QAM
64QAM
QPSK
16QAM
64QAM

## Slide 8: Power Back Off for GaAs and CMOS PA
In order to keep the EVM within the 3GPP Specification (17.5% for QPSK, 12.5% for 16QAM and 8% for 64QAM) the PA needs to operate in the linear range i.e. power backoff.
4dB Backoff
4dB Backoff
CP-OFDM Requires 4-5 dB more PA power backoff to achieve the same EVM as SC-FDE

## Slide 9: Impact of Power Back-off on Coverage
Power back-off directly leads to loss in coverage. For a giver target cell edge spectral efficiency SC-FDE has 4dB of coverage advantage:
Normalized Coupling Loss
0
-1
Basic EVM Analysis seems to indicate a significant advantage for SCE-FDE in terms of achievable power for both GaAS and CMOS based PA
Need to extend the study to account for phase noise, especially focusing on the PTRS overhead required to mitigate the phase noise in such high frequency bands.
Besides waveform we also need to study the numerology and understand the two opposing tradeoff: Higher numerology more roust for phase noise, however for channel with finite delay spread higher numerology is less robust because of potential ISI

## Slide 10: Summary
Choice of a waveform for beyond 52GHz is critical as it needs to carefully consider various factors such as use case requirements, RF and HW impact, specifications impact. Therefore this decision should not be rushed at least for FR5 (i.e. the licensed bands)
Evaluation metric for a waveform should also consider RF component imperfections and should include end to end metric such as throughput, power besides just signal quality such as EVM, OOBE, and PAPR.