## Slide 1: Agenda Item: 8.2.3 Source: AT&T Title: Key Considerations for MIMO Enhancements in Rel. 17 Document for: Discussion/Decision
3GPP TSG RAN Plenary Meeting #85 RP-192112
Newport Beach, USA: September 16-20, 2019

## Slide 2: MIMO Enhancement
Multi-Beam and Multi-TRP/Panel Enhancements
    Leftovers from Rel. 16
    Optimizations for FR2
Reciprocity and Feedback Enhancements
    Reciprocity across separate carriers e.g. FDD (DL and UL on separate center frequency)
    New reference signal and feedback design for overhead reduction in FDD
    UE-assisted calibration for FDD-based reciprocity
Non Linear Precoding
    More spectrally efficient than linear precoding but needs high fidelity feedback and suffers from higher computation complexity
    Low complexity non linear precoding
    CQI estimation for non-linear receivers e.g. DMRS based CQI
RP-192112

## Slide 3: Multi TRP Enhancements
Multi TRP transmission is a key feature for improving robustness and reliability of NR based networks particularly in FR2. Multiple use cases such as URLLC, V2X, NR-U still require enhancements in Rel. 17
Enhancements to URLLC based single DCI solutions for all the downlink and uplink channels
Enhancements on multi-TRP/multi-Panel operation in FR2
CP
CP
CP
CP
CP
CP
CP
CP
Synchronous
Asynchronous
TRP 1
TRP 2
TRP 1
TRP 2
Overlapped
PRB allocation
Non-overlapped
PRB allocation
TRP 1
TRP 2
Single FFT Window
Joint Demodulation
Ideal Backhaul with joint scheduling
Joint or independent CSI
Single FFT Window
Joint Demodulation
Ideal Backhaul with independent scheduling
Joint or independent CSI
Dual FFT Window
Independent Demodulation (SIC)
Non Ideal Backhaul with semi-static resource
Partitioning
Independent CSI
Dual FFT Window
Independent Demodulation (SIC)
Non Ideal Backhaul with no coordination
(UE handles the layer partitioning)
Independent CSI
RP-192112

## Slide 4: Multi-Beam/Panel Enhancements
Simultaneous multi-panel transmission for IAB
    SDM: Simultaneously Tx or Rx on backhaul and access links
    Multi-Panel Tx/Rx: Simultaneously Tx/Rx on backhaul
    and access links (UEs to remain half-duplex)
    Multi-panel enhancements leads to a reduction
    in latency and more efficient frame structure for
    IAB nodes
SDM
Multi-panel Tx/Rx
SDM
Multi-Panel Tx/Rx
Multi Beam/Panel Enhancements to improve reliability and robustness and reduce the overhead of the beam management procedure in NR are still required in Rel. 17. Multiple use cases such as IAB, URLLC, and V2X could benefit from multi-panel improvements, beyond the scope of Rel. 16.
Multi-beam enhancements for robustness and overhead reduction
Panel selection and multi-panel transmission enhancements
RP-192112

## Slide 5: FDD MIMO Performance Enhancements
Unlike TDD, exploiting reciprocity in FDD can be challenging depending on the separation between the UL and DL carriers, and over the air calibration limitations
Commonality between the UL and DL channels in FDD can be conducive to FDD reciprocity techniques
Invariance and sparsity in the delay-Doppler domain used to exploit reciprocity in FDD
Mean reciprocity up to 3.5 dB for FDD
DL
UL
1.9GHz
280MHz
SFFT
ISFFT
RP-192112

## Slide 6
FDD MIMO Performance Enhancements
Current LTE/NR MIMO feedback considers the angle domain as “long term” component thus designing the DFT beams to trace angles (DoA, AoA, ZoA, ZoD)
Explore the power-delay and power-Doppler profiles to track long term and frequency domain changing trends
Extract reciprocity or partial reciprocity (channel covariance) based on delay-Doppler plane invariance
UE-assisted over the air calibration for FDD
gNB
UE
Channel
Calib/Feedback Container
Unlike TDD Reciprocity, FDD Reciprocity requires UE assistance for calibration
RP-192112

## Slide 7
FDD MIMO Performance Enhancements
Feedback enhancements based on exploring the channel variations over time (Doppler) and frequency (delay) are beneficial for feedback overhead reduction, especially in high mobility scenarios
CSI-RS design in the delay Doppler domain: CSI-RS may be overlaid with data REs in the time-frequency domain
Feedback overhead reduction through adaptive feedback and grid subsampling in the delay-Doppler domain
SFFT
ISFFT
Time domain
Frequency domain
Doppler domain
Delay domain
Time frequency grid
Delay Doppler grid
RP-192112

## Slide 8: Low Complexity Non Linear Precoding
Tomlinson Harashima Precoding (THP) significantly outperforms linear precoding with high fidelity feedback, it suffers however from high complexity. The main complexity for THP is due to large matrix manipulations. The size of the matrix is proportional to the number of antennas.
Explore ways to reduce to the complexity of THP while preserving near optimal performance.
Split the MIMO precoding in Rel 17 into two different stages
CQI estimation for non-linear receivers (e.g. DMRS based CQI estimation)
8
Low complexity THP done on P1. I.e. non linear precoding within a CSI-RS beam
P2 stage is traditional CSI-RS beamforming. Reciprocity based
RP-192112