## Slide 1: Motivation of power saving in Rel-17
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #85 RP-192150
Newport Beach, USA, September 16th -20th , 2019

## Slide 2: Vision of 5G
5G is expected to change every aspects of modern society
  Smart city, education, health, industry, transportation, environment, entertainment, finance, agricultures…
Agriculture
Health
Education
Transportation
Finance
Environment
Wearable devices
Home
AR
VR
Entertainment
Cloud
Mobile device
Industry

## Slide 3: NR Evolution to Rel-17 and Beyond
User-oriented system evolution –
  Better user experience is one important aspects in marketing NR and further development
  NR power consumption is more than double of that in LTE
    NR PDCCH monitoring in CONNECTED mode is more than double of that in LTE
    Initial access power is more than double of that in LTE
  Power consumption is high in EN-DC due to individual configuration of DRX for LTE and NR
Green project – reduce power consumptions to protect the earth
Rel-16 power Saving study and works provide the framework for UE power saving for eMBB
  Continue power consumption reduction at UE and gNB
Power savings for other Rel-17 SIs/WIs
Coordination among power saving for some Rel-17 features
  Rel-17 NR Light
  Rel-17 eV2X
  Rel-17 Positioning enhancement
  Rel-17 AR/VR
  Rel-17 NB-IoT/eMTC enhancement
  Rel-17 Broadcast

## Slide 4: UE Power Saving Study in Rel-16
Rel-16 Study on UE power saving gains had been shown in multiple dimensions
  UE adaptation to the DRX operations in RRC_CONNECTED mode
    Power saving signal/channel in triggering UE adaptation
    Dynamic DRX configuration
  Reduce PDCCH monitoring
    PDCCH skipping
    Switching PDCCH monitoring periodicity
    Blind decoding reduction
  UE adaptation to the BWP/SCell operation
  UE adaptation to the maximum number of MIMO layers/ number of antenna
  UE assistance information
  RRM measurements reduction
    Relaxing in time domain
    Relaxing in intra and inter-frequency measurements
    Measurements with Additional RS
UE assistance for fast transition from RRC_CONNECTED to RRC_IDLE/RRC_Inactive

## Slide 5: UE Power Saving Work in Rel-16
Specify power saving techniques with PDCCH-based power saving signal/channel triggering UE adaptation in RRC_CONNECTED mode [RAN1, RAN2, RAN4]
  Specify procedures triggering a MAC entity to “wake up” to monitor PDCCH at reception of the PDCCH-based power saving signal/channel for the next occurrence(s) of the drx-onDurationTimer [RAN2, RAN1]
    NOTE: Any change of PDCCH channel coding and payload interleaver is not in the scope
  Specify the procedure of cross-slot scheduling power saving techniques [RAN1, RAN4]
    NOTE: The procedure is in addition to Rel-15 cross-slot scheduling procedure
Specify the power saving techniques of UE adaptation to the maximum number of MIMO layers [RAN1, RAN2, RAN4]
  Specify configuration of a different MIMO layer configuration of the initial/default BWP compared with other BWPs of a Serving Cell. [RAN2, RAN4]
    Discuss whether to also extend this to define per-BWP MIMO layer configuration [RAN1, RAN2]
  Evaluate if switching and interruption times for UE dynamic adaptation to the maximum number of MIMO layers are needed and which case assuming a relationship between the number of RF ports and the MIMO layer configuration [RAN4]
    NOTE: Switching on/off the RF is part of the evaluation
Specify a mechanism for a UE to indicate its preference of transitioning out of RRC_CONNECTED state. [RAN2]
Specify, if agreed, the mechanism to provide UE assistance information [RAN2, RAN1]:
Study and select among the following UE assistance information for RAN2 by RAN#85:
power preferred information (baseline LTE PPI in a well-defined manner) and UE's preference on C-DRX, BWP and SCell configuration [RAN2].
  NOTE: additional UE assistance information for RAN1-specific power saving techniques to indicate what setting of parameters related to this Work Item will lead to power savings for the UE can be included if agreed in RAN1.
Specify network-configured mechanism to relax intra and inter-frequency RRM measurement for neighbour cells for RRC_IDLE/INACTIVE with minimal mobility performance impacts [RAN2, RAN4]
  Specify RRM measurement relaxation by allowing measurements with longer intervals, and/or by reducing the number of cells/carriers to be measured [RAN4, RAN2]
  Define triggering criteria for the UE to move between relaxed and normal RRM measurements, that considers at least if UE is not at cell edge, or if UE is stationary or with low mobility [RAN2, RAN4].
    Evaluate and specify requirements (if needed) depending on RAN2 criteria [ RAN4]
    NOTE: No new measurement quantities should be introduced

## Slide 6: Revolution to “Green”
Power consumption reduction for through antenna adaptation
    Dynamic antenna adaptation based on the traffic - reduced the number of Tx/Rx antenna
      Low system load
      Time of day
Multi-RAT UE power saving
  Power Saving signal/channel to indicate the wakeup of selected RAT
    Preparation period – for channel tracking and triggering RS transmission
    Measurements
CONNECTED/IDLE mode power saving
PDCCH monitoring reduction
  PDCCH skipping
  Reduce No. of blind decoding
gNB: 4Tx/Rx for high data rate
UE: 4Tx/Rx for high data rate
gN: 2Tx/Rx for no traffic
UE: 2Tx/Rx for
PDCCH monitoring
LTE: DRX ON
NR: DRX ON
Low power
Power Saving signal triggering
Preparation
period
Preparation
period

## Slide 7: Rel-17 UE and Network Power Saving WI
Extending the UE power saving frameworks to support UE power saving of features in Rel-17 and beyond, such as NR Light, Broadcast/Multi-cast, V2P, Positioning, AR/VR
Power saving signal/channel triggering UE adaptation to the power saving techniques in multi-RAT network [RAN1]
  Power saving signal/channel for triggering UE adaptation in both CONNECTED and IDLE/Inactive
    Study the low power consumption power saving signal
    Study and specify the interaction to Rel-16 PDCCH-based power saving signal/channel
    Specify the power saving signal triggering UE adaptation to DRX operation in multi-RAT operation, such as EN-DC, NE-DC, NR-DC, NR-CA
  Study and specify the power saving signal triggering preparation period in multi-RAT operation
    Configuration additional RS in assisting UE measurements, such as RRM and CSI measurements
    Enhancements of CSI feedbacks
Multi-RAT UE PDCCH monitoring reduction
  Power saving signal triggering PDCCH monitoring reduction
    PDCCH skipping
  PDCCH blind decoding reduction techniques
Adaptation of Tx/Rx Antenna adaptation
  UE adaptation to the number of Rx/Tx antenna
  Antenna adaptation based on system load and the day of use