## Slide 1
Discussion on the unpredicted/undefined UE capability from UE specific implementation
CMCC
3GPP TSG RAN Meeting #85 RP-192246
Newport Beach, USA, September 16-20, 2019
Document for: discussion
Agenda Item: 9.8

## Slide 2
Backgrounds
  In the procedure of 5G trial and frequency reframing, several unpredicted/undefined UE capabilities that resulted from UE specific implementation are identified, which will consequently impose some unpredicted burden or restriction on the network side or operator’s deployment, e.g.,
    Case 1: Report defined capability but only partial part of the capability is supported from UE implementation
    Case 2: Selective implementation of some features of a future set in some stage although the whole future set is mandatory capability
    Case 3: Different interpretations from different companies on the same description or definition of the procedure
    Case …...
  Such kind capabilities are forcing our network to take special mechanisms to accommodate their drawbacks, which is unfair to other compliant UEs

## Slide 3
Case 1
    Case 1: Report defined capability but only partial part of the capability is supported from UE implementation
      In LTE, some UE report its support B41, however, in fact, they only support partial part of the whole band, e.g., it may only supports 2575-2635MHz while the whole band spans 2496-2690MHz, which lead to fail in the measurement and hence unpredicted latency when they are configured with a measurement objective that is not supported. The network can not avoid the cases unless prohibit all UE claiming capable of B41 from measuring the frequency out of 2575-2635MHz

## Slide 4
Case 2
    Case 2: Selective implementation of some features of a feature set in some stage although the whole future set is mandatory capability
      In NR, some UE functionalities are categorized into one capability, however, some UE only implemented partial functionalities of the capability while no claiming its missed functionalities, which is even worse when the capability is mandatory one. The network has to be forced to preclude some operation or scheduling behaviors to guarantee some kind of UE still alive in the network.

## Slide 5
Case 3
    Case 3: Different interpretations from different companies on the same description/definition of the procedure
      In LTE, some UE implementation think that closed-loop enabled or not only impacts the PUSCH behavior. So for SRS transmit in open-loop antenna selection, even it is not implicitly specified, some UE implementation follows the SRS transmit rule defined in closed-loop since this rule is quite reasonable which will not only help the network to decide which antenna is good for PUSCH transmission, but also help the network to exploit the reciprocity for PDSCH transmission, however, unfortunately, PUSCH transmit rule in open-loop is dependent only on UE’s perceived path-loss, and when PUSCH and SRS transmit is not coordinated appropriately in the implementation, UE will crash if closed-loop antenna selection is not enabled

## Slide 6
Proposals
    To avoid forcing the network to take uniform solution for all UEs by introducing standard mechanism/solutions to allow(provide opportunity to ) the network to take additional handle for UEs with unpredicted/undefined capability or with unexpected implementation
    Introduce RAN aware implementation specific version based on information composed of at least UE/chipset version and/or launch time
      Such version information should not necessarily be reported by default, and it can be reported based on UE manufactory triggering after some unexpected behavior identified