## Slide 1: Key points on NR sidelink WID
Huawei, HiSilicon
3GPP TSG RAN Meeting #86
Sitges, Spain, December 9th – 12th, 2019
RP-192790

## Slide 2
Proposal 2: Support Rel-17 SI relaying SI objectives include SL-CSI report to gNB
Justification
Observation 1: With limited bandwidth in FR1, it is challenging for sidelink to meet high data rate requirement up to 1 Gbps or more as defined in many use cases in 5G services.
Proposal 1: Support Rel-17 WI objectives include sidelink FR2 enhancements, with followings:
Beam management (with limited number of beams)
Multi-panel operation
Assistance from FR1 sidelink
Use Cases | Characteristic parameter (KPI) |  | 
 | Max Allowed End-to-end latency | Service bit rate: user-experienced data rate | Reliability
Audio-visual interaction (a human being interacting with the environment or people, or controlling a UE, and relying on audio-visual feedback) | 7-15ms | [1] Gbps | 
Gaming or Interactive Data Exchanging NOTE 3: Communication includes direct wireless links (UE to UE). | 10ms | 0.1-[1] Gbps supporting visual content (e.g. VR based or high definition video) with 4K, 8K resolution and up to120fps content. | 99.99%
AR/VR performance requirements [TS 22.261]
Communication scenario description |  | Max end-to-end latency (ms) | Reliability (%) | Data rate (Mbps) | Min required communication range (meters)
Scenario | Degree |  |  |  | 
Sensor information sharing between UEs supporting V2X application | Higher degree of automation | 10 | 99.99 | 1000 | 50
Extended sensor requirements [TS 22.186]
Sidelink FR2 in Rel-17 WI should focus on commercial use cases, and can be potentially reused in V2X use cases. In order to support sidelink in FR2, multi-panel operation with panel-specific sidelink transmission/reception is beneficial for higher data rate and coverage. For instance, in AR/VR gaming, one HMD can have multiple panels (e.g. AIPs) towards multiple directions in order to maintaining high reliable link to cloud/edge server or application devices whilst moving body and head.
For short distance sidelink communication, beam management is beneficial for 360° coverage and power consumption reduction, with limited number of relatively wider beams. Moreover, FR2 sidelink can be assisted by FR1 sidelink, e.g., on the aspects of initial link establishment, beam failure recovery, etc. If TU are a concern for FR2 work, it can be prioritized over e.g. sidelink multicarrier operation in Rel-17
 | Characteristic parameter (KPI) |  |  | Influence quantity
 | Max Allowed End-to-end latency | Service bit rate: user-experienced data rate | Reliability | UE Speed
Consume VR content via tethered VR headset | [5 -10] ms (note 5) | 0.1-[10] Gbit/s (note 5) | [99,99%] | Stationary or Pedestrian
Additional AR/VR performance requirements [SA1 CR 0405]
SL CSI report to gNB has also been identified with increased data rate, enhanced reliability, reduced latency thanks to improved network control and scheduling abilities. It also benefits to discovery for relaying functionality