## Slide 1: Motivation for new WI on Introduction of NB-IoT in AAS specification
ZTE, Ericsson
3GPP TSG RAN Meeting #86
Sitges, Spain, Dec 9-12, 2019
Agenda: 9.1.4
RP-193157

## Slide 2: Background
During the R14, NB-IoT have been introduced into MSR spec including in-band/guard band operation and standalone operation.
  NB-IoT in-band/guard band operation introduced into CS2, CS3, CS5,CS7;
  NB-IoT standalone operation introduced into CS8/9/10/11/12/13/14/15.
During the R15, CS17 including NR, E-UTRA, standalone NB-IoT have been introduced into MSR spec .
During the R16, NB-IoT operations in NR in-band/guard band into MSR spec are still under discussion.

## Slide 3: Motivation of new WI
MSR BS will support E-UTRA+NR+NB-IoT operation (e.g.CS17 defined in 37.141) considering refarming GSM/UTRA/E-URTA/NB-IoT spectrum.
From the implementation perspective, NR BS will basically utilize the AAS architecture which means MSR BS including NR configuration will also utilize the AAS architecture.
In addition, many of the existing NR/E-UTRA operating bands such as bands 3/8 designed to NB-IoT are suitable for AAS based on MSR BS deployment. Support for band 42/43 for NB-IoT has recently been introduced
However, the current AAS specification does not include support for NB-IoT,
  i.e., there are no core requirements and conformance testing specified yet in current AAS spec, which cannot meet the desirable market demand on the AAS based MSR BS.
If NB-IoT is introduced into AAS spec, NB-IoT configured within the legacy MSR BS could migrate smoothly to new MSR BS configured with both NR RAT and standalone NB-IoT. This will also speed up the 5G MSR BS deployment.
It would be undesirable for the RAN4 specifications to preclude such scenarios

## Slide 4: Proposal
Introduce NB-IoT, including inband/guardband and standalone modes, into the AAS specification such that the specification provides equivalent performance and protection as the conducted specifications.
Update the core specification 37.105 to include NB-IoT operation
Update the conformance specification 37.145-1/2 to include new CS(s) and associated test configurations
Update the test requirements in the conformance specification 37.145-1/2 as appropriate

## Slide 5: Expected workload
The aim of the WI is to migrate existing NB-IoT requirements supported for E-UTRA in MSR to AAS
Existing procedures for translating conducted requirements to OTA can be adopted:
  ”Scaling” from conducted to TRP emissions requirements
  Direct translation of directional TX requirements
  Translation of RX requirements by means of ”sensitivity RoAoA”
Existing test procedures and MU expected to be re-used for all requirements
Workload of 0.25 TU in 2Q foreseen