## Slide 1: Handling of power class in Rel-15 OPPO, Xiaomi
3GPP TSG-RAN Meetings #87 RP-200211
RAN plenary reflector 16th March.– 19th March. 2020

## Slide 2: Rel-15 power class report
Power class 2 and Power class 3 were defined in RAN4 Rel-15 spec.
For NR SA, only one power class per band is reported, without distinguishing single antenna port and UL MIMO.
In reality, the power capability might be different for these two modes, e.g. PC2 with UL MIMO and PC3 with single antenna port.

## Slide 3: Issues caused by Rel-15 power class report
How to interpret the UE reported power class and which power class requirements these UEs shall comply with these two modes needs to be clarified since it has large impact to UE design, RAN5 test case definition and GCF certification.
  Now, on the market there are different PC2 UE implementations, typically many UEs have implemented with two PC3 capable PAs to achieve PC2 under UL MIMO, i.e. power capability will be different for single antenna port and UL MIMO.
    This kind of UE implementation was agreed in RAN4#86 meeting (Feb 2018) [1]
    Some of these UEs support Tx diversity while others don’t, since Tx diversity is transparent to RAN1/2 spec and not been specified in RAN4 spec, purely up to UE implementation.
    UEs without Tx diversity can only transmit with one antenna, i.e. can only achieve PC3 under single antenna port.
  Currently, Rel-15 test cases in RAN5 are designed with 1 antenna connector tested in basic test cases, and 2 antenna connectors tested in UL MIMO test cases.
  After RAN5 released Rel-15 test cases, many test cases were already validated with test platforms in certification organizations like GCF and widely adopted on the market.
    Changing the test cases from 1 antenna connector to 2 antenna connectors in basic tests will lead to revalidate large number of test cases and test platforms which seems to be not preferred by testing industry.

## Slide 4: Different Rel-15 power class interpretations
In RAN4#94e meeting, clarification of UE reported power class has been discussed but views are divergent. Finally no consensus has been reached [2].
  Option 1: Power class baseline is UL MIMO, and exception is allowed for UE configured to single antenna port. Either PC2 or PC3 MOP requirements could apply for a PC2 UE supporting UL MIMO.
  Option 2: Power class baseline is single antenna port mode, and exception is allowed for UE configured to UL MIMO. Either PC2 or PC3 UL MIMO MOP requirements could apply for a PC3 UE.
  Option 3: Power class should be the same for both UL MIMO or single antenna port mode.
  Option 4: No clarification is needed to current spec
  Options 5: Power class is the same for both UL MIMO or single antenna port mode. Exception is allowed for some UE implementation and RAN5 test cases may consider this kind of exception
In RAN5#86e meeting, how to accommodate different UE implementations in the market like 23+23, 23+26, 26+26 PA configurations also had been discussed, however, it was postponed due to pending on RAN4 power class interpretation conclusion.
  One solution similar to option 1 above was provided in RAN5 that testing UL MIMO with UE reported power class, and test single antenna port mode with UE declared power capability at single antenna connector [3].

## Slide 5: Proposed solutions
To cater for different parties in the industry, the following solutions are proposed:
  Keep Rel-15 RAN4 and RAN5 power class status unchanged.
    Re-acknowledge the agreement RAN4 made two yeas ago, i.e. UE implement with 23+23 capable PAs will report PC2 to the network.
    Acknowledge the single antenna port test case in RAN5 is tested with one antenna connector, i.e. no Tx diversity is considered.
    The requirements under single antenna port mode can be tested based on UE declared power capability.
      Detailed test case design can be further discussed in RAN5.
  Further clarify the power class capability in Rel-16 by either of the following approaches:
    Introduce new power class capability in Rel-16 to distinguish single antenna port power capability and UL MIMO power capability.
    No new power class will be introduced in Rel-16, and keep same power class for single antenna port and UL MIMO.

## Slide 6: Reference
[1] R4-1803259, “Proposal on NR HPUE definition for PC2”, CMCC, Huawei, HiSilicon, OPPO, vivo, Xiaomi, ZTE, CATT, Intel, Qorvo, Skyworks, broadcom
[2] R4-2002738, “WF on UL MIMO PC2”, Huawei, HiSilicon, vivo, OPPO
[3] R5-201196r1, “Cleaning up of power class 2 test cases in FR1”, Huawei, HiSilicon, CMCC, VIVO, CAICT, China Unicom, Oppo