## Slide 1: On mandatory features without capability signalling and number of antenna ports
ORANGE, Telecom Italia, BT, Deutsche Telekom, Telia Company
3GPP TSG RAN#87e 16 – 19 March 2020 E-meeting | TDoc RP-200311 Agenda Item 9.9

## Slide 2: Background
During RAN1#100 e-meeting, an email discussion on the reply LS to R1-2000164 was particularly revealing on the issue we may face in the future with features which are “mandatory without capability signalling”.
The topic of the LS addressed specifically the default number of antenna ports which UEs have to support for MIMO codebook type I (Single Panel)
There is a more general concern about “the introduction of signalling whose flexibility can override mandatory features without capability signalling”.

## Slide 3: Issue 1: mandatory features without capability signalling
Currently such features are only captured as “agreements” in TR, not in TS
Nokia has made a proposal (R1-1903151 - On features mandatory without capability, Nokia, Nokia Shanghai Bell) to copy all the mandatory features within TR38.822 into the respective sections of the other RAN2/RAN1 Technical Specifications (e.g., TS38.306, TS 38.214…)
The proponents are supportive of Nokia’s proposal

## Slide 4: Issue 2: number of antenna ports
RAN1 response (R1-2001307) to the LS from RAN2 was:
  “RAN1 was not able to agree on what default values the gNB should assume in absence of this IE. RAN1’s understanding is that the UE is expected to provide this IE with its capability signalling.” The IE allows any values among {p2, p4, p8, p12, p16, p24, p32} which goes below the mandatory values agreed in RAN1 for FR1.
However, the mandatory number of antenna ports is captured in the MIMO feature 2-32 “Basic CSI feedback” of TR38.822, as follows:
  “2Tx codebook for FR1 and FR2”
  “4Tx codebook for FR1”
  “8Tx codebook for FR1 when configured as wideband CSI report”
that is to say: in Rel. 15 and Rel. 16, RAN1 agreed that the minimum mandatory value for FR1 is:
  4 for Narrow Band reporting
  8 for wideband reporting.
The current agreement is very risky. Without minimum values, the UE may report values below those agreed as mandatory.

## Slide 5: Issue 2: number of antenna ports
Why a minimum mandatory value is important?
  The minimum mandatory values were carefully selected in order to ensure that NR has a better, or at least similar, coverage and capacity than LTE
    The number of antenna ports the UE can measure is directly related to the beam-forming gain of codebook type I
  If the UEs does not support a common value then the network has to configure several CSI-RS resources, i.e., per group of UEs supporting the same number of antenna ports. It means higher CSI-RS overhead and higher complexity at the network side

## Slide 6: Proposals
Proposal 1: On mandatory features without capability signalling
  The UE features which are mandatory without capability signalling shall be captured in TS 36.306 and 38.306
  The UE values for features defined as mandatory without capability signalling cannot be overridden with any lower value than those agreed as mandatory.
Proposal 2: On the number of antenna ports
  Agree on the mandatory & default values for the following parameters for type I single panel codebook which the UE is mandated to report in supportedCSI-RS-ResourceList, as follows:
    maxNumberTxPortsPerResource
      “2Tx codebook for FR1 and FR2”
      “4Tx codebook for FR1”
      “8Tx codebook for FR1 when configured as wideband CSI report”