## Slide 1: Motivation for RAN SI : Study on sidelink positioning
LG Electronics
3GPP TSG RAN Meeting #88e RP-200858
Electronic Meeting, June 29 - July 3, 2020
Agenda item: 9.1

## Slide 2: Interests on SL positioning inside 3GPP
There were significant number of companies’ supports on sidelink positioning for Rel.17 NR positioning enhancement [1].
  RAT-dependent and RAT-independent sidelink positioning techniques
    RAT-dependent: Positioning reference signals transmitted in sidelink
    RAT-independent: Exchange of positioning information such as those related to GNSS or sensor via sidelink
  UE-based and network-based sidelink positioning techniques
    UE-based: UE calculates the position based on the sidelink operation.
    Network-based: Network calculates the position using UE report on sidelink.
Positioning accuracy requirements for V2X application developed in SA1 [2]
  Relative lateral position accuracy of 0.1 m between UEs
  Relative longitudinal position accuracy of less than 0.5 m for UEs
Though not included in the final scope of Rel.17 positioning SI [3], continuing investigations on sidelink positioning in RAN would be needed to build a common understanding on how to progress in this topic in 3GPP.
  A RAN study activity to look into use cases/scenarios/requirements for sidelink positioning can be a reasonable option.

## Slide 3: Interests on SL positioning outside 3GPP
V2X industry has indicated the necessity of 3GPP evolution for sidelink positioning.
  “5GAA is of the opinion that precise positioning is one of the key component of cellular V2X technologies and sidelink positioning is an essential enabler in addition to other positioning technologies. […] 5GAA suggest starting the study soon in order to build a good basis for the standardization of the sidelink positioning and to show that cellular V2X evolution path includes sidelink positioning in addition to other positioning technologies.” (5GAA LS in [4])
  “However, because V2X using 3GPP transport-layer technology, has been considered one of the most successful verticals so far, AA TC recommends, from an automotive industry perspective, that 3GPP RAN should start a Feasibility Study, looking into the core value of side-link (SL) positioning as a supplementary means for improving the operational cost and performance of the advanced V2X services coming soon.” (SAE LS in [5])
Positioning technique is under development in IEEE 802.11bd as a whole technical package for V2X communication [6]
  “This section describes the functional blocks that support positioning in conjunction with V2X communications. 11bd supports round-trip-time (RTT) ranging for 10 MHz and 20 MHz bandwidth PPDUs.”

## Slide 4: Examples of sidelink positioning use cases
Basic and enhanced V2X services including advanced driving and VRU protection
Public safety when no other positioning solutions are available
Positioning for automated guided vehicle (AGV) and drone
<Advanced driving>
<VRU protection>
<AGV positioning>
<Drone positioning>
<Positioning for lifesaving>

## Slide 5: Necessity of sidelink positioning
Complementary solution to the conventional Uu positioning
  Uu positioning is not available out of the network coverage
    SL infrastructure (e.g., RSU) can be expected out of the network coverage.
  In case where GNSS is not reachable (e.g., tunnel, underground parking lot, city canyon, etc.), sidelink positioning can provide the positioning functionality
  In network coverage, sidelink positioning can improve Uu positioning accuracy by providing additional information.
Relative position
  Easy to obtain via sidelink positioning
    Simpler & faster than calculating relative position after acquiring absolute position
  Relative position is sufficient in many use cases.
    E.g., VRU protection, UE discovery for public safety, etc.
Competitiveness of 3GPP V2X solution
  As a leading technology in V2X, sidelink positioning together with sidelink communication needs to be provided as a total C-V2X solution package.
5

## Slide 6: Study scope consideration
Considering all the needs, benefits and interests of industries so far, we can start a RAN SI.
  The study outcome can be used as the solid basis during the discussion for potential future WG level SI/WI on SL positioning.
  It can give a clear message on the 3GPP V2X/sidelink technology evolution.
Study scope may include:
  Identify the existing use cases and requirements relevant to the sidelink positioning considering, e.g., in V2X, public safety, commercial services
  Identify potential operation scenarios and design considerations considering, e.g.,
    Network coverage
    Frequency band
    UE type
    RAT-dependent and RAT-independent positioning
    Mobile-based and mobile-assisted SL positioning
It is proposed to approve SI for sidelink positioning at RAN#88
  SID is proposed in [7].

## Slide 7: References
[1] RP-192412, “Email summary on NR positioning,” Qualcomm Incorporated (Moderator).
[2] 3GPP TS 22.186 Service requirements for enhanced V2X scenarios
[3] RP-193237, “New SID on NR Positioning Enhancements,” Qualcomm Incorporated.
[4] RP-200546, “LS on the 3GPP work on the NR sidelink,” 5GAA WG4
[5] RP-200567, “LS on Sidelink Positioning for advanced V2X applications,” SAE Advanced
Application Technical Committee.
[6] IEEE 802.11-19/0497r5 802.11bd Specification Framework Document
[7] RP-200859, “New SI proposal: Study on sidelink positioning,” LG Electronics.