## Slide 1: Rel-16 Lower NR UE Capabilities
MediaTek Inc., CHTTL, Deutsche Telekom, Orange, Telia Company, TIM, Futurewei, Spreadtrum, Huawei, HiSilicon
3GPP TSG RAN#88E RP-200936
June 29th – July 3rd, 2020 Agenda Item 9.8

## Slide 2: Background
RAN#86 – RP-192411 (not agreed)
  For FR1 allow UEs to support BW of 50MHz for bands mandating 100MHz; and
  For FR1 allow UEs to support 2Rx for all NR bands mandating 4Rx
  A number of companies expressed focusing on a) but proponents stuck to a)+b)
RAN#86 – Proposed way forward 1 – RP-193207 (not agreed)
  For FR1 allow UEs to support BW of 50MHz for bands mandating 100MHz; and
  For FR1 n40*, n41, n48* and n90 allow UEs to support 2Rx 4RX remains mandatory for n7, n38, n77, n78, n79
  A number of companies expressed focusing on a) but proponents stuck to a)+b)
RAN#86 – Proposed way forward 2 – RP-193245 (not agreed)
  For FR1 allow UEs to support BW of 50MHz for bands mandating 100MHz; and
  For FR1 n41 allow UEs to support 2Rx for NR bands mandating 4Rx 4RX remains mandatory for n7, n38, n77, n78, n79, n90
  A number of companies expressed focusing on a) but proponents stuck to a)+b)
3GPP TSG RAN#88e – RP-200936 – MediaTek Inc., et al.
2/8
  * 38.101-1 §7.2: FR1 bands requiring 4Rx: n7, n38, n41 (n90), n77, n78, n79

## Slide 3: Claimed motivations (RP-192411)
Business value for lower NR UE capabilities in Rel-16 timeframe
Help the timely proliferation of NR into more tiers of devices
  e.g. “non premium” devices, “low end” smartphones & other segments
  “Timely” means ~2021/2022 timeframe
Migrate corresponding subscribers away from LTE spectrum into spectrum where NR is deployed thereby improving operator flexibility in deploying NR into more frequency bands
Do these really hold?
3/8
3GPP TSG RAN#88e – RP-200936 – MediaTek Inc., et al.

## Slide 4: Discussion [1/2] Claimed motivations
4/8
Business value for lower NR UE capabilities in Rel-16 timeframe
  This assertion is very subjective and tied to specific business models
  There is clear operator business value in NOT degrading NR performance where 4Rx is required
Help the timely proliferation of NR into more tiers of devices
  This assertion is dubious and once again tied to specific business models
  NR is proliferating into lower tiers of devices *already* today without requiring NR perf. degradation
Migration to NR spectrum
  This is a by-product of the above
3GPP TSG RAN#88e – RP-200936 – MediaTek Inc., et al.

## Slide 5: Discussion [2/2] Consequences of degrading NR 4Rx to 2Rx
No guarantee of claimed cost reductions
  Regional optimization challenging global economies of scale
  Cost benefits subjective and tied to very specific implementations and business models
Downgrading 5G promise to 4G
  No/limited 5G roaming for 2Rx UEs (operation only in networks allowing such 2Rx UEs)
  Erasing 5G spectral efficiency gains over 4G for high data rates in key mid-band(s)
  Risk of substantial VoNR impact
  Degraded performance without coverage recovery until Rel-17 (ref. SID Coverage Enh.)
Potential competitive disadvantage for operators not having access to the degraded band(s)
Impact on Rel-16 timeline remains a major concern subject to very high RAN4 workload
Clearly no time in Rel-16 Continue discussions in Rel-17
5/8
3GPP TSG RAN#88e – RP-200936 – MediaTek Inc., et al.

## Slide 6: Proposal
No Lower NR UE Capabilities to be introduced in Rel-16
Continue discussions in Rel-17
6/8
3GPP TSG RAN#88e – RP-200936 – MediaTek Inc., et al.

## Slide 7: Appendix

## Slide 8: 4Rx bands incl. bands requiring 4Rx
LTE/NR bands:
  n1, n2, n3, n7, n28, n34, n38, n39, n40, n41, n66, n70, n71
NR bands:
  n48, n77, n78, n79
Bands requiring 4Rx (38.101-1 §7.2)
  n7, n38, n41 (n90), n77, n78, n79
  n40, n48 are not defined as requiring 4Rx
UL/DL (MHz)
8/8
3GPP TSG RAN#88e – RP-200936 – MediaTek Inc., et al.