## Slide 1
Agenda Item: 14
Source: Samsung
Title: On SIB24 issues
Document for: Discussion and Decision
3GPP TSG RAN Meeting #89e
Electronic Meeting, September 14-18, 2020, 2020
RP-201472

## Slide 2: Background
RAN2-111e intensively discussed SIB24 issues
The problem was identified, number of solutions were debated.
RAN2 decided to ask RAN to make the final decision.
In this slide set, we make set of proposals together with the analysis on the issues, with the hope to provide the assistance in RAN making the decision

## Slide 3: Discussion in RAN2
Two problems were identified and discussed during RAN2 111-e
  SIB24 extension problems
    Some legacy UE fails to decode SIB1 if scheduling info for SIB24 is included within SIB1
  SIB24 multiplexing problem
    Some legacy UE fails to decode SystemInformation multiplexing SIB24 and other legacy SIBs together
RAN2 111-e endorsed a set of CRs addressing SIB24 extension problem only. The reason behind that is because SIB24 multiplexing was not widely acknowledged.

## Slide 4: SIB 24 Extension: Problem Description
SIB-Type used in SIB1 was extended since Release 12 as below.
SIB-Type ::= ENUMERATED {
sibType3, sibType4, sibType5, sibType6, sibType7, sibType8, sibType9, sibType10, sibType11, sibType12-v920, sibType13-v920, sibType14-v1130, sibType15-v1130, sibType16-v1130, sibType17-v1250, sibType18-v1250, ...,
sibType19-v1250, sibType20-v1310, sibType21-v1430, sibType24-v1530, sibType25-v1530, sibType26-v1530, sibType26a-v1610, sibType27-v1610, sibType28-v1610, sibType29-v1610}
Upon receiving SIB 1 including new SIB-Type, legacy UEs not understanding the value are supposed to ignore the SIB-Type and to process the other part of SIB 1. However, it is reported some legacy UEs (apparently wrongly implements the specification) ignore the entire SIB 1 which results in considering the cell being barred
The problem is found for SIB 24, but could occur to other New SIBs as well
New SIB-Type
Legacy SIB-Type
LTE base station
SIB 1
Scheduling Info
  SIB-Type = sibType3
  Periodicity = 320 ms
Scheduling Info
  SIB-Type = sibType24
  Periodicity = 640 ms
Wrongly implemented legacy UE ignores entire SIB1
Correctly implemented legacy UE ignores only sibType24

## Slide 5: SIB 24 Extension: Solutions Discussed in RAN2 #111-e
Basically two types of solutions were discussed during RAN2.
  Solution 1: Workaround
    SIB24 is not transmitted
    As a consequence the functionality supported by SIB24 needs to be provided by other means. SIB 24 concerns NR IDLE mobility (for NR SA UE)
    With this workaround, NR SA UE (capable of LTE as well) first makes connection with LTE NW which redirect the UE to NR network
  Solution 2: Spec Amendment
    SIB1 is basically multiple of containers. New container is introduced in SIB 1. Legacy UE does not decode the container. New sib-Types are used only in the new container
    RAN2 endorsed CRs will be submitted for RAN meeting

## Slide 6: SIB 24 Extension: Comparison between Possible Solutions
Solution 1
  Not broadcasting SIB24
  Limitation: SIB19+ linked services/functionalities are blocked
Solution 2
  Change the specification such that SIB 19+ is included in the separate container in SIB 1
  Limitation: Correct implementation takes the burden of update
 | Wrong implementation | Correct implementation | Correct implementation without SIB19+ reception | Correct implementation with SIB19+ reception | Implementation without SIB19+ transmission | Implementation with SIB19+ transmission | Blocked Services
Sol 1: NW workaround | No impact | No impact | No impact | No impact | No impact | Update (RRM) | Table 2
Sol 2: Fixing new UE | No impact | No impact | No impact | Update | No impact | Update | None
<Table 1>
 | Legacy UE (pre-R12 UE) | Rel-12 onward UE | ENB | 
Table 1 provides the comparison between solutions in terms of update requirements and blocked services

## Slide 7: SIB 24 Extension: Implication of Absence of New SIBs
The problem is not only about SIB24, but about all new SIBs introduced after extension.
If LTE network is not allowed to transmit any of new SIB, the functionality linked with the SIB should be provided via other means or the functionality is virtually disabled. SIB24 may be the only SIB whose linked functionality can be worked around.
Table summarizes the functionalities and consequence of absence
SIB-Type | Release | Functionality | Consequence of absence (not transmitting the SIB)
SIB 19 | R12 | Sidelink Discovery | D2D discovery cannot be serviced
SIB 20 | R13 | SC-PTM | SC-PTM cannot be serviced
SIB 21, 26 | R14, R15 | V2X | V2X cannot be serviced
SIB 24 | R15 | NR SA Idle mode mobility | NR SA idle mode mobility is provided via inefficient way
SIB 25 | R15 | Unified Access Control | Architecture Option 5 cannot be deployed
SIB 26a | R16 | NR icon display | NR icon cannot be displayed when UE is in EN-DC coverage
SIB 27 | R16 | NB-IoT frequencies | NB-IOT inter-RAT mobility is not supported
SIB 28 | R16 | NR sidelink | Inter-RAT sidelinke is not supported
SIB 29 | R16 | NR-LTE coexistence | Resource reservation for NR-LTE coexistence is not known to UE
<Table 2>

## Slide 8: SIB 24 multiplexing: Problem Description
During the e-mail discussion, it was reported that SchedulingInformation with which SIB24 and other legacy SIBs are multiplexed together is discarded by some legacy UE. Hence the legacy SIBs there is lost.
Alike SIB24 extension, it is not intended behavior in specification perspective. The source of problem is known as old version ASN.1 decoder.
The problem is found for SIB 24, but could occur to other New SIBs as well.
It was argued whether the problem is real one or only speculated one. It should be confirmed again the problem is existing.
LTE base station
2nd SystemInformation [SIB 4, SIB 24]
Wrongly implemented legacy UE ignores the 2nd SystemInformation
Correctly implemented legacy UE ignores only SIB24 in 2nd SystemInformation
1st SystemInformation [SIB 2, SIB 3]
SIB1
[SchedulingInfo for 1st SI, SchedulingInfo for 2nd SI]

## Slide 9: SIB 24 Multiplexing: Possible Solution and Implication
Solution is straightforward. If legacy SIBs and new SIBs are transmitted in different SystemInformation(s), the problem is gone.
  It can be achieved by specifying a guideline in the specification e.g. with following text added in the CRs for SIB24 extension
The solution may restrict the SystemInformation scheduling flexibility for the network in theory. But the limitation is trivial in the real deployment. See the details in Annex.
If the problem remains unsolved, all the networks currently (or potentially) having the problematic legacy UEs may have to refrain itself from transmitting the new SIBs in their network (or accept the possibility that there could be some misbehaving UEs)
schedulingInfoList
Indicates scheduling information of SI messages. The schedulingInfoList-v12xy (if present) provides additional SIBs mapped into the SI message scheduled via schedulingInfoList (without suffix). If E-UTRAN includes schedulingInfoList-v12xy, it includes the same number of entries, and listed in the same order, as in schedulingInfoList (without suffix). E-UTRAN provides schedulingInfoList-v12xy only if the UEs receiving the corresponding SystemInformation are able to process the comprehended SIBs in the SystemInformation.

## Slide 10: Observations and Suggestions
Observations
  It is an unfortunate event stemmed from the wrong UE implementations deployed long ago.
  Workaround solution has a limitation that it works only for a specific SIB.
  If the problem remains unsolved, NW vendors and operators will be forced to, whenever new SIBs are to be deployed, either handle the problems with proprietary solutions, take the risk of misbehaving UE(s) being in their network, or simply refrain themselves from broadcasting the new SIBs .
  SIB24 extension and SIB24 multiplexing are different problems in nature. However, they cause similar consequences and deserve the solutions especially when the solutions have great commonalities.
  Timely solution is important because the number of UE(s) impacted by the solution will continuously increase
Proposals
  RAN agree to solve SIB 24 extension problem based on the technically endorsed CRs in September version specifications.
  RAN agree to solve SIB 24 multiplexing problem by updating the technically endorsed CRs in September version specifications.

## Slide 11: Annex. Scheduling (in)flexibility of SystemInformation
Transmitting legacy SIB and new SIB together in a SystemInformation and transmitting them in separate SystemInformation(s) makes difference in time domain scheduling.
One additional si-Window is required. Unless the sum of si-Windows > si-Periodicity, it doesn’t matter
Si-Window
Si-Window
Si-Periodicity
Si-Window
Si-Window
Si-Periodicity
Legacy SIB
New SIB
2) Transmitting legacy SIB and new SIB in seperate SystemInformation(s)
1) Transmitting legacy SIB and new SIB in a SystemInformation
One more Si-Window