## Slide 1: Motivation for supporting non-colocated scenarios for band 42 and n77
SoftBank Corp., KDDI,
3GPP TSG RAN meeting #89e
Electronic Meeting, Sept. 14 – 18, 2020
Agenda Item: 9.1.2
Document for: discussion
RP-201599

## Slide 2: Background – Spectrum point of view
Co-existence with other systems
Timing of Spectrum allocation
  The 3 blocks in C-band were allocated at different time
   This makes Tx antenna colocation cost-inefficient (or sometimes infeasible)
SoftBank
X
X
Y
SoftBank
3400
3440
3480
3520
3560
3600
X
Y
Z
SoftBank
Y
3600
3700
3900
3800
4000
Satellite Systems
Different co-existence conditions apply.
 As a result, Tx antenna co-location is not always available
1st allocation
2nd allocation
3rd allocation

## Slide 3: Background – 3GPP point of view
3GPP standards
  Rules for “intra-band” apply to EN-DC 42_n77
  TS38.133 cls. 7.6.3 defines MRTD limit for intra-band EN-DC (=3us)
  Power imbalance limit has been discussed in Rel-16
    One candidate value is 6dB
   These limitations reduce the availability of EN-DC in our network

## Slide 4: Scenario and target value for new perf. Req.
Conditions bw. eNB and gNB
Very short Rx time difference(3us)
Power imbalance (6dB?)
Rel-16 (Discussion ongoing)
eNB
gNB
Deployment scenario
Colocated
Different antenna pattern
Our Proposal
eNB
gNB
Conditions bw. eNB and gNB
Short Rx time difference([10]us)
Power imbalance ([25]dB)
Deployment scenario
Non-colocated (at maximum 3 Tx points)
Different antenna pattern
Our goal: Define UE performance requirements for intra-band EN-DC and NR-CA for non-colocated scenarios

## Slide 5: Proposals
RAN4 to define performance requirements assuming non-colocated scenario for intra-band non-contiguous EN-DC/NR-CA (e.g. band 42, n77)in Rel-17
  Extend the target MRTD to [10†]us
  Extend the target power imbalance
    to [25††] dB assuming single Rx chain, and/or
    by introducing a UE capability report that indicates the support of dual Rx chain in a band of interest
Note †: This value can be further discussed considering operators’ scenarios & UE complexity.
Note ††: This value comes from R4-2000953, which can be a starting point of the discussions.

## Slide 6: EOF