## Slide 1: Considerations on NR-U
MediaTek Inc.
3GPP TSG RAN#89E RP-201699
September 2020 Agenda Item 9.2.2

## Slide 2: Background
Rel-16 NR-U Exception Sheet granted at RAN#88e/Jun 2020 to allow
  Completion of 5GHz work in Q3
  Completion of 6GHz work in Q3
  RP-201387
RAN4#96E Status
  5GHz work deemed ~complete (Spectrum utilization 60kHz SCS pending)
  6GHz work: major progress achieved though work incomplete

## Slide 3: 6GHz Status Outstanding Issues
BS RF Requirements critical
Support for Standard-power AP & Clients
  Standard-power access points & client devices
    Permitted indoors and outdoors in U-NII-5, 7 only with AFC
    AP: max power 36dBm EIRP (PSD of 23dBm/MHz EIRP)
    Client: max power 30dBm EIRP (PSD of 17dBm/MHz EIRP)
  Low-power access points & client devices
    Permitted indoors only in U-NII-5, 6, 7, 8
    AP: max level 30dBm EIRP (PSD of 5dBm/MHz EIRP)
    Client: max power 24dBm EIRP (PSD of -1dBm/MHz EIRP) (AP levels allowed in some config. only e.g. mesh, extenders)
  Plenary decision needed whether to support Low-power only or both Low- and Standard-power
Other requirements e.g. ΔfOBUE, ΔfOOBB, co-existence, IBB, OOBB, LO leakage etc.
  “Blind” copy of 5GHz requirements unsuitable
  Requirements to be defined based on proper analysis to ensure sound deployable standard
U-NII-5 (5.925-6.425 GHz) and U-NII-7 (6.525-6.875 GHz)
U-NII-6 (6.425-6.525 GHz) and U-NII-8 (6.875-7.125 GHz)

## Slide 4: 6GHz Status Outstanding Issues
UE RF Requirements
Rx REFSENS
  MediaTek requests min 1.1dB relaxation vs. n46 (5GHz)
  1.1dB is a fair average of the different values proposed by vendors, noting not all vendors have been able to propose a value at this stage
UE co-existence
System Parameters
Spectrum Utilization 60kHz SCS
Channelization band n96
Band plan
US focus vs. US+EU focus: EU Regulations incomplete
  Plenary decision needed
U-NII-5 (5.925-6.425 GHz) and U-NII-7 (6.525-6.875 GHz)
U-NII-6 (6.425-6.525 GHz) and U-NII-8 (6.875-7.125 GHz)

## Slide 5: Proposals
Proposal 1: Further Rel-16 exception required to complete the work (not maintenance)
Proposal 3: RAN#89e decision needed whether to support in Rel-16 specs
  Low-power ONLY; or
  BOTH Low-power and Standard-power
Proposal 3: UE Rx REFSNS: min 1.1dB relaxation vs. 5GHz required
Proposal 4: BS RF requirements definition subject to another meeting cycle
Proposal 5: Decision required whether to focus only on US band in Rel-16