## Slide 1: Handling of SIB19 onwards Discussion on non 3GPP compliant UEs
MediaTek Inc.
3GPP TSG RAN#89E RP-201706
September 2020 Agenda Item 14

## Slide 2: Background
Non-3GPP Compliant LTE UEs on the field
  ENUMERATED extension marker in LTE SIB1 (in SIB-Type) NOT correctly implemented starting from Rel-12
  Impact:
    Affected UEs unable to camp on LTE cells broadcasting any of SIB19 onwards – LTE cells barred
    Affects at least: LTE D2D (Rel-12 SIB19), LTE SC-PTM (Rel-14 SIB20), LTE V2X (Rel-14/15 SIB21/26), NR SA (Rel-15 SIB24), LTE UAC (Rel-15 SIB25), EN-DC enh. (Rel-16 SIB26a), etc.
    For NR SA : SIB24 provides NR cell reselection info in LTE cells
MediaTek UEs are 3GPP-compliant and are unaffected by this bug
RAN2#111E – No consensus
  Technical Endorsed CRs: delivery of SIB19+ scheduling info not using SIB1 SIB-Type extension
  CRs starting from Rel-12 introducing major changes to LTE RRC specifications
  No consensus reached to proceed with the proposal: Decision deferred to RAN#89E

## Slide 3: Discussion
Adapting 3GPP specifications to badly implemented UEs is always discouraged
  Additional effort required to change correct implementations (NW, UEs)
  Additional effort required to OTA-update correctly implemented UEs already on the field
  Work around ~systematically seeked on infra+MNO side instead
Severity of the issue: several millions of LTE UEs seem affected by the bug
  Misc. types of devices with buggy chipsets: IoT devices and smartphones
  OTA update is arguably a major challenge
  Idle mode issue i.e. individual UE workaround not possible on infra+MNO side
RAN2 Technically endorsed CRs may require OTA update of other UEs on the field
Technically endorsed CRs include major changes to long-frozen specifications
  No guarantee confirmed that the CRs will NOT unleash other unforeseen problems with UEs on the field

## Slide 4: Proposal
MediaTek recommends
  No approval of RAN2 technically endorsed CRs at RAN#89E No principle agreement towards RAN#90E
  Min. 3-month additional review period to
    Confirm whether OTA update of affected UEs is out of question
    Verify impact of the CRs on all UEs on the field
    Identify workaround (no spec impact)
  Proper Test Cases MUST always be defined esp. for such basic mechanisms as a field extension