## Slide 1: Clarification of supporting SRS transmission in Scell Dormancy in Rel-17 further MR-DC enhancements WI
Futurewei, MediaTek
RAN 89e
2020/09/14 - 2020/09/18
RP-201894
Agenda Item: 9.8.9
Document for: Discussion and Decision

## Slide 2: R16 SRS in dormancy: RAN1/2/4 LS and replies
RAN2 LS (R2-2002381, R1-2001514, R4-2003371 )
  Supporting of AP CSI trigger and reporting for dormant BWP is discussed in RAN2, RAN2 concluded that the AP CSI is not supported due to UE power saving concern.
  For supporting of (periodic, semi-persistent, aperiodic) SRS transmission, RAN2 concluded that SRS transmission is not supported in case the DL BWP is switched to dormant BWP.
  Q3: Are there any issues due to RAN2 agreements on CSI reporting and SRS transmission, i.e. not support aperiodic CSI reporting for dormant BWP and not support SRS transmission on dormant BWP?
RAN1 LS reply (R1-2003075, R2-2004360)
  RAN1 could not reach a consensus on the support of A-CSI measurement in dormant BWP (with report triggered by another cell e.g. PCell) or SP/A-SRS transmission in dormant BWP. RAN1 sees no issue with supporting at least long periodicity P-SRS (e.g. >100ms).
RAN4 LS reply (R4-2009245, R2-2006135)
  RAN4 discussed the impact of not supporting CSI reporting and SRS transmission. Not supporting UL P-SRS transmissions risks performance losses on UL/DL performance in TDD systems, UL PC, BFR/Beam management and Timing Advance. RAN4 see some benefits and these performance losses can be prevented by maintaining some UL P-SRS with long periodicity while at the cost of power saving.
RAN2 Chair note (R2-2006501)
  Chair: It seems this doesn’t really change the situation. R2 already acknowleged that there are benefits but anyway decided to not do this in R16. So as positions seems non-changed the current decision stays. It seems however that as R4 agreed on benefits there are indeed significant support to have this, so maybe it should be in R17.

## Slide 3: WID in R16/R17
R16 DCCA Enh. (RP-192336)
  3. Efficient and low latency serving cell configuration/activation/setup
  SCell dormancy was included under this objective in R16 (and later on the dormancy discussed in Power Saving was also merged into here)
R17 Further MR DC Enh. (RP-201040)
  Support efficient activation/de-activation mechanism for one SCG and SCells
    Support for one SCG applies to (NG)EN-DC, and NR-DC [RAN2, RAN3, RAN4]
    Support for SCells applies to NR CA, based on RAN1 leading mechanisms [RAN1, RAN2, RAN4]
    This objective applies to FR1 and FR2
   SCell dormancy should be considered as within the scope of FeMRDC

## Slide 4: Observations and Proposal for Scope Confirmation
Observations
  SRS in SCell dormancy helps maintain UL connection (TA/PC/beam), DL/UL CSI acquisition, and facilitate out-of-dormancy transition
  With proper network decisions (e.g., gNB configuration), SRS in SCell dormancy may also help save UE power (see next page for details)
  In RAN1/2/4, there is a general common understanding that at least some long-periodicity P-SRS can be supported and beneficial
  Some suggested to consider supporting SRS in SCell dormancy in Rel-17
  SCell dormancy is within the scope of Rel-17 Further MR DC Enh.
Proposal for Rel-17
  Confirm that the following is within the Rel-17 Further MR DC Enh. scope:
    SRS transmission in Scell Dormancy (e.g. long-periodicity P-SRS, if configured)

## Slide 5: Further detail on technical motivations for SRS in dormancy
Technical motivations for support SRS in SCell dormancy
  Maintaining the UL connection in dormancy
    With SRS in dormancy, the UL connection would not be lost even with long dormancy
    UL TA, UL PC and UL beam can be maintained via SRS
  DL/UL CSI acquisition
    DL full MIMO CSI in TDD, DL partial MIMO CSI in FDD (related to R17 FeMIMO FDD CSI enh.), and UL CSI in TDD/FDD can be acquired via SRS. This improves DL/UL spectrum efficiency when data arrives
  Facilitate out-of-dormancy transition
    Network can make a more appropriate decision on when/whether to leave dormancy with SRS than without SRS
    Network can make a more appropriate UL/DL scheduling decision after leaving dormancy with SRS than without SRS
    Shortens out-of-dormancy transition, as no need to re-establish UL TA/PC/beam or UL/DL CSI
UE power saving considerations
  Depending on the scenarios and gNB decisions, supporting SRS in dormancy may save power
  E.g., with SRS in dormancy, gNB can allow UE to have very long dormancy, which saves power (rather than waking up UE often to maintain the connection)