## Slide 1: 3GPP TSG RAN Meeting #89e RP-202095 Online Meeting, Sept. 2020
Title: Achieving consistency on FR2 fallback behaviour across WGs
Source: Qualcomm Incorporated

## Slide 2: Background – from moderator summary on #7
[89E][07][FR2_fallback]_Summary_final round.docx
Based on the overall discussion in RAN#88e and RAN#89e, moderator recommends approving the following tdoc
  WF RP-201538
  TS38.101-2 CR RP-201872(R15) and RP-201873(R16)
  TS38.101-3 CR RP-201874(R15) and RP-201875(R16)
Strong concerns were expressed with WF and CR by Qualcomm

## Slide 3: Inconsistencies in WF RP-201538
Relaxed ‘conformance requirements’ in WF proposal becomes ‘no requirements’ in CR implementation
Proposed WF (RP-201538) is in line with RAN#88e agreement and suggests:
  UE must support all the fallback band combinations
  UE conformance requirements w.r.t. the fallback band combinations are relaxed:
    The fallback band combinations fulfilling both the following conditions are exempt from requirements:
      consists of multiple sub-blocks
      has at least one sub-block comprising a contiguous CA combination (i.e. a letter B, C, D, …).
  The UE shall comply to all regulatory requirements for all supported band combinations, i.e. including for all fallback band combinations.
But implementation in proposed CRs (RP-201872-5) says:
  For FR2 intra-band CA combinations with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination, there are no RF performance requirements for the fallbacks with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination. Requirements in other specifications are not affected.

## Slide 4: CR wording problem
CR Wording:
  For A terminal which supports CA or DC configurations, which include FR2 intra-band CA combinations with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination, there are no RF performance requirements for the fallbacks with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination.
‘No performance requirement’ is a blank check to UEs:
  Missing explicit list of RF requirements that will not be met by UEs under fallback conditions.
  No consideration for legacy UEs that are designed to a higher standard (meets all RF requirements for all fallbacks)

## Slide 5: Proposed WF for FR2 CA fallbacks
Signalling solution:
  Shall be instituted to allow a network to distinguish between the following types of UEs:
    Those that support all RF requirements for all fallbacks
    Those that do not support all RF requirements for fallbacks when configured with combinations with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination
  Shall be backward compatible for legacy UEs that that support all RF requirements for all fallbacks (Type ‘A’ above)
    No change required by such legacy UEs to convey same capability as before
CR Wording:
  For A terminal which supports CA or DC configurations, which include FR2 intra-band CA combinations with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination, RF requirements of sub-sections [7.5A and 7.6A] are waived for the fallbacks with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination.