## Slide 1
Steven Chen
RAN4 Chairman (Apple)
Status Report RAN WG4 to TSG-RAN #90-e
3GPP TSG RAN #90-e RP-202131
E-meeting, Dec. 7-11, 2020

## Slide 2: Summary (1/3)
In Q4, RAN4 had one e-meeting, i.e. #97-e
  Email discussions were organized in 110 email threads, each with a moderator, in three parallel sessions (Main, RRM, BS RF_Test_Demod). Moderators generated summaries that allows traceability of discussions and decisions. Delegates were more comfortable and familiar with the arrangement.
  6500+ emails
  9 GTW calls in each session, a total of 81 hours of call, were used to treat critical or controversial topics.
  Overall, the progress was good.
Continue to enforce meeting improvement measures detailed in R4-2016602, and meeting deadlines.
  Given the large number of contributions, CR quality is still a serious issue.
  CR Quality Control measures in R4-2016602 will be strictly enforced from RAN4 meeting #98-e onwards

## Slide 3: Summary (2/3)
    Updated R16 LTE/NR UE feature list sent to RAN2. While normal maintenance work may take place in future meetings, no major change is expected.
  A working agreement was made to reach agreement on R4-2016850.
R15 NR
  Still a substantial amount of effort was put into R15 NR maintenance. It seems no delegates challenged the essentiality of any R15 CR.
  Very high threshold for essential correction after Q4. New measures may be proposed for this purpose.
R16 NR
  Normal maintenance work on completed R16 WI took place
  The only open spectrum WI NR_n48_LTE_48_coex was completed
  Remaining issues of NR-U were closed.
  Good progress on R16 Perf part for the WIs with completed Core part.
    Several WIs performance part was completed (NR 2-step RACH, NR Mobility Enhancements, HST, OTA BS testing)
    The performance part for most WIs is planned for completion by March 2021.
    Some WIs are behind the progress with <50% completion due to late start and may need to be extended to June 2021. Final decision can be made in March 2021.

## Slide 4: Summary (3/3)
Rel-17 NR
  Ramped up work on selected Rel-17 work items
LTE maintenance (up to Rel-15)
  Good progress. No major issues
Rel-16 LTE
  Perf part is complete for eMTC and NB-IoT WIs. LTE FeMob WIs to be extended till Q1’21.

## Slide 5: Statistics
Chart: 
| #90bis | #91 | #92 | #92bis | #93 | #94-e | #95-e | #96-e | #97-e
Delegates | 324 | 387 | 266 | 298 | 382 | 226 | 308 | 349 | 367
Chart: 
| #90bis | #91 | #92 | #92bis | #93 | #94-e | #95-e | #96-e | #97-e
Contributions | 2774 | 2337 | 2576 | 2230 | 2886 | 2883 | 3297 | 2971 | 3736
Meeting | Date | Location | Host | Delegates registered/attendees | Documents requested/uploaded
RAN4 #97-e | 2 – 13 Nov. 2020 | Electronic meeting |  | 367/367 | 3736/3551

## Slide 6: NR

## Slide 7: R16 NR RAN4 led WI/SIs
Title | Target completion date from last RAN | Notes
WI: FR1 UE RF | Core: Sep 2020 Perf: Dec 2020 | Perf part completed.
WI: RRM Req. Enhancements | Core: Sep 2020 Perf: March 2021 | RRM Perf part ongoing
WI: CSI-RS based L3 Measurement | Core: Sep 2020 Perf: March 2021 | RRM Perf part ongoing
WI: High Speed Train Scenarios | Perf: Dec 2020 | Perf part completed.
WI: FR2 DL 256QAM | Perf: March 2021 | Demod part ongoing.
WI: OTA BS Testing | Perf: Dec 2020 | Completed
WI: Performance Req. Enhancement | Perf: Dec 2020 | Incomplete, rapporteur proposed to extend the Perf part to March 2021

## Slide 8: R16 NR other WG led WI/SIs
Title | Target completion date from last RAN | Notes
WI: eMIMO | Core: Sep 2020 Perf: Dec 2020 | RRM Perf part ongoing. Demod part incomplete. Rapporteur proposed to extend to March 2021
WI: NR-U | Core: Dec. 2020 Perf: March 2021 | RF core complete. RRM Perf part ongoing. Demod part ongoing
WI: eURLLC | Perf: Dec 2020 | Demod part incomplete. Rapporteur proposed to extend the Perf part to March 2021
WI: Power Saving | Perf: Dec 2020 | RRM Perf part completed Demod part incomplete. Extension on completion date expected.
WI: Positioning | Core: Sep 2020 Perf: March 2021 | RRM Perf part ongoing. Rapporteur proposed to extend to June 2021
WI: NR V2X | Perf: March2021 | RRM Perf part ongoing. Demod part ongoing.
WI: NR Mobility Enhancement | Perf: Dec 2020 | RRM Perf part completed.

## Slide 9: R16 NR other WG led WI/Sis (Cont.)
Title | Target completion date from last RAN | Notes
WI: MR-DC | Perf: March 2021 | RRM Perf part ongoing. No demod part impact.
WI: IAB | Perf: June 2021 | RRM Perf part ongoing. RF conformance testing ongoing. Demod part ongoing.
WI: 2-step RACH | Perf: Dec 2020 | Perf part completed

## Slide 10: R16 NR Spectrum WI/SIs
Title | Target completion date from last RAN | Notes
WI: LTE/NR spectrum sharing in band 48/n48 | Core: Dec. 2020 | Core part completed.

## Slide 11: R17 NR Spectrum WI/SIs
Title | Target completion date from last RAN | Notes
WI: NR_FR2_FWA_Bn257_Bn258 | Core: Dec 2020 Perf: Feb 2021 | Core part incomplete. To be extended to Q1 2021.
WI: Introduction of NR band n13 | Core: Dec 2020 | Completed
SI: FS_6425_10500MHz _NR | Dec. 2020 | Ongoing. To be extended to Q1 2021.
SI: Study on high-power UE operation for fixed-wireless/vehicle-mounted use cases in LTE bands 5 and 12 and NR band n71 | March 2021 | Ongoing
SAR schemes for UE PC2 for NR inter-band CA and SUL configurations with 2 bands UL | Core: Mar 2021 Perf: Mar 2021 | Ongoing

## Slide 12: R17 NR Spectrum WI/SIs (Cont.)
Title | Target completion date from last RAN | Notes
WI: Introduction of CBW 35MHz and 45MHz for NR FR1 | Core: Mar 2021 Perf: Mar 2021 | Ongoing
WI: Introduction of NR SUL band 1880-1920MHz | Core: Dec 2020 Perf: Dec 2020 | Core part and Perf part completed
WI: Introduction of 2300-2400MHz SUL band for NR | Core: Dec 2020 Perf: Dec 2020 | Core part and Perf part completed
WI: Introduction of NR 47 GHz band | Core: Mar 2021 Perf: Mar 2021 | Ongoing
WI: Introduction of NR band n24 | Core: Jun 2021 Perf: Jun 2021 | Ongoing
WI: Introduction of 1.6 GHz NR SUL band with same uplink frequency range of Band 24 | Core: Jun 2021 Perf: Jun 2021 | Ongoing
WI: LTE/NR spectrum sharing in Band 40/n40 | Core: Sep 2020 | Completed

## Slide 13: R17 NR RAN4 led WI/SIs
Title | Target completion date from last RAN | Notes
WI: RF requirements enhancement for NR frequency range 1 (FR1) | Core: Sep 2021 Perf: Dec 2021 | First meeting, ongoing
WI: Further enhancement on NR demodulation performance | Perf: Mar 2022 | Not started in RAN4 yet
WI: Introduction of DL 1024QAM for NR FR1 | Core: June 2021 Perf: | Not started in RAN4 yet
WI: Enhanced NR support for high speed train scenario for frequency range 1 (FR1) | Core: Sep 2021 Perf: Mar 2022 | First meeting, only work plan discussed
WI: MIMO OTA requirements for NR UEs | Core: Sep 2021 Perf: Sep 2021 | Ongoing
SI: Study on efficient utilization of licensed spectrum that is not aligned with existing NR channel bandwidths | Jun 2021 | First meeting, ongoing
WI: Further enhancements of NR RF requirements for frequency range 2 (FR2) | Core: Sep 2021 Perf: Dec 2021 | First meeting, ongoing

## Slide 14: R17 NR RAN4 led WI/Sis (Cont.)
Title | Target completion date from last RAN | Notes
WI: NR and MR-DC measurement gap enhancements | Core: Sep 2021 Perf: Mar 2022 | First meeting, only work plan discussed
WI: NR support for high speed train scenario in FR2 | Core: Sep 2021 Perf: Mar 2022 | First meeting, ongoing
WI: Further RRM enhancement for NR and MR-DC | Core: Sep 2021 Perf: Mar 2022 | First meeting, only work plan discussed
SI: FR2 Test enhancement | Jun 2021 | Ongoing

## Slide 15: R17 NR other WG led WI/SIs
Title | Target completion date from last RAN | Notes
SI: Study on supporting NR from 52.6 GHz to 71 GHz | Mar 2020 | Ongoing.
WI: UE Power Saving Enhancements for NR | Core: Sep 2021 Perf: Mar 2022 | First meeting, ongoing
WI: Solutions for NR to support NTN | Core: Jun 2021 Perf: Dec 2022 | First meeting, ongoing
WI: WI on SL enhancements in Rel-17 | Core: Perf: | First meeting, ongoing

## Slide 16: Rel-17 NR Basket WIs
WI Title | Status Report | Revised WID
NR intra-band CA | RP-202184 | RP-202187
NR Inter-band CA for 3 bands DL with 1 band UL | RP-202721 | RP-202720
NR Inter-band CA for 4 bands DL with 1 band UL | RP-202186 | RP-202189
DC for 2 bands DL with 2 bands UL (1 LTE band + 1 NR band) | RP-202536 | RP-202545
DC for 3 bands DL with 2 bands UL (2 LTE bands + 1 NR band) | RP-202612 | RP-202613
DC for 4 bands DL with 2 bands UL (3 LTE bands + 1 NR band) | RP-202185 | RP-202188
DC for 5 bands DL with 2 bands UL (4 LTE bands + 1 NR band) | RP-202589 | RP-202560
DC for 6 bands DL with 2 bands UL (5 LTE bands + 1 NR band) | RP‑202539 | RP‑202540
DC of x bands (xDL/1UL x=1, 2,3,4) LTE and 2 NR bands (2DL/1UL); | RP-202293 | RP-202292
DC of x bands (x=1,2) LTE inter-band CA (xDL/xUL) and y bands (y=3-x) NR inter-band CA (yDL/yUL) | RP-202193 | RP-202192
NR Inter-band CA/DC for 2 bands DL with x bands UL (x=1,2) | RP-202200 | RP-202199
NR Inter-band CA/DC for 3 bands DL with 2 bands UL | RP-202202 | RP-202201
Band combinations for SA NR supplementary uplink (SUL), NSA NR SUL, NSA NR SUL with UL sharing from the UE perspective (ULSUP) | RP-202610 | RP-202611

## Slide 17: Rel-17 NR Basket WIs (Cont.)
Above revised WIDs have been endorsed by RAN4
WI Title | Status Report | Revised WID
DC of x bands (x=1,2,3) LTE inter-band CA (xDL/1UL) and 3 bands NR inter-band CA (3DL/1UL) | R4-202195 | R4-202194
NR inter-band CA/DC for DL 4 bands and 2UL bands | RP-202543 | RP-202544
NR inter-band CA for 5 bands DL with x bands UL (x=1, 2) | RP-202608 | RP-202609
DC of x bands (x=2,3,4) LTE inter-band CA (xDL/1UL) and 1 NR FR1 band (1DL/1UL) and 1 NR FR2 band (1DL/1UL) | RP-202541 | RP‑202542

## Slide 18: Rel-17 NR Basket WIs (Cont.)
WI Title | Status Report | Revised WID
High power UE (power class 2) for NR inter-band CA with 2 bands DL and 2 bands UL | RP‑202367 | RP-202373
Adding new channel bandwidth(s) support to existing NR bands | RP‑202278 | RP-202277
High power UE (power class 2) for EN-DC | RP‑202283 | RP-202282
Band combinations on concurrent operation between Uu frequency bands and V2X bands | RP‑202722 | 

## Slide 19: LTE

## Slide 20: R16 LTE other WG led WI/SIs
Title | Target completion date from last RAN | Notes
WI: eMTC5 | Perf: Dec 2020 | Perf part completed
WI: NB-IOTenh3 | Perf: Dec 2020 | Perf part completed
WI: LTE even further mobility enhancement | Perf: Dec 2020 | RRM Perf part ongoing. Extension to March 2021 requested

## Slide 21: R17 LTE RAN4 led WI/SIs
Title | Target completion date from last RAN | Notes
WI: LTE Band 24 Specifications to comply with updated regulatory emission limits | Core: Jun. 2021 Perf: Jun. 2021 | Ongoing

## Slide 22: Rel-17 LTE Basket WIs
  Above revised WIDs have been endorsed by RAN4
WI Title | Status Report | Revised WID
LTE inter-band CA for 2 bands DL with 1 band UL | RP-202572 | RP-202573
LTE inter-band CA for 3 bands DL with 1 band UL | RP-202614 | RP-202615
LTE inter-band CA for x bands DL (x=4, 5) with 1 band UL | RP-202213 | RP-202212
LTE inter-band CA for 2 bands DL with 2 band UL | RP-202616 | N/A
LTE inter-band Carrier Aggregation for x bands (x= 3, 4, 5) DL with 2 bands UL | RP-202290 | RP-202289
Additional LTE bands for UE category M1&M2 and/or NB1&NB2 in Rel-17 | RP-202294 | N/A

## Slide 23: RAN4 TU Budget
Total capacity is 45 TUs with 3 parallel sessions, which does not include
  Monday morning common session
  Friday comeback session
  Evening AH session
3
3
3
4
4
4
4
4
4
4
4
4

## Slide 24: RAN4 TU Budget
Proposal for future meetings
  RF: 24.5 TUs
  RD: 20.5 TUs
Detailed TU allocation for each WI/SI will be shared in a separate document

## Slide 25: General Principles for TU allocation
  R15 and R16 maintenance
  R15: Plan no TU allocation after Q1 2021
  R16: reduced TU allocation from Q3 2021 onwards
  Rel-16 perf part
  TU allocation till Q2 2021 for following WIs: NR-U, NR V2X, NR Pos, NR IAB, MR-DC, and L3 CSI-RS
  Rel-17 WI/SIs
  Core part completion by Q1 2022 and Perf part completion by Q3 2022
  For other WG led WI/SIs:
    RRM Core part: Slow start in Q2 2021 and ramp up in Q3 2021 (except for NTN and Power Saving WIs which already started)
    RRM Perf part: Start in Q2 2022
    Demod Perf part: start from Nov. meeting in 2021 at the earliest
  For RAN4 led WI/SIs:
    RRM Core part: Start in Q1 2021
    RRM Perf part: Start in Q2 2022
    Demod Perf part: start from Q2 2021 except NR FR1_HST
Note: For WI/SIs whose RAN4 impact is not clearly defined in their WIDs, TU allocation is based on RAN4 leadership’s judgment.

## Slide 26: Thank You!
  Vice chairs Haijie Qiu and Andrey Chervyakov for helping structure the e-meeting and chairing sessions
  Kai-Erik Sunell for efficient secretary support
  Email moderators for leading the email discussions and providing summaries
  Delegates for contributions and discussions