## Slide 1: Views on Reduced Capability NR device WI
3GPP TSG RAN Meeting #90-e RP-202353
7th – 11th December 2020
Agenda Item: 9.1.1
Source: Intel Corporation
Document for: Discussion/Decision

## Slide 2: Rel-17 RedCap: Motivation & target use-cases
Key motivation for Reduced Capability (RedCap) NR devices
  Effectively support use-cases that are not optimally addressed by Rel-15/Rel-16 NR devices in terms of tradeoff between performance (throughput, coverage, latency, and reliability) and device cost/complexity and power consumption.
  Expected to address requirements served by UEs with capabilities in between those for LPWA (e.g., eMTC, NB-IoT) solutions and Rel-15 NR specifications
Use-cases prioritized during the SI
  Industrial Wireless Sensors
  Video surveillance
  Wearables

## Slide 3: Rel-17 SI on RedCap: Summary (1/2)
Rel-17 studies on RedCap completed in RAN1
The study focused on the following areas:
  Features targeting UE cost/complexity reduction
  Features targeting UE power consumption reduction via reduced PDCCH monitoring
  Evaluation of achievable coverage and identification of need for coverage recovery to compensate for any coverage reduction due to reduced UE RF/baseband capabilities
RAN1 converged on the following recommendations on cost/complexity reduction features:
  UE BW reduction:
    Max UE BW of 20 MHz and 100 MHz for FR1 and FR2 respectively
  Max # of Tx/Rx branches and max # of DL MIMO layers:
    For both FR1 and FR2, UE # Tx branches = 1
    In bands where NR UE is required to support 2 Rx, UE # Rx branches = max # of DL MIMO layers = 1
  Max DL modulation order:
    Mandatory support of max DL modulation order in FR1 limited to 64QAM (from 256QAM).

## Slide 4: Rel-17 SI on RedCap: Summary (2/2)
Several details on exact work scope deferred to RAN Plenary or for resolution during the WI phase
  Some of the details depend on exact UE cost/complexity reduction features and the coverage recovery targets for RedCap UEs.
  Some details also depend on RAN2 decisions (e.g., options related to RedCap UE type definition and RedCap UE identification).
    Note: For RAN2 and RAN4, the Rel-17 studies on RedCap are still in progress, to be concluded at RAN #91-e
Further scoping of objectives with RAN1 involvement include:
  Remaining details on UE cost/complexity reduction features beyond recommendations from RAN1
  UE power savings via reduced PDCCH monitoring
  Coverage recovery targets for RedCap UEs
  RedCap UE type(s) and RedCap UE identification

## Slide 5: Summary of cost estimates for combinations of cost/complexity reduction features
FR2 UE complexity reduction technique(s) | RF cost metric | BB cost metric | Total cost metric | Total reduction
100 MHz (instead of 200 MHz) | 100.0% | 65.5% | 82.8% | 17.2%
100 MHz, 1 layer, 1 Rx | 63.1% | 37.4% | 50.2% | 49.8%
100 MHz, 1 layer, 1 Rx, double N1 and N2 | 63.1% | 31.9% | 47.5% | 52.5%
FR1 FDD UE complexity reduction technique(s) | RF cost metric | BB cost metric | Total cost metric | Total reduction
20 MHz (instead of 100 MHz) | 100.0% | 44.7% | 66.8% | 33.2%
20 MHz, 1 layer, 1 Rx | 71.0% | 25.9% | 43.9% | 56.1%
20 MHz, 1 layer, 1 Rx, DL 64QAM, UL 16QAM | 69.7% | 24.7% | 42.7% | 57.3%
20 MHz, 1 layer, 1 Rx, DL 64QAM, UL 16QAM, double N1 and N2 | 69.7% | 21.0% | 40.5% | 59.5%
20 MHz, 1 layer, 1 Rx, DL 64QAM, UL 16QAM, HD-FDD type A, double N1 and N2 | 58.5% | 21.0% | 36.0% | 64.0%
FR1 TDD UE complexity reduction technique(s) | RF cost metric | BB cost metric | Total cost metric | Total reduction
20 MHz (instead of 100 MHz) | 100% | 43.4% | 66.0% | 34.0%
20 MHz, 2 layers, 2 Rx | 69.5% | 24.7% | 42.6% | 57.4%
20 MHz, 2 layers, 2 Rx, DL 64QAM, UL 16QAM | 67.9% | 23.4% | 41.2% | 58.8%
20 MHz, 2 layers, 2 Rx, DL 64QAM, UL 16QAM, double N1 and N2 | 67.9% | 20.1% | 39.2% | 60.8%
20 MHz, 1 layer, 2 Rx | 69.5% | 20.4% | 40.0% | 60.0%
20 MHz, 1 layer, 2 Rx, DL 64QAM, double N1 and N2 | 67.9% | 16.4% | 37.0% | 63.0%
Note: The cost estimates are based on those in R1-2009025 (Intel) and not based on the averaged values across companies captured in the TR
  This was necessary for accurate relative comparisons in consideration of the adjustments (not limiting to 16QAM for UL per RAN1 agreement, and max 1 DL MIMO layer for 2Rx UEs) to the combination of components considered in the TR.
Observations:
  For FR1 FDD
    In addition to [20 MHz, 1 layer, 1Rx and max DL modulation of 64QAM], doubled N1/N2 and HD-FDD type A provides ~7% additional cost reduction
  For FR1 TDD
    Compared to [20 MHz, 2 layers, 2Rx and max DL modulation of 64QAM], the combination [20 MHz, 1 layer, 2Rx, max DL modulation of 64QAM, and doubled N1/N2] provides more than 4% additional cost reduction.
  For FR2
    In addition to [100 MHz, 1 layer, 1Rx], doubled N1/N2 provides ~3% additional cost reduction.

## Slide 6: RedCap UE cost/complexity reduction features
In addition to the existing recommendations from RAN1, following aspects need to be resolved for WI scoping:
  # of Rx/MIMO layers
    In bands where NR UE is required to support 4 Rx, max # Rx branches = 1 or 2?
      Proposal: Max # of Rx branches = 2
        Justification: Significant impact to link performance coverage/reliability and spectral efficiency (link and cell-level) in going from 4Rx to 1Rx
    MIMO layers for cases with 2Rx?
      Proposal: 1 layer is mandatory; 2 layers can be optional
      Justification: 2 DL MIMO layers is not necessary for most use-cases targeted for RedCap; 1 MIMO layer can further help reduce baseband cost/complexity while 2Rx branches can provide robust reliability/coverage performance (see previous slide for cost comparisons).
  Whether to support relaxed UE min. processing times for PDSCH/PUSCH processing
    Proposal: Support relaxed UE min. processing times for PDSCH/PUSCH processing, preferably also including relaxation of CSI processing timelines
    Justification: Relaxes demands on baseband processing and parallelization; allows for lower UE power consumption; can satisfy QoS requirements for RedCap use-cases; minimal impact to NW operations or coexistence. Relaxing requirements on CSI processing timelines help realize full benefit of PDSCH/PUSCH processing time relaxations (e.g., PDCCH processing time can be relaxed for all cases) and allows for simplified MIMO processing blocks (see previous slide for cost comparisons).
  Whether to support HD-FDD Type A or FD-FDD or both from spec perspective for FR1 RedCap UEs
    Proposal: Both FD-FDD and HD-FDD Type A can be supported from specifications perspective
      See previous slide for cost comparisons

## Slide 7: RedCap UE power savings via reduced PDCCH monitoring
Whether and which UE PS schemes to introduce for RedCap UEs of the following:
  Scheme #1: Reducing limits of BDs per slot and/or reducing max number of DCI format sizes
  Scheme #2: Sparse (in time) PDCCH monitoring
  Scheme #3: Dynamic adaptation of PDCCH SS sets and monitoring configurations
Proposal: Specify reduced limits for BDs per slot by approximately 50% of the Rel-15 values (under Scheme 1)
  Reduction on max number of DCI format sizes can be further considered
  Justification:
    Reducing the limits on # of BDs per slot by about 50% (under Scheme #1) provides reduced UE power consumption as well as allows for relaxed dimensioning of the UE (lower complexity)
      No significant impact on PDCCH blocking performance or any other latency/reliability/co-existence issues observed
    Schemes #2 and #3 are not aligned with RedCap SI objective (see below) and better suited for potential consideration as part of Rel-17 WI on UE power saving enhancements.

## Slide 8: RedCap coverage recovery objectives (1/2)
Observations from RAN1 studies on RedCap coverage recovery:
  For FR1, coverage recovery (up to 3 dB to compensate for UE antenna efficiency loss) may be needed for PUSCH and Msg3.
  For FR1, if RedCap UEs with 1Rx branch are supported for bands requiring NR reference UE to support 4Rx branches, coverage recovery may be necessary for PDCCH CSS and Msg4 for such RedCap UEs.
  For FR2, coverage recovery may be necessary for Msg2/Msg4/PDSCH for RedCap UEs with 1Rx when max TRP 23 dBm is assumed for the reference NR (and RedCap) UE
Relationship to Rel-17 WI on Coverage Enhancements (CE)

## Slide 9: RedCap coverage recovery objectives (2/2)
Proposal:
  Coverage recovery objectives for Rel-17 RedCap WI:
    For FR1, specify coverage recovery (up to 3 dB to compensate for UE antenna efficiency loss) mechanism(s) for PUSCH and Msg3.
      Mechanisms considered as part of Rel-17 WI on CE serve as the starting point, while detailed solution and applicability to RedCap UEs to be specified as part of Rel-17 WI on RedCap
      Justification: Allow for support of small form factor devices (following original target of the SI) in FR1 bands by accommodating RedCap UEs with antenna efficiency losses (up to 3 dB).
    For FR2, specify coverage recovery mechanism(s) for Msg2/Msg4/PDSCH for RedCap UEs with 1Rx to address (reference NR and RedCap) UEs with max TRP of 23 dBm
      Justification: Otherwise, in deployments with (reference NR and RedCap) UEs with max TRP of 23 dBm, the cell coverage would be limited by the reduced coverage for RedCap UEs, which is undesirable

## Slide 10: On RAN2-led items for Rel-17 RedCap
RAN2 is still in progress with the Rel-17 SI on RedCap
  It would be premature to try to conclude any RAN2-led objectives before study is complete in RAN2.
Proposal: Objectives related to RAN2-led RedCap SI objectives to be discussed and finalized at RAN #91-e
  RedCap UE power savings
    eDRX for RRC Inactive/Idle devices
    RRM relaxations for stationary devices
  RedCap Framework/Principles
    RedCap UE type(s) and UE identification
    RedCap UE access restriction

## Slide 11: Summary of Proposals
Rel-17 WI on RedCap

## Slide 12: Rel-17 WI on RedCap: RAN1-led objectives (1/2)
Specify support for the following UE complexity reduction features [RAN1, RAN4]:
  Reduced maximum UE bandwidth:
    Maximum bandwidth of an FR1 RedCap UE during and after initial access is 20 MHz
    Maximum bandwidth of an FR2 RedCap UE during and after initial access is 100 MHz
  Reduced minimum number of Rx branches:
    For frequency bands where a legacy NR UE is required to be equipped with a minimum of 2 Rx branches, the minimum number of Rx branches supported by specification for a RedCap UE is 1. The specification also supports 2 Rx branches for a RedCap UE.
    For frequency bands where a legacy NR UE (other than 2-Rx vehicular UE) is required to be equipped with a minimum of 4 Rx branches, the minimum number of Rx branches supported by specification for a RedCap UE is 2. The specification also supports 4 Rx branches for a RedCap UE.
  Reduced maximum number of DL MIMO layers:
    For a RedCap UE with 1 Rx branch, the maximum number of DL MIMO layers is 1.
    For a RedCap UE with 2 Rx branches, the maximum number of DL MIMO layers is 1. The specification also supports 2 DL MIMO layers for RedCap UE with 2 Rx branches.
  Relaxed maximum modulation order:
    Support of 256QAM in DL is optional (instead of mandatory) for an FR1 RedCap UE.
  HD-FDD Type A for RedCap UEs in FDD bands
    Specifications support both HD-FDD Type A and FD-FDD RedCap UEs in FDD bands.
  Relaxed UE minimum processing times for PDSCH processing and PUSCH preparation:
    Specify relaxed UE minimum processing times (N1 and N2) that are approximately double of their counterparts according to UE minimum processing time capability #1.

## Slide 13: Rel-17 WI on RedCap: RAN1-led objectives (2/2)
Specify reduced PDCCH monitoring to facilitate lower UE power consumption and complexity by reducing limits of BDs per slot [RAN1].
Specify coverage recovery to compensate for coverage reduction due to device complexity reduction as needed [RAN1, RAN4].
  For FR1, specify coverage recovery (up to 3 dB to compensate for UE antenna efficiency loss) mechanism(s) for PUSCH and Msg3.
    Mechanisms considered as part of Rel-17 WI on CE serve as the starting point, while detailed solution and applicability to RedCap UEs to be specified as part of Rel-17 WI on RedCap
  For FR2, specify coverage recovery mechanism(s) for Msg2/Msg4/PDSCH for RedCap UEs with 1Rx to address (reference NR and RedCap) UEs with max TRP of 23 dBm
  Any further relation to or overlaps with the Coverage Enhancement WI can be discussed and resolved in RAN#91e or later.
Specify higher layer support of enhancements listed above [RAN2].