## Slide 1: Motivation for new SI: Study on Duplexing Flexibility for NR
3GPP TSG RAN Meeting #90-e
Electronic Meeting, December 7 - 11, 2020
RP-202546
Agenda Item: 9.12

## Slide 2
Motivation
Explosive increase in demand for data traffic
  Service requirement with asymmetric UL and DL traffic increases, and the ratio between UL and DL traffic changes over the time
  Symmetric DL/UL partitioning may not be effective from spectral efficiency perspective particularly when traffic patterns are either DL heavy or UL heavy
Requirement of ultra low latency
  Limitation in TDM between DL and UL leads higher latency in both DL and UL due to time partitioning between DL and UL
Further enhancement to duplexing flexibility for NR is essential.
Service type | UL/DL ratio -average
Online video | 1:37
Software download | 1:22
Web browsing | 1:9
Social Netwok Service | 4:1

## Slide 3
Enabling Techniques
Dynamic and flexible frequency resource utilization
  Flexible DL/UL resource allocation with FDM manner
    e.g., multiplexing between eMBB DL and URLLC UL with FDM manner
    e.g., multiplexing between mMTC UL and eMBB/URLLC DL with FDM manner
Full duplex functionality
  Simultaneous DL/UL resource allocation for spectral efficiency enhancement and latency reduction
    By allowing full duplex at one spectrum, enhanced spectral efficiency can be achieved (ideally by 2x)
Advanced Cross-Link Interference (CLI) mitigation schemes
  Interference cancellation/rejection receiver
  Resource/beamforming coordination
  CLI measurement and reporting
  eNB/UE Power control

## Slide 4
CLI issues with dynamic duplexing schemes
In Rel-14 NR SI, performance benefits of duplexing flexibility are observed in various deployment scenarios
  Observations for indoor hotspot scenario:
    Evaluations show that duplexing flexibility with cross-link interference mitigation schemes and on a 4GHz and 30GHz provides better UPT compared to static UL/DL resource partition and duplexing flexibility without cross-link interference mitigation schemes
    Evaluations show that duplexing flexibility without cross-link interference mitigation schemes on a 4GHz and 30GHz provides better UPT compared to static UL/DL resource partition at least for some cases
    The evaluated cross-link interference mitigation schemes include sensing based methods, advanced receivers (e.g. MMSE-IRC, EMMSE-IRC), coordinated scheduling/beamforming, power control, link adaptation, hybrid dynamic/static UL/DL resource assignment.
  Observations for urban macro scenario:
    Evaluations show that duplexing flexibility with cross-link interference mitigation schemes on a 4GHz unpaired spectrum and on a 2GHz paired spectrum provides better average UPT compared to static UL/DL resource partition and duplexing flexibility without cross-link interference mitigation schemes.
    The evaluated cross-link interference mitigation schemes include advanced receivers (e.g. MMSEIRC, EMMSE-IRC, packet exchange for interference cancellation), coordinated scheduling/beamforming, power control, link adaptation.
    Evaluations show that duplexing flexibility on a 2GHz paired spectrum with SRS on the DL part without dynamic DL/UL resource allocation provides better cell average/edge throughput compared to no SRS on the DL part of the spectrum.
Dynamic duplexing schemes provides system level gain with/without CLI handling for specific deployment scenarios

## Slide 5
Full Duplex in unpaired spectrum for NR
(1) Full Duplex at gNB, and Half Duplex at UE
  Full Duplex with FDM manner at gNB, or Full Duplex with shared resources (i.e., subcarriers, RBs,…) at gNB
    Occurrence of Self-Interference at gNB
  Separated DL/UL operation in time at UE
    Occurrence of Intra-cell Cross-Link Interference between UEs
(2) Full Duplex at gNB, and Full Duplex at UE
  Full Duplex with FDM manner at gNB and UE, or Full Duplex with shared resources (i.e., subcarriers, RBs,…) at gNB and UE
  Simultaneous DL/UL operation at UE
    Occurrence of Self-Interference at both gNB and UE
    Occurrence of Intra-cell Cross-Link Interference between UEs
Potential gains
  DL or UL resource availability at any time
  Multiplexing becomes easy for different usage scenarios
   Latency reduction and spectral efficiency enhancement are achieved.
UE #2
FD
<Example of Full Duplex operation in a carrier>
gNB
Self-interference
UE-to-UE cross-link Interference
DL
Full Duplex (DL+UL)
UL
FD
FD
Sub-band#1
Sub-band#2
UE #1
FD
HD
HD

## Slide 6
Potential Objectives
Feasibility study of Full Duplex operation in gNB – UE [RAN1, RAN4]
  Define/prioritize scenarios for Full Duplex operation in terms of some aspects such as:
    Deployment scenario (e.g., Rural, Urban, Indoor, Isolated)
    Antenna configuration (e.g., Single-/multi-panel, Co-located/distributed antenna),
    Frequency resource utilization (e.g., separated frequency resource in a carrier is used for DL and UL, same frequency resource in a carrier is used for simultaneous operation of both DL and UL), etc.
    Frequency range (e.g., FR1, FR2)
  Note1: In a resource allocation perspective, Full Duplex operation includes simultaneous TX-RX in a same carrier
  Note2: The study may focus on unpaired spectrum, but necessity of enhancements for other scenarios(e.g. paired spectrum, sidelink) may be considered further
Study standardization impacts for the selected scenarios for Full Duplex operation [RAN1]
  Resource allocation (e.g., BWP)
  Interference handling (i.e., self-interference, UE-UE interference, gNB-gNB interference)
  MIMO operation (e.g., Beam management, Reference signal, CSI measurement, Multi-TRP/Cell)
  Duplex adaptation

## Slide 7
Annex: Effect of Intra-cell UE2UE Cross Link Interference
Measurement Environment
  Deployment
  Indoor (Parking lot)
  One gNB (Wideband Full Duplex operation for simult. DL &UL)
  BW: 100MHz, Center Frequency: 3.5GHz
  1Tx-1Rx, Tx power (5dBm)
  One aggressor UE (UL) :
  2Tx, Tx power (5, -5, -15, -25dBm, & No Tx)
  6 candidate locations
  One victim UE (DL):
  2Rx
  4 candidate locations
Observation
  Measured SINR (dB) of victim UE is varying depending on Tx power of aggressor UE, and distance between aggressor UE and victim UE.
  In many cases (e.g., lower Tx power for aggressor UE, or longer distance between victim UE and aggressor UE), intra-cell UE2UE CLI is negligible.
  It seems that the intra-cell UE2UE CLI is manageable by cross-Link Interference (CLI) mitigation schemes and network scheduling.
<Deployment for CLI measurement of Victim UE>
Candidate Locations of Aggressor UE for transmission
A1 (3m,10m) A7(20m,10m)
A3 (3m,30m) A9(20m,30m)
A6 (3m,60m) A12(20m,60m)
Candidate Locations of Victim UE for reception
V1 (0m,10m)
V2 (0m,20m)
V4 (0m,40m)
V6 (0m,60m)

## Slide 8
Annex: Effect of Intra-cell UE2UE Cross Link Interference
UE2UE CLI Measurement Result
  Victim UE1
  Victim UE4
  Victim UE2
  Victim UE6
Source of severe UE2UE CLI to victim UE