## Slide 1: Motivation for UE EMC enhancement
--Xiaomi
3GPP TSG-RAN Meeting #90e RP-202548
Electronic Meeting, Dec 7 -11, 2020

## Slide 2: Background
Reason for the WID:
From daily certification experience, it is found that different test lab has different understanding for UE configuration especially for CA and DC cases. Besides single carrier test, additional tests are requested for UE supporting different CA and DC combinations. Some comparison has been made for EMC and RF requirements within 3GPP specs.
Only General requirement
EMC
General Requirement
Additional Requirement
RF
What we can get from the WID:
  Define standardized test configuration to influence the regulatory requirement and test labs.
  Specification to be more complete.
  Test cases with more coverage.
CCSA TC9 WG1
YD/T 2583.18
ETSI ERM WGEMC
301 489 -52
Potential affected other STOs:

## Slide 3: Latest status
WF agreement on the UE EMC enhancement work during RAN4#96-e in 2020,8.
Fully discussed on the RAN draft reflector during the email discussion period in 2020,9.
During the RAN#89-e, it is proposed to have a combined umbrella WID for both BS EMC and UE EMC enhancement within RAN4 on the RAN Draft Reflector. (2020,9).
The umbrella WID was fully discussed during the email discussion period in 2020,10.
A revised WID for was provided after the email discussion and submitted to RAN4#97-e (2020,11).
Propose to be agreed in RAN#90-e (2020,12) with 4 months online and offline discussion.
RAN4#96-e
RAN #89-e
RAN4 #97-e
RAN #90-e
RAN Draft
Discussed in 1024QAM and EMC thread
RAN Draft
Discussed in EMC thread
2020.8
2020.9
2020.10
2020.11
2020.12

## Slide 4: Objectives (Core part)
Phase 1 (till RAN#92e):
Study on the need and motivation for additional UE features as per priority outlined below (highest to lowest):
  NR UE: CA, DC
  NR UE: SUL, UL MIMO and V2X
  EUTRA UE: CA, DC(Based on the NR study outcome), other features as captured in TS 36.101 v16.5.0 subclause 4.3A
  NOTE: Limit the scope within FR1 as currently the UE EMC specification only covers FR1 UE..
Investigate current 3GPP UE EMC radiated emission limit as whether current test frequency range is suitable, including the lower and upper test frequency range.
Investigate how to establish the communication link for NR and LTE UEs with different features:
  Possible deltaRIB to be considered.
  Possible MSD to be considered.
Phase 2 (based on phase 1 outcomes, till RAN#93e):
The objectives of this work item are to enhance the UE EMC with integrity of the requirements, as related to the ambiguity caused by lack of the requirements for different UE features. To complete the UE EMC requirements as per Phase 1 outcome, following are as the scope:
Introduction of Potential modification of current EMC requirements for UE features as in bullet 1:
  All emission requirements and immunity requirements
  Define receiver exclusion band for UE supporting features as in bullet 1
Define communication link establishment (refer to sub clause 4.2 of TS 36.124 and TS 38.124) for NR and LTE UEs for features as in bullet 1.
Frequency range modification for the radiated emission limit, including the lower and upper test frequency range.

## Slide 5: Objectives (Perf part)
Phase 1 (till RAN#92e):
  Analyse regulatory requirements to better understand the UE features performance under certain EMC tests and corresponding test configurations to ensure the tests are carried out correctly for general and additional requirements.
Phases 2 (based on phase 1 outcomes till RAN#94e):
  Define proper test configurations for NR and LTE UEs. (Sub clause 8.1 and 9.1 of TS 36.124 and TS 38.124)
    Investigate whether current test configuration defined in RAN5 specification TS 38.521-1/-2/-3 can be re-used in EMC tests. (Cross group co-operation within RAN4 and RAN5 might be needed when defining the test configuration)
    Investigate whether regulations have already defined test configurations and if these regulations can be reused.

## Slide 6: TU allocation
leading WG | RAT | WI code | WI or SI | Title | latest WID/SID | rapporteur | target |  | comment | 90 Dec.20 | 104 | 113 | 111 | 98 | 98 | 91 March 21 | 104bis | 113bis | 111bis | 98bis | 98bis | 105 | 114 | 112 | 99 | 99 | 92 June 21 | 106 | 115 | 113 | 100 | 100 | 93 Sep.21 REL-17 freeze | 106bis | 115bis | 113bis | 100bis | 100bis | 107 | 116 | 114 | 101 | 101 | 94 Dec.21 REL-17 ASN.1 freeze
R4 | LTE, NR |  | WI | Core part: UE EMC enhancement Rel-17 |  | Xiaomi | Dec 21 |  |  |  |  |  |  | 0.25 |  |  |  |  |  | 0.125 |  |  |  |  | 0.125 |  |  |  |  |  | 0.125 |  |  |  |  |  |  |  |  |  |  |  |  | 
R4 | LTE, NR |  | WI | Perf part: UE EMC enhancement Rel-17 |  | Xiaomi | Dec 21 |  |  |  |  |  |  |  |  |  |  |  |  | 0.125 |  |  |  |  | 0.125 |  |  |  |  |  | 0.125 |  |  |  |  |  | 0.25 |  |  |  |  | 0.25 |  | 
Target to finish at Dec, 2021.
  Average as 0.25 TU per meeting
  With limited and prioritized scope as stated in previous slide