## Slide 1
3GPP TSG RAN Meeting #90-e RP-202550
Electronic Meeting, December 7 - 11, 2020
Agenda Item: 9.7.5
Source: Xiaomi
Title: Views on Reduced Capability NR devices
Document for: Discussion for decision

## Slide 2: Outline
Remaining issues in the SI
WI Scope
Relationship with other projects

## Slide 3: Remaining issues
During the discussion in SI, the following issues are pended in the RAN plenary meeting （ or WI phase ）
  Minimum number of Rx branches supported by specification for FR1 TDD
  The maximum number of DL MIMO layers for Redcap with 2 Rx branches in FR1 and FR2
  Whether to have support FD-FDD or HD-FDD type A or both by specification for an FR1 FDD RedCap UE
  Whether to support relaxed UE processing time in terms of N1/N2 by specification for a RedCap UE

## Slide 4: Remaining issues
  Remaining issue #1: Minimum number of Rx branches supported by specification for FR1 TDD
  Xiaomi’s view:
    Analysis:
      1 Rx is critical for devices size in wearable use-case
      Only the coverage of broadcast PDCCH, Msg.4 in limited case (4GHz with 24dBm/MHz) is impacted due to the Rx reduction
      Obvious cost saving and power saving gain
    1 Rx should be supported in FR1 TDD
Agreements: For FR1 TDD bands where a non-RedCap UE is required to be equipped with a minimum of 4 Rx branches, the minimum number of Rx branches supported by specification for a RedCap UE is N. To be down-selected during the WI phase or at RAN plenary: Alt 1: N=2 Alt 2: N=1, where N=2 is also supported

## Slide 5: Remaining issues
  Remaining issue #2:The maximum number of DL MIMO layers for Redcap with 2 Rx branches in FR1 and FR2
  Xiaomi’s view:
    Analysis:
      For use cases requiring low data rate or further low cost, 1 Rx with 1 MIMO layer is already supported to target these low-end use cases.
      2 Rx with 2 MIMO layer could be supported to target the high-end use case
       The motivation to support 2Rx with 1MIMO layer is weak. 2 Rx with 1 MIMO layer should not be supported
Agreements: For FR1 FDD bands where a non-RedCap UE is required to be equipped with a minimum of 2 Rx branches, For a RedCap UE with 1 Rx branch, the maximum number of DL MIMO layers is 1. For a RedCap UE with 2 Rx branches, the maximum number of DL MIMO layers is M. Down-select between the following during the WI phase or at RAN plenary Option 1: M=1, where M=2 is also supported Option 2: M=2

## Slide 6: Remaining issues
  Remaining issue #3: Whether to have support FD-FDD or HD-FDD type A or both by specification for an FR1 FDD RedCap UE
  Xiaomi’s view:
    Analysis
      HD-FDD type A is beneficial for cost reduction with relatively low specification impact
      HD-FDD type A can satisfy the identified Redcap service requirements
      FD-FDD can also be supported without any specification impact and potential NW impact
     Both HD-FDD type A and FD-FDD are supported for FR1 FDD RedCap UE
Agreements: Recommend that HD-FDD type B is not supported for RedCap FR1 FDD UEs in Rel-17. Decide at RAN plenary whether to have support FD-FDD or HD-FDD type A or both by specification for an FR1 FDD RedCap UE

## Slide 7: Remaining issues
  Remaining issue #4:Whether to support relaxed UE processing time in terms of N1/N2 by specification for a RedCap UE
  Xiaomi’s view:
    Analysis:
    The cost saving gain is not significant while it results in potential negative impact on the latency and coexistence
       Relaxed processing time in term of N1, N2 is not supported
Agreements: Decide at RAN plenary whether to support relaxed UE processing time in terms of N1/N2 by specification for a RedCap UE.

## Slide 8: WI scope
UE complexity study
  UE bandwidth reduction
    Support 20MHz/100MHz during initial access for FR1/FR2, respectively
    In FR1, support of larger UE bandwidth after initial access can be further discussed in the WI
  Rx and MIMO layer reduction
    Support 1Rx with 1MIMO layer and 2 Rx with 2 MIMO layer in FR1 and FR2
      1 Rx with 1MIMO layer is mandatory, 2 Rx and 2 MIMO layer is optional
Coverage recovery
  UL channels: PUSCH, Msg.3
    Recommended in CE project as well. Target common solution in both projects
  DL channels: Msg.2, Msg.4 and broadcast PDCCHs

## Slide 9: WI scope
Power saving
  Support reduction of blind decoding
  RRM relaxation
  e-DRX
Framework :
  UE type definition
  Capability reporting
  Msg.1-based early indication
  Access control

## Slide 10: Relationship with other WIs
Relationship with coverage enhancement project
  Coverage enhancement focus on the coverage enhancement or the UL channels
  Coverage recovery in Redcap could firstly focus on the DL channels and reuse the solutions to UL channels specified in the CE WI
Relationship with power saving project
  Redcap project should firstly focus on the Redcap-specific power saving solutions
  Power saving schemes common for normal NR UE and Redcap UEs should be worked in the power saving WI