## Slide 1: NTNViews on WI scope for inter-UE coordination in Rel-17
3GPP TSG RAN Meeting #91-e RP-210251
Electronic Meeting, March 22 - 26, 2021

## Slide 2: Views on WI scope for inter-UE coordination
Following objectives on inter-UE coordination are captured in the WID for NR Sidelink enhancement*
*RP-202846, WID revision: NR sidelink enhancement
Study the feasibility and benefit of solution(s) on the enhancement(s) in mode 2 for enhanced reliability and reduced latency in consideration of both PRR and PIR defined in TR37.885 (by RAN#91), and specify the identified solution(s) if deemed feasible and beneficial [RAN1, RAN2]
  Inter-UE coordination with the following.
    A set of resources is determined at UE-A. This set is sent to UE-B in mode 2, and UE-B takes this into account in the resource selection for its own transmission.
  Note: The solution should be able to operate in-coverage, partial coverage, and out-of-coverage and to address consecutive packet loss in all coverage scenarios.
  Note: RAN2 work will start after RAN#89.

## Slide 3: Views on WI scope for inter-UE coordination
Inter-UE coordination has been studied for 3 meeting in RAN1 (RAN1#102-e~RAN1#104-e).
One conclusion was made in RAN1#103 where schemes for inter-UE coordination were categorized into 3 types:
  Type A: UE-A sends to UE-B the set of resources preferred for UE-B’s transmission
    e.g., based on its sensing result
  Type B: UE-A sends to UE-B the set of resources not preferred for UE-B’s transmission
    e.g., based on its sensing result and/or expected/potential resource conflict
  Type C: UE-A sends to UE-B the set of resources where the resource conflict is detected
RAN1 concludes that inter-UE coordination for Mode 2 is feasible and beneficial (e.g., for improving the reliability, etc.) compared to the baseline Rel-16 Mode 2 RA scheme, and thus, recommends to specify the feature in Rel-17.
  A conclusion was drawn along with detailed observations of evaluation results submitted from companies on the performance for the above 3 categories of inter-UE coordination types in RP-210032.

## Slide 4: Views on WI scope for inter-UE coordination
The observations in R1-2102166 (attachment in RP-210032) are further summarized in the table below:
Scheme | Traffic | w/ signaling overhead and latency | w/o signaling overhead and/or latency
Type A | Periodic | Beneficial for Unicast: 3 sources Beneficial for broadcast: 1 source Not beneficial for Unicast:1 source Not beneficial for groupcast: 1 source | Beneficial for Unicast: 3 sources Beneficial for groupcast with HARQ feedback Option 1: 1 source Beneficial for broadcast: 1 source
 | Aperiodic | Beneficial for Unicast: 3 sources Not beneficial for Unicast:1 source | Beneficial for Unicast: 3 sources Not beneficial for Unicast: 2 sources
Type B | Periodic | Beneficial for Unicast: 1 source | Beneficial for Unicast: 5 sources Beneficial for groupcast: 1 source
 | Aperiodic | Beneficial for groupcast: 1 source | Beneficial for Unicast: 1 source Beneficial for groupcast with HARQ feedback Option 1: 1 source Not beneficial for Unicast: 1 source
Type C | Periodic | Beneficial for groupcast with HARQ feedback Option 1: 2 sources | 
 | Aperiodic | Beneficial for groupcast with HARQ feedback Option 1: 4 sources | 

## Slide 5: Views on WI scope for inter-UE coordination
From the table in the previous slide, we can see the following:
  Performance of Type A scheme is controversial, particularly in the evaluations with signaling overhead and latency.
  Quite a few companies claim that Type B scheme is beneficial for periodic/aperiodic unicast/groupcast. However there is 1 company claim that it is not beneficial for aperiodic unicast.
  2 companies claim that Type C scheme is beneficial for periodic groupcast with SL HARQ-ACK feedback Option 1, 4 companies claim that Type C scheme is beneficial for aperiodic groupcast with SL HARQ-ACK feedback Option 1.
Proposal 1: In view of the above, we suggest that Type A scheme is NOT included in the WI scope.

## Slide 6: Views on WI scope for inter-UE coordination
For the remaining 2 Types, our view is to support Type B scheme only:
  Type B scheme is justified to be beneficial for both unicast and groupcast, while Type C scheme is only beneficial for groupcast with HARQ feedback Option 1.
  In Type B scheme, resource conflict expected to happen in the future can be indicated by UE-A, which means resource conflict could be avoided before it happens, therefore there is no need to support Type C scheme anymore if Type B scheme is supported.
  Type C scheme requires UE-A to decode more than 1 PSCCH within 1 PSCCH resource, which would complicate UE implementation.

## Slide 7: Views on WI scope for inter-UE coordination
Proposal 2:
  For Rel-17 inter-UE coordination, only following scheme is supported:
    Type B: UE-A sends to UE-B the set of resources not preferred for UE-B’s transmission
      e.g., based on its sensing result and/or expected/potential resource conflict