## Slide 1: Motivation of introduction of smartphone in NTN
3GPP TSG RAN Meeting #91-e RP-210257
Electronic Meeting, March 22 - 26, 2021

## Slide 2: Comparison between NTN and TN
TN
Smart phone
NTN
Handheld UE
Key parameters | Difference
Band | S-band, Ka-band
Propagation delay | Few 100ms
Speed | Few 1000Km/h(LEO)
Typical MS service | VoNR, short message, data service low data rate
Typical MSS service | As backhaul between stations on group
Cell size | Few 1000kms
Mobility | Earth fixed or moving cell Earth fixed TA
Typical service | Voice, short message, data service with low rate. (Note eMBB is not considered for smart phone to save power)
?
Smart phone should support features introduced in NTN WID

## Slide 3: UE characteristics
The difference between handheld UE and smart phone
  TX/RX antenna : it is assumed up to -5dbi antenna gain i.e. up to 5 dB less compared to handheld terminal in real deployment
  Battery capacity: much less than handheld terminal
[1] 38.821 Solutions for NR to support non-terrestrial networks (NTN)
Notes: Jingqiang: smart phone is -5dbi TX/RX antenna gain;
Linhao: Satellite could use circular(left-hand or right-hand) or linear polarization while smart phone is normally configured with linear polarization. And smart phone need change from passive to be active. Or there is 3 db loss for both RX and TX. It impacts the cost and increase antenna size.
Zhisong: smart phone could consume more than normal handheld device assuming transmit/receive same size of packets

## Slide 4: Coverage gap(PUSCH)
Assuming 0dBi TX antenna gain, up to 7.85 dB coverage gap in PUSCH is observed
For smart phone, with realistic -5dBi TX antenna gain, even larger coverage gap is resulted
  It means NTN in Rel17 doesn’t support VoIP service at all
Note1: the problem is more serious for GEO case
Note2: for downlink, the coverage problem is less severe

## Slide 5: Simulation assumption and required CNR of PUSCH
Parameters | Values
Scenario | NTN
Frequency | 2GHz
VoIP | 5.9kbps: 192 bits (70bits overhead) , 20slot repetition / 13.2kbps: 352 bits (70bits overhead), 20slot repetition
Target data rates | 5.9kbps-13.2kbps
Frame structure | FDD
Waveform | DFT-s-OFDM
Subcarrier spacing | 15kHz
BLER | 2%
Pathloss model | NLoS
Channel model | NTN TDL-C NTN TDL-D
Delay Spread | 20ns
UE velocity | 3km/h
PRBs | 2/4
# BS Rx chains | 1
# UE Tx chains | 1
DMRS configuration | Type I, 2 DMRS symbol, no multiplexing with data.
Frequency hopping | w/o
NTN-TDL_C
5.9 kbps
13.2kbps
NTN-TDL_D

## Slide 6: Coverage gap(PUCCH)
Assuming 0dBi TX antenna gain, up to 12.04 dB coverage gap in UL control is observed
For smart phone, with realistic -5dBi TX antenna gain, even larger coverage gap is resulted
  Considering the PUCCH repetition can provide 8 dB gains, the coverage should be further enhanced.
    Further repetition schemes, channel enhancements
Note1: the problem is more serious for GEO case
Note2: for downlink, the coverage problem is less severe

## Slide 7: Simulation assumption and required CNR of PUCCH
Parameters | Values
Scenario | NTN
Frequency | 2GHz
Frame structure | FDD
Format type | Format 1, 2bits UCI.
Waveform | DFT-s-OFDM
Subcarrier spacing | 15kHz, 30kHz
BLER | DTX to ACK probability: 1%. NACK to ACK probability: 0.1%. ACK missed detection probability: 1%.
Occupied channel bandwidth | 30MHz
Pathloss model | NLoS
Channel model | NTN TDL-C NTN TDL-D
PRBs | 1
# BS Rx chains | 1
# UE Tx chains | 1
Frequency hopping | w/
Link budget template: 38.821 v15.0.0
NTN-TDL_C
NTN-TDL_D
30kHz
15kHz
Notes: Zhangzhi: satellite need power saving also
Lihaitao: how about HARQ ACK/NACK? HARQ feedback could be disabled. We need solid calculation to show what is the gain.
Zhisong: maybe CDRX is not a proper solution considering long propagation delay. GEO seems not a proper use case for smart phone. Maybe LEO should be focus. And every 7 seconds UE need change serving satellite
Zhangzhi: UE doesn’t need track satellite every few seconds to save power
Zhongda: as long as the whole system works, saving battery is more important for smart phone
Zhongda: one solution is that UE can be configured on service inactivity timer. Once timer expires, UE can switch to deep sleeping to save power
Lihaitao: no specific power saving solution is discussed in RAN2 and RAN1
Zhisong: maybe PUCCH coverage is more important. And also PRACH could be more interesting. Some evaluation is needed
Zhangzhi: for Very high power UE (29dbm) which is not more efficient transmitting power. 29dbm=26dbm+26dbm. And the antenna could be 2TX/2RX which is popular configuration for high-end terminal.
Zhangyuan: additional antenna is also possible within an extra shell (which could be used for charging)
Zhongda: the 26dbm maximum transmission power is more reasonable
Linhao: RRM will start soon in RAN4 focusing on measurement
Shicong: power saving could potential impact MAC
Linhao: for handheld, there is no limitation between GEO and LEO

## Slide 8: Delay budget of VoNR
The worst one way propagation delay(d) in NTN with transparent payload :
  541.46/2 ms for GEO
  41.77/2 ms for LEO at 1200km
  25.77/2 ms for LEO at 600km
The worst one way delay budget:
  (1+BLER)*(d+n*Repeating slots)+BLER*d
  RLC UM mode , configured grant and one HARQ retransmission is assumed
VoNR is not supported for GEO unless new PDB is introduced
VoNR could be supported for LEO if linkage budget can be met within PDB
…
…
TX
RX
PDCCH or NACK
PDB of VoNR is 100ms and BLER is 2% with one retransmission

## Slide 9: Potential spec impact for smart phone@NTN
It is assumed that smart phone has 5 dB less antenna gain compared to handheld UE in NTN WID. For power saving it is assumed that degradation of service to some extent is acceptable i.e. functionality is core requirement.
1, Coverage enhancement
  To evaluate the potential coverage gap on FR1 for at least LEO
  To figure out solution to fill the gap
2, Power saving for UE
  eDRX cycle for IDLE/INACTIVE state
  Power saving solution for VoNR
  Relaxed RRM and/or RLM
3, Power saving for gNB e.g. satellite
4, If new features need be introduced for smart phone
  It is necessary for NTN network to differentiate between smart phone and other handheld device
  Access control for smart phone
5, Relevant RF and RRM work w.r.t. antenna gain
Notes: Zhangzhi: satellite need power saving also
Lihaitao: how about HARQ ACK/NACK? HARQ feedback could be disabled. We need solid calculation to show what is the gain.
Zhisong: maybe CDRX is not a proper solution considering long propagation delay. GEO seems not a proper use case for smart phone. Maybe LEO should be focus. And every 7 seconds UE need change serving satellite
Zhangzhi: UE doesn’t need track satellite every few seconds to save power
Zhongda: as long as the whole system works, saving battery is more important for smart phone
Zhongda: one solution is that UE can be configured on service inactivity timer. Once timer expires, UE can switch to deep sleeping to save power
Lihaitao: no specific power saving solution is discussed in RAN2 and RAN1
Zhisong: maybe PUCCH coverage is more important. And also PRACH could be more interesting. Some evaluation is needed
Zhangzhi: for Very high power UE (29dbm) which is not more efficient transmitting power. 29dbm=26dbm+26dbm. And the antenna could be 2TX/2RX which is popular configuration for high-end terminal.
Zhangyuan: additional antenna is also possible within an extra shell (which could be used for charging)
Zhongda: the 26dbm maximum transmission power is more reasonable
Linhao: RRM will start soon in RAN4 focusing on measurement
Shicong: power saving could potential impact MAC
Linhao: for handheld, there is no limitation between GEO and LEO