## Slide 1: Motivation for REL-17 WID on L2 Relay Architecture
Xiaomi
RP-210431

## Slide 2: Motivation for Relay Support
Objectives
Sidelink and Network Coverage enhancement
  including out of coverage, indoor and enterprise environments
UE power efficiency improvements
  Remote UE Tx power reduction, reduced cell search, improved local device interaction
Justifications
More local device interactions
  Optimal service continuity during mobility, high reliability and minimal latency impacts
Provide Remote UE coverage enhancement,
  Home IoT, local device clusters, end user QoE with optimal power budget during relay deployment
  Relay UEs require minimal additional investment from MNO
    Relay UE may be owned by end users or commercial enterprises, authorized by networks
Relay seen as enabler or major component for real world feature deployments

## Slide 3: Relay Architecture for REL-17
L2 Relay preferred
End user identifiable by peer
  individual bearers addressable and adoption of 3GPP Security throughout
Both UE-to-network and UE-to-UE relaying configurations are in scope
Verified as viable solution to both configurations in conclusion of study item
Access Stratum control and integration with higher layers to maximise RAN deployment,
  minimising latency, reliable security (integrity and encryption) and optimum service continuity and all directly related to each hop of deployed relay configuration

## Slide 4: Additional Observations
Wide range of use cases and verticals expected to adopt Sidelink Relays to enhance coverage and improve Remote UE power efficiencies, e.g. V2X, PS, IIoT, NCIS, eCAV, ATRAC, REFEC
Single Relay architecture solution
  Avoids market fragmentation
  Supports a clear path/ choice for market adoption
    reduces implementation of redundant optionality
  Minimises time to adoption

## Slide 5: Proposal for RAN#91e
Approve Sidelink Relay work item for single Relay architecture for REL-17
Adopt L2 Relay Architecture as NR Sidelink Relay architecture for U2N and U2U Relay Configurations
Support proposal in WID RP-210649