## Slide 1: Remaining issues for Redcap
Xiaomi
3GPP TSG RAN Meeting #91-e
Electronic Meeting, March 16 - 26, 2021
Agenda: 9.7.27
RP-210473

## Slide 2: Background
Remaining issues
  Support of 1Rx in TDD: For frequency bands where a legacy NR UE (other than 2-Rx vehicular UE) is required to be equipped with a minimum of 4 Rx antenna ports, the minimum number of Rx branches supported by specification for a RedCap UE will be decided at RAN#91e; hence no specific work for these frequency bands will be done before RAN#91e.
  Support of 40MHz in FR1: The possibility of, and any associated conditions for, optional support of a wider bandwidth up to 40MHz after initial access for this case will be further discussed at RAN#91e.
  Higher layer enhancement: Specify higher layer enhancements [RAN2, RAN1]. Details are to be refined at RAN#91e taking the outcome of the RedCap SI into account, and work on this objective shall start after RAN#91e
we will share xiaomi’s view on these remaining issues

## Slide 3: Reduced minimum number of Rx branches
Reduced minimum number of Rx branches
  Analysis：
    1 Rx is critical for devices size in wearable use-case
    Obvious cost saving gain
    Only the coverage of broadcast PDCCH, Msg.4, Msg.2 in limited case (4GHz with 24dBm/MHz) is impacted due to the Rx reduction
    In the real implementation, the performance gain of 2Rx on wearable over 1Rx in wearable device is marginal due to more antenna efficiency loss and high antenna correlation
  Proposal:
    1 Rx shall be supported in FR1 TDD
    Restricting the access of Redcap with 1 Rx is allowable

## Slide 4: Coverage recovery
Coverage recovery
  Analysis:
    There is certain DL coverage loss in Msg.4，Msg.2 and broadcast PDCCH due to Rx reduction
    Antenna efficiency loss would also result in the coverage loss in both DL channels and UL channels
      Up to 3dB antenna efficiency loss is assumed during the SI phase
  Proposal:
    Coverage recovery shall be supported for both UL channels (PUSCH, Msg.3) and DL channels (Msg.4, Msg.2 and broadcast PDCCH)
      FFS: Redcap-specific or UE common coverage enhancement solution

## Slide 5: Support of up to 40MHz in FR1
Possibility of supporting up to 40MHz as an optional UE capability after initial access in FR1
  Analysis：
    Supporting 40MHz enables the wearable devices with 1Rx to achieve the peak data rate of up to 150Mbps
    UEs with 40MHz and 1Rx achieve better cost saving gain than UEs with 20MHz and 2Rx
    UEs with 40MHz and 1Rx achieve similar power saving gain with UEs with 20MHz and 2Rx
  Proposal：
    Support UE bandwidth of 40MHz at least for wearable devices
      FFS： Whether it is only applicable to the Redcap with 1 Rx or not

## Slide 6: Power saving enhancement
Specify UE power saving and battery lifetime enhancement for reduced capability UEs
  Extended DRX for both RRC Inactive and Idle
  RRM relaxation for stationary devices

## Slide 7: Summary
Proposal 1:
    1 Rx shall be supported in FR1 TDD
    Restricting the access of Redcap with 1 Rx is allowable
  Proposal 2 :
    Coverage recovery shall be supported for both UL channels (PUSCH, Msg.3) and DL channels (Msg.4 and broadcast PDCCH)
      FFS: Redcap-specific or UE common coverage enhancement solution
Proposal 3：
    Support UE bandwidth of 40MHz at least for wearable devices
    FFS： Whether it is only applicable to the Redcap with 1 Rx or not
Proposal 4：
    Extended DRX for both RRC Inactive and Idle
    RRM relaxation for stationary devices

## Slide 8: Thank you