## Slide 1: Proposed RAN2 Work Scope for REDCAP WI

## Slide 2: Current Status
Latest WID (RP-202933)
  Specify higher layer support of enhancements listed above [RAN2, RAN1]. Details are to be refined at RAN#91e taking the outcome of the RedCap SI into account, and work on this objective shall start after RAN#91e:
    Specify definition of RedCap UE type(s) including set(s) of L1 capabilities for RedCap UE identification and for constraining the use of those RedCap L1 capabilities only for RedCap UEs, and preventing RedCap UEs from using capabilities not intended for RedCap UEs including at least carrier aggregation, dual connectivity and wider bandwidths.
    Specify functionality that will enable RedCap UEs to be explicitly identifiable to networks and allow operators to restrict their access if desired.
    Specify necessary updates of UE capabilities (38.306) and RRC parameters (38.331).

## Slide 3: Potential Issues from RAN2 Discussion
RAN2 discussed followings in the previous RAN2 meetings.
  Framework
    Number of UE types
    UE identification
    Access control
  Power saving
    eDRX
    RRM Relaxation

## Slide 4: Number of UE Types
RAN2 discussion
  It was discussed how many number of UE types should be supported for REDCAP.
  Three options are on the table: one, two, many (>2)
One, two, vs. many
  Reducing number of UE type is desirable to prevent market fragmentation.
  Distinction of UE types during initial access may be beneficial for fine-tuned configuration.
  Support for multiple UE types requires lots of specification works.
Proposal
  Support one or two REDCAP UE type.

## Slide 5: UE Identification
RAN2 discussion
  It was discussed when to identify REDCAP UEs during RA procedure.
  For 2-step RACH, MsgA is used for identification.
  For 4-step RACH, Msg1- based and Msg3-based options were discussed.
Msg1 vs. Msg3 options for 4-step RACH
  It was difficult to conclude which option should be taken.
  Down-select between two options in WI phase.
Proposal
  For 2-step RACH, specify UE identification solution based on MsgA.
  For 4-step RACH, specify UE identification solution based on Msg1 or Msg3, and down-select between them.

## Slide 6: Access Control
RAN2 discussion
  It was discussed how to restrict access from REDCAP UEs.
  Two main options are on the table:
    Cell barring
    Unified Access Control
Cell barring vs. UAC
  Device-type specific UAC requires SA1/2 involvement. However, stable requirements in SA1/2 are missing for now.
  Cell barring may be sufficient in Rel-17, given that network can choose whether to apply cell barring or not.
Proposal
  Specify a mechanism for cell barring from REDCAP UE access.
  Device-type specific UAC is considered in later releases.

## Slide 7: eDRX
Observations
  The eDRX scheme is not specified in the latest WID.
  However, RAN2 spent a lot of meeting time to discuss power saving scheme based on eDRX.
  RAN2 see the benefit of supporting >10.24s in RRC_IDLE and RRC_INACTIVE.
Proposal
  Specify eDRX mechanism supporting > 10.24s in RRC_IDLE and RRC_INACTIVE.

## Slide 8: RRM Relaxation
Observations
  The RRM relaxation scheme is not specified in the latest WID.
  However, RAN2 spent a lot of meeting time to discuss power saving scheme based on RRM relaxation.
RRM relaxation
  RAN2 see potential benefit of RRM relaxation for both time-domain and frequency-domain.
  RAN2 recommended that serving cell RRM relaxation is not considered in Rel-17.
Proposal
  Specify time-domain and frequency-domain RRM relaxation method for neighbour cell.

## Slide 9: Summary of Proposed RAN2 Scope
  Support one or two REDCAP UE types.
  For 2-step RACH, specify UE identification solution based on MsgA.
  For 4-step RACH, specify UE identification solution based on Msg1 or Msg3, and down-select between them.
  Specify a mechanism for cell barring from REDCAP UE access.
  Device-type specific UAC is considered in later releases.
  Specify eDRX mechanism supporting > 10.24s in RRC_IDLE and RRC_INACTIVE.
  Specify time-domain and frequency-domain RRM relaxation method for neighbour cell.